## Slide 1: Compatibility Checking for Autonomous Lane-Changing Assistance Systems
Po-Yu Huang1, Kai-Wei Liu1, Zong-Lun Li1, Sanggu Park2, Edward Andert2, Chung-Wei Lin1, Aviral Shrivastava2
1National Taiwan University 2Arizona State University

## Slide 2: Incompatible Lane-Changing Models
An incompatible example of lane changing
  Two vehicles always accelerate or decelerate together
  They always keep the same longitude along a road segment
  They fail to exchange their lanes before the end of the road segment
Challenges
  Different automotive makers (and suppliers) develop different types of systems by their own
  A compatibility issue may be resolvable by human drivers, but it can cause a functional failure for autonomous vehicles

## Slide 3: Compatibility Checking
Contribution: a methodology to verify if lane-changing models are compatible so that the vehicles can exchange their lanes
Usage of verification results (if incompatible)
  Design time: trigger redesign of lane-changing models
  Runtime: prevent incompatible vehicles from entering a road segment with the incompatible conditions
Sensors or
Communication
Lane-Changing Model 1
Vehicle 1
Vehicles'
States
Sensors or
Communication
Lane-Changing Model 2
Vehicle 2
Vehicles'
States
Initial
States
Compatible? (Exchange Lanes?)