## Slide 1: Blame-Free Motion Planning in Hybrid Traffic
Sanggu Park
Notes: Good morning, and thanks for coming to attend my defense presentation.
Before the beginning, I really appreciate my advisor Professor Aviral, Professor Yezhou, and Professor Fisher for committee attendance.
Today, I present my defense for a master of science in Computer Engineering.
The subject is blame-free motion planning in hybrid traffic.
Throughout the presentation, I will propose the motion planning algorithm that makes autonomous vehicles to be blame-free against unavoidable accidents.

## Slide 2: The Goal is to make AVs Blame-Free
Autonomous Vehicles (AVs) cannot avoid all accidents.
  Collisions come from multiple sources
Court and insurance company decides the blame by using the ‘negligence rule’ [1]
  Causation : the driver must have caused the accident.
  Negligence: the driver must have acted less than ‘due care.’
To be ‘blame-free’ in case of accident,
the driver has to disprove both causation and negligence.
(dead)
I was merely following the lane, and the opponent cut in. So I didn’t cause the accident!
If you had tried full-braking, I would not have died at least. So you take the partial blame!
[1] Kahan, M. (1989). Causation and incentives to take care under the negligence rule. The Journal of Legal Studies, 18(2), 427-447.
Notes: First, I want to say that now is the time to make autonomous vehicles to be blame-free.
As shown in the figure, the probability of collision comes from the front and behind in the same lane that AV is driving, or from the adjacent lanes.
Even if AV is equipped with the safest motion planning algorithm, if multiple vehicles surrounding the AV cause an accident at the same time, then it is obvious that AV might not avoid the accident.
Currently, in the event of a traffic accident, the insurance company or court determines the ratio of blame between the involved vehicles. Similarly in hybrid traffic in the near future, the blame will also be judged, no matter whether the vehicle is an autonomous or not.
Meanwhile, as the ‘negligence rule’ defines, the blame decision is done by proving two conditions, which are causation and negligence.
  Causation means whether the driver caused the accident or not, and
  negligence means whether the driver has acted with less than due care.
In other words, the driver can be 'blame-free' by disproving both of the conditions. More specifically, in case of accident, it needs proof that the driver did not cause the accident and also did his best to fulfill the due care.

## Slide 3: Limitations of Existing Work
‘Collision-free’ motion planning in hybrid traffic is impossible.
  ‘Collision-free’ is only possible in AV-only traffic [2,3]
    Every vehicle communicates in the same protocol or using the same algorithm.
  Game-theory based methods are proposed for hybrid traffic [4,5]
    ‘probabilistic’ prediction of others’ driving is not always correct.
[2] Hilscher, M., Linker, S., Olderog, E. R., & Ravn, A. P. (2011, October). An abstract model for proving safety of multi-lane traffic manoeuvres. In International Conference on Formal Engineering Methods (pp. 404-419). Springer, Berlin, Heidelberg.
[3] Kessler, T., & Knoll, A. (2019, June). Cooperative multi-vehicle behavior coordination for autonomous driving. In 2019 IEEE Intelligent Vehicles Symposium (IV) (pp. 1953-1960). IEEE.
[4] Fox, C., Camara, F., Markkula, G., Romano, R., Madigan, R., & Merat, N. (2018). When should the chicken cross the road. Game theory for autonomous vehicle-human interactions.
[5] Yu, H., Tseng, H. E., & Langari, R. (2018). A human-like game theory-based controller for automatic lane changing. Transportation Research Part C: Emerging Technologies, 88, 140-158.
’s claimed space
’s prediction
might not brake!
’s claimed space
=
’s prediction
properly brakes!
Notes: From what I said earlier, now I point out the limitations of existing work about ‘blame’.
First, the proposed methods which guarantee ‘no collision’ are not collision-free in hybrid traffic, because they use ideal prerequisites which assume that the traffic is AV-only, or the communication is perfect. However, when it comes to the real world that human-driven vehicles drive together, the methods are not collision-free and not applicable.
Recently, the game-theory based methods are proposed to make AVs work with human-driven vehicles to overcome this. However, the methods still rely on probabilistic prediction so that AV’s prediction of other vehicles’ driving might be wrong.

## Slide 4: Limitations of Existing Work
RSS [6] suggests distance-based blame ☞ not applicable in real-world traffic
  The suggested lateral safe distance can be longer than the lane width.
  Right-of-way rule: ‘The closest vehicle from the merging point has the right-of-way.’
    The decision is inconsistent, as its distance changes continuously.
[6] Shalev-Shwartz, S., Shammah, S., & Shashua, A. (2017). On a formal model of safe and scalable self-driving cars. arXiv preprint arXiv:1708.06374.
We need a ‘negligence rule’-based blame-free motion planning algorithm!
Lane width
Lateral safe distance by RSS
Merging point
has a right-of-way at first.
At the next time, has a right-of-way.
Notes: Furthermore, whereas RSS suggests the distance-based blame, its suggestion is still not applicable in real-world for two reasons.
First, its lateral safe distance can be longer than the lane’s width, and this makes AVs to be farther from other car in the adjacent lane so that AV has to get out of the current lane.
Next, RSS also decides the right-of-way by the distance. According to the rule, the closest vehicle from the merging point has a right-of-way. And this makes the right-of-way decision inconsistent.
As expressed in the figure, for example, ‘c1’ was closer to the merging point than ‘c2’ so that it had the right-of-way. However, if c2 ran faster than c1 at the next time step and got closer from the point than c1, then c2 has the right-of-way at the moment.
For this reason, now there is no blame-free methods for autonomous driving.
Now, I want to insist that we need a blame-free motion planning algorithm that proves its zero-blame by the negligence rule.

## Slide 5: Thesis Contributions
An algorithm for Blame-Free motion planning in hybrid Traffic (BlaFT).
Proofs
  Safety proof: there is no collision in BlaFT-only traffic.
  Blame proof: BlaFT is blame-free against other drivers’ misbehavior.
Simulation Setup: SUMO-based hybrid traffic simulation
Experiments: BlaFT reduces the accidents, and can be more efficient.
  Safety: as AV ratio increases to 100%, the number of collisions decreases to ‘0’.
    There is no accident in BlaFT-only traffic.
  Efficiency: BlaFT decreased the traffic delay in aggressive .
Notes: In this presentation, I propose four contributions of the research.
First, I propose an algorithm that enables a blame-free motion planning in hybrid traffic, which is named as ‘BlaFT.’
Second, I propose two induction proofs that show the motion planning algorithm guarantees safety and blame-free states.
3. Third, I show the simulation setup of hybrid traffic which is built on SUMO simulator.
At the end, I show the experimental results of safety and efficiency.
  For the safety, by increasing the AV ratio to 100%, the number of accident decreased to 0
  For the efficiency, it showed that the delay time might be decreased as BlaFT manipulates its safe distance.

## Slide 6: Outline
Definitions
  Negligence Criteria
  Crash and Response envelopes
  Crash & Safe States
  Blame States
Motion Planning Algorithm
Proofs
Experimental results
Notes: Next, let me explain the definitions.

## Slide 7: Negligence Criteria: Response & Crash Distance
Response distance
  After the response time ‘’, a vehicle must apply the braking at least the amount of ‘’ against the potential collision within the sensing range ‘’.
Crash distance
  After the response time ‘’, a vehicle applies the max. braking ‘’ against the danger.
  ☞ If the collision area is within this distance, it is unavoidable. Thus, it is NOT negligent!
Notes: First I propose two distances as negligence criteria, which are response and crash distance.
The response distance is the longest braking distance that AV is negligent during the response time ‘rho’ so that it accelerates at maximum during the time, and starts to brake after the ‘rho’. Among the variables in the equation, the response deceleration rate, marked with red circle, is the one that autonomous vehicle applies as the minimum braking. And its distance is constrained by the sensing range. To satisfy the constraint, the responding deceleration rate should be manipulated by the AV.
Next, the crash distance is the one from which AV is not possible to avoid the accident even with the maximum braking. Not like the response distance, the crash distance uses the maximum braking rate, which is usually specified by the manufacturers, law, or manual. So if the collision area was initially within this distance, it is unavoidable for AV. In this case, AV is not negligent.

## Slide 8: Response and Crash Envelopes
Response Envelope () and Crash Envelope ()
Notes: Based on two distances, AV creates two kinds of envelopes to detect the collision, which are called response and crash envelope.
The envelope calculation is based on the lane-based coordinate system, as shown in an equation. ‘t’ is the vehicle’s trajectory function, and ‘Y’ is the longitudinal position following the trajectory. The function ‘w’ is the vehicle’s width and t-perpendicular is the norm vector of function ‘t’ at the position ‘Y.’
And The interval of ‘Y’ and ‘alpha’ allows us to define the area of the envelopes. The width is same as the vehicle’s width by alpha, and the length starts from the vehicle’s tail and ends at the response distance or crash distance from the head.

## Slide 9: Safe and Crash States
Crash: there is an overlap between multiple vehicle’s
Safe: there is no overlap between multiple vehicle’s (no crash)
Notes: By using two envelopes, now we define the safe and crash states.
First, the crash state is the moment multiple CEs overlap with each other. In this case, the distance they are maintaining is not enough to avoid the collision by braking.
Second, the safe state is the negation of the crash state. In fact, it means there is no overlap among CEs. In the safe state, vehicles are able to avoid accidents by braking with less than the maximum deceleration rate.

## Slide 10: Blame-Free State
Definition by ‘Negligence Rule’
  Causation comes from the right-of-way (ROW) in the structured road.
    If accident happened, then vehicle without ROW caused an accident.
  Negligence: did AV do its best to avoid the accident?
    Ego AV is not negligent if at every moment it satisfies the state
Collision area
Collision area
Notes: Now we discuss the ‘blame-free’ state.
Based on the negligence rule, AV is blame-free in two cases: either AV is not involved in an accident or involved an accident but disproved the causation and the negligence.
First, the causation comes from the right of way. And in the structured road, the right-of-way can be decided by the relative positions and by behavior.
In the right figure, for example, if ego is under the control of traffic sign and accident happened between other car ‘c’ and ego, then ego is the one who caused an accident.
Next, for negligence, we define this by using two envelopes.
Let’s assume the collision happened between two vehicles.
  In the left figure, if the collision area was initially detected within RE but not CE, then it was predictable by ego vehicle, since the collision area was avoidable by the braking with less than maximum deceleration rate. So ego is negligent if accident happened.
  However, if the collision area was initially detected within CE, in the right figure, ego vehicle cannot avoid the accident even with maximum braking. Thus, ego is not negligent in this case.

## Slide 11: Blame-Free State
Blame-free: if there was an accident, then AV had a right-of-way against the opponent.
Notes: As a result, the blame-free state can be re-arranged that it equivalents to the state that it is safe or crash but also possesses the right-of-way .
Now, the main idea is to not develop an algorithm that does not cause any accidents but to make sure that whenever there is an accident, then the AV had the right-of way.

## Slide 12: Outline
Definitions
  Negligence Parameters
  Crash and Response envelopes
  Crash & Safe States
  Blame States
Motion Planning Algorithm
  Behavior Decision
  Conservative Sensing
  Collision Detection
  Collision Avoidance and Mitigation
Proofs
Experimental results
Notes: Next, we will go through the motion planning algorithm.

## Slide 13: Motion Planning Algorithm (Overview)
Behavior Decision
  : AV decides if it is lane-changing or lane-following.
Conservative Sensing
  : AV senses other vehicle’s state considering the sensing error.
Collision Detection
  : AV predicts the collision area.
Collision Avoidance & Mitigation
  : AV produces the new trajectory and acceleration rate, or mitigates the damage.
,
Behavior
Decision
Conservative
Sensing
Collision
Detection
Collision Avoidance & Mitigation
Notes: The algorithm consists of four parts, which starts from behavior decision and ends at collision avoidance and mitigation at each time step.
First, AV decides its behavior, whether lane-following or lane-changing based on the trajectory and map graph.
Second, AV senses the other vehicle’s information and produces the error-conservative information to be safe from the sensing error.
Third, AV detects the collision by finding out the overlap between ego’s response envelope and other vehicle’s worst-case response envelope by the prediction.
At last, if a collision area exists, AV finds out a pair of safe trajectory and safe acceleration rate to avoid the collision area. In case there is no option for avoidance, it mitigates the damage by the maximum braking.

## Slide 14: Behavior Decision
Behavior is decided by the Behavior Line ()
Notes: First, to decide the behavior, AV uses the ‘behavior line’, or BL.
(As defined in an equation and the figure shows, the BL is a vertical line that is long as same as the ego vehicle’s width, and distant from the ego AV as much as blinking distance alongside the AV’s trajectory. )
(Blinking distance is the maximum velocity ‘v_max’ multiplied by the constant ‘t_blink’.)
(BL aenables AV to turn on the blinker at a specific fixed point before it changes its lane.)
The BL enables AV to decide its behavior, either lane-changing or lane-following, by discriminating the lane area.
Let me explain this with animation.
  (Lane following) (CLICK) First, if both ego AV and BL overlap with the lane ‘L0’, then it meets the lane-following condition. It is continued until the blinking line touches the next lane ‘L1’ and AV’s behavior is lane-following
  (Lane changing) As AV maneuvers and the BL starts to overlap with the lane L1, however, the ego vehicle does not overlap with L1. (CLICK) Now, its behavior becomes lane-changing. And it is continued until the moment ego vehicle enters L1. (CLICK)
  (lane following) Now that AV starts to enter L1, the ego vehicle overlaps with both L0 and L1. Since AV overlaps with the lane where the BL overlaps, now AV’s behavior becomes the lane-following. And it is continued as AV fully enters the lane.

## Slide 15: Conservative Sensing
AV calculates the worst-case information ().
  The prediction is based on Constant Turn Rate & Velocity (CTRV) model.
: real-world information
: predicted information at next time step
: worst-case information
Notes: At the next step, AV senses the other vehicle’s driving information.
Basically, the information contains other vehicles’ x-y coordinates, heading angle, and velocity, because these are the minimum required ones to estimate the future trajectory of the sensed ones.
And we apply the Constant Turn Rate and Velocity model for the trajectory estimation, which applies 0 acceleration and constant angular velocity for the next time step.
By using the CTRV model prediction, we calculate the worst-case information which makes the estimated position of other cars and ego vehicle to be the closest.

## Slide 16: Collision Detection
At first, AV estimates other vehicle’s Response Envelope ()
Ego predicts the other vehicle c’s worst-case RE
RE
Estimated RE ()
Notes: After calculating the worst-case information, AV starts the collision detection.
To this, AV first estimates other vehicle’s response envelope using the worst-case information.
The trajectory is extracted based on the CTRV model, and then the envelope area is determined by the car’s width, length, and position.
As shown in the figure, the estimated RE is closer from the ego’s position, compared to the other car’s RE.

## Slide 17: Collision Detection
Lane-following mode: AV detects the overlap between REs
Notes: If the envelope estimation is done, then it starts the detection. The detection process differs by the behavior, in fact, lane-following and lane changing.
First, in lane-following mode, AV finds out the overlap between its RE and other’s RE, and considers the overlapped area as collision area.
(CLICK!) Let me explain the example case with an figure. Initially, if there is no overlap between response envelopes which are expressed as green rectangles, then there is no collision area for ego AV.
(CLICK!) However, as ego vehicle maneuvers and another car in front slows down, the overlapped area might appear at the tip.
(CLICK!) Otherwise, if other cars in adjacent lanes cut into the ego vehicle’s front area, multiple overlaps might appear. In this case, the union of the areas becomes the collision area.

## Slide 18: Collision Detection
Lane-changing mode: AV also detects the collision area in the target lane
  AV creates ‘Lane-change Envelope’ () to detect the collision in the target lane.
Notes: If ego vehicle is in lane-changing mode, it also has to detect the collision area in the target lane.
To do this, AV creates an area called ‘lane-change envelope’,or 'LE', as the white polygon shown in the figure.
This is an envelope to detect the potential collision in the target lane and it does not let ego vehicle to enter the lane whenever the potential collision is detected.

## Slide 19: Collision Detection
Lane-changing mode: AV also detects the collision area in the target lane
  AV’s assumption #1: “Others will not notice my lane-changing until I get into their lane!”
    Lengthened by longer response time:
  AV’s assumption #2: “I will not enter the lane, whenever I cut into other’s RE!”
    Widened by lane width:
Notes: Also, AV expands the other vehicles’ response envelope areas where it overlaps with ego vehicle’s target lane.
The reason AV do this is to be safe from the other car’s worst-negligence during the lane-changing. And this assumes two things.
  First, AV assumes that others will not notice its lane-changing so that they might accelerate at maximum while it is entering the lane. (CLICK!) For this reason, AV makes the other’s envelope longer by adding its lane-entering time to other vehicle’s response time.
  Second, AV does not allow itself to invade the other vehicle's response envelope from the side, so as not to force them to decelerate more than the minimum deceleration. (CLICK!) However, if the width of other’s envelope which is estimated by ego is the same as the vehicle width, ego vehicle might concur other’s RE from the side.

## Slide 20: Collision Detection
Lane-changing mode: AV also detects the collision area in the target lane
  AV’s assumption #1: “Others will not notice my lane-changing until I get into their lane!”
    Lengthened by longer response time:
  AV’s assumption #2: “I will not enter the lane, whenever I cut into other’s RE!”
    Widened by lane width:
Notes: But if RE’s width is same as the lane width, then AV is able to prevent the other vehicle's RE overlap from the side. (CLICK)

## Slide 21: Collision Avoidance and Mitigation
First, BlaFT finds out multiple pairs of safe trajectory () and acceleration ()
  Safe trajectories make BlaFT disjoint with the collision area. (At most one lane change)
  Safe acceleration rates make BlaFT safe from other vehicles. ()
Notes: If the collision is detected, then AV tries the collision avoidance and mitigation.
First, if AV percieves the collision area,then it finds out all possible responses, which are pairs of safe tajectory and acceleration rate.

## Slide 22: Collision Avoidance and Mitigation
Then, BlaFT selects the most optimal response by ‘Threat Number (TN).’
  Response with the smallest TN is the optimum.
    Braking Threat Number (BTN) & Steering Threat Number (STN)
: lateral acceleration alongside the trajectory
:
:
Notes: If BlaFT finds out multiple safe responses, then it selects the most optimal one by the quantified criteria. And it is called ‘Threat Number’, or TN.
As shown in the equation, the optimal response is the one that minimizes the TN. And TN is a function that takes ‘Braking Threat Number’, or BTN, and ‘Steering Threat Number’, or STN, as variables.
First, BTN is the index that indicates how much braking is needed to avoid collision. For example, if it is bigger than 1 then collision is unavoidable by maximum braking.
Second, STN is the index that indicates the danger of flipping caused by lateral acceleration.
In addition, it is free to decide the function ’f’, according to the driver’s preference for braking and steering level.

## Slide 23: Example: TN calculation
☞ Ego selects .
Notes: Here is the example of TN calculation.
Let’s assume that ego AV found out two safe responses.
The response ‘0’ in green letters requires AV to decelerate less, and the lateral acceleration caused by the curvature of trajectory is less than the response ‘1’.
In contrast, as the red letters shows, the response ‘1’ requires AV to decelerate more, and the lateral acceleration is more than the other one because of the higher curvature.
Because the function ‘f’ is the sum of BTN and STN, the TN calculation for each response follows the equation.
As a consequence, ego selects the response 0 which makes the TN smaller.

## Slide 24: Outline
Definitions
Motion Planning Algorithm
  Behavior Decision
  Conservative Sensing
  Collision Detection
  Collision Avoidance and Mitigation
Proofs
  Safety Proof
  Blame Proof
Experimental results
Notes: Other than the algorithm, I also propose the induction proofs that explain how the safe and blame-free state can be satisfied by BlaFT.

## Slide 25: Safety Proof: there is no accident in BlaFT-only traffic
Lane-changing AVs do not cut into other vehicle’s RE on the target lane.
RE overlap only happens at the front tip. And it is avoidable by braking.
Notes: The safety proof shows that the whole traffic is safe whenever it is BlaFT-only.
According to the algorithm, whenever all vehicles follow the BlaFT, then they satisfy the two things:
  First, lane-changing vehicles do not cut into other vehicles’ RE on the target lane, and lane-following vehicle’s RE is not overlapped by lane-changing vehicles.
  Second, the only moment that REs overlap is from the front vehicle. Even in this case, ego’s crash envelope is not overlapped so that it can resolve the overlap.
And this leads to the state that no crash envelope is overlapped and vehicles are ‘safe’ at every moment.

## Slide 26: Blame Proof: BlaFT is blame-free in hybrid traffic
Disproof of Negligence
  Lane-changing mode: ego AV does not allow RE overlap
  Lane-following mode: ego AV only allows the CE to overlap from the side
Notes: Next, the blame proof shows that AV with BlaFT is blame-free in hybrid traffic.
According to the algorithm, whenever AV follows the blaft, then it satisfies the two things:
  First, same as the safety proof, if BlaFT is lane-changing, then it does not make any overlap against others in the target lane.
  Second, as shown in the figure below, BlaFT only allows its CE to be overlapped with other vehicles’ REs that are coming from the adjacent lanes. Because of this reason, it equivalents that the overlap was ‘unpredictable’, or ‘not negligent’.

## Slide 27: Blame Proof: BlaFT is blame-free in hybrid traffic
Disproof of Causation
  If accident happened, it means that
    There was no safe response by the collision avoidance & mitigation process.
    AV was LF and the opponent was LC, thus AV has the right-of-way against the opponent.
Notes:   And in case an accident happened, it implies that it fulfilled the ‘due care’ by two facts:
    there was no possible response for collision avoidance,
    and the vehicle had a right-of-way against the opponent, since AV was lane-following and others must be lane-changing.
And this leads to the state that if crash happened, then BlaFT always has the right-of-way. Consequently, AV is blame-free at every moment.

## Slide 28: Outline
Definitions
Motion Planning Algorithm
Demonstrations
Proofs
  Safety Proof
  Blame Proof
Experimental results
  Traffic Setup
  Simulation
  Safety
  Efficiency
Notes: Lastly, we will discuss the experimental results.

## Slide 29: Traffic Setup: Aggressive HVs + BlaFT
Vehicular parameters by naturalistic driving data [9]
  AV assumes other’s parameters to be the worst ones (, , )
Scenario
  30 vehicles / 30 minutes / AV:HV = 0:30, 5:25, , 25:5, 30:0
  Road environment: two 4-lane loops around the intersection
    Lane width: 3.2m / Loop length: 1km
  Maximum velocity (): (27), (56)
  HV’s velocity distribution:
  HV’s minimum safe distance:
[9] Wishart, J., Como, S., Elli, M., Russo, B., Weast, J., Altekar, N., ... & Chen, Y. (2020). Driving safety performance assessment metrics for ads-equipped vehicles. SAE Technical Paper, 2(2020-01-1206).
 | () [] | () [] | () [] | [] | []
AV |  | () |  |  | 
HV (sensing) | () |  | () |  | 
AV |  |  |  |  | 
HV (sensing) |  |  |  |  | 
Notes: The vehicular parameters are based on naturalistic driving data shown in the table. I manipulated the response deceleration rate for each experiment to check if different RE length affects the traffic.
Also, AV senses other vehicle’s parameters to be the conservative ones, not to underestimate the worst-case sensing.
When it comes to the scenario, 30 vehicles drive for 30 minutes with different AV-HV ratio, such as from 0 versus 30, to 30 versus 0
The road environment is two 4-lane loops around the intersection, and its lane width is 3.2m and loop’s length is 1km
The allowed maximum velocity in the traffic was set to be 27 miles per hour or 56 miles per hour to assume the typical traffic.
Also, to simulate the collisions, I set human-driven vehicle’s velocity to follow normal distribution.
If the distance between vehicles is less than 0.1m, It is considered the collision. Then, the simulator makes the colliding human-driven vehicles drive safely at the moment.

## Slide 30: Simulation
Notes: Following the setup, the hybrid traffic simulation was done. As shown in the video, HVs, (or grey vehicles) and AVs, (or the white vehicles with colored envelopes) drive together on the structured road.

## Slide 31: BlaFT makes the hybrid traffic safer.
As BlaFT became more prevalent, the number of collisions linearly decreased.
No difference between different ‘’
  ** Distance less than 0.1m is considered a collision.
  ** Collided vehicles are teleported automatically by SUMO
Video #2: Sudden stop in HV-only traffic
Video #3: Sudden stop in hybrid traffic (BlaFT+HV)
Notes: To evaluate the safety empirically, we counted the number of collisions in each case. 10 experiments are done by differentiating the AV ratio, response deceleration rates, and the maximum velocities.
The X and Y-axis are AV ratio and the number of collisions to evaluate how the number of BlaFT affects collisions in the whole traffic.
The graph shows the average number of collisions and their error intervals by AV ratio.
The result tells that the number of collisions decreased linearly, as the number of BlaFT got increased while the number of human-driven vehicles decreased. When the ratio became 100%, the collision did not happen.
And this was common in both of the maximum velocities.
However, There was no significant difference in different response deceleration rates. In other words, BlaFT does not have to maintain a longer response distance from other vehicles, but it is just a matter of driver’s freedom.
And this came from the simple fact that BlaFT drives in a safe-guaranteeing way.
(CLICK) As shown in the first video, in HV-only traffic, some HVs might malfunction or stop at some point, cut into the lane so tightly, or maintain a very small distance. And when combined together, it leads to a collision.
(CLICK) However, the hybrid traffic with BlaFT becomes safer by maintaining the response distance, and reacting properly to the sudden danger.
As a result, more BlaFT AVs make hybrid traffic safer.
The other application is distributed cameras to take synchronized photos. In fact, 3D image reconstruction based on multiple 2D images taken from different angles of a scene has application in many fields, including entertainment, autonomous driving, and sports.
In this application, we had two cameras to take the images at the same time with tolerance of 100𝜇𝑠. Also, they should have taken the images at most 30 seconds after issuing the command. Therefore, we had two timing specifications: One as simultaneity for the events at which the photos are taken, and the other is the latency between the command and the actuation.
Obviously, they are not inconsistent, but we examined them by the deduction system.
The monitoring system was NI-9035 chassis with NI-9232 that had 14.8𝜇𝑠 as measurement uncertainty that is small enough to monitor a system with 100𝜇𝑠 tolerance.

## Slide 32: BlaFT makes hybrid traffic efficient
In slower traffic (),
  The difference in minimum safe distance between HV and AV is less significant.
  Length of RE is less affected by ‘’
In faster traffic (),
  The delayed time decreased by 0~34%.
  Shorter RE by larger ‘’ is more efficient.
Video #5: BlaFT with longer RE (, )
Video #6: BlaFT with shorter RE ()
Video #4: BlaFT in slow traffic (, )
Notes: And we checked if BlaFT can be efficient by measuring the delayed time of each vehicle.
The delayed time on the Y-axis means the vehicle’s time loss by the braking. So whenever vehicles brake more and frequently the delayed time increases.
Same as the previous one, we conducted 10 simulations for each AV-ratio, response deceleration rates, and maximum velocities.
The result shows that when it comes to the slower traffic, where the maximum velocity is 12m/s, there was no relevance between response deceleration rates and delay.
However, on average, the overall delay decreased about maximum 20% as BlaFT became more prevalent.
In the faster traffic, where its maximum velocity is 25m/s, it resulted in the bigger delayed times compared to the slower traffic.
Also, when the response deceleration was at a minimum, the delay did not change significantly. However, with two other bigger response deceleration rates, they showed 25% and 34% decrease in delayed time.
In other words, the key factor that affects the delayed time was the length of RE.
(CLICK) (CLICK)
First, In the slow traffic, BlaFT maintains the shorter RE compared to the ones in the fast traffic. As you see in the second video, the faster AVs brake more frequently than the other ones, since it has more chance of detecting the collision area because of longer RE.
However, BlaFT can choose its own response deceleration to be up to maximum deceleration rate.
(CLICK)
The last video shows the shorter RE that its length is much shorter than the second video. Even if the AVs are under the same maximum velocity, the smaller RE area prevents frequent braking.
As a result, as the maximum allowed velocity gets higher, the whole traffic becomes more efficient as BlaFT maintains shorter RE and endures the sharp braking.

## Slide 33: Conclusion
Contributions
  An algorithm of Blame-Free motion planning in hybrid Traffic (BlaFT).
  Proofs
    Safety proof: there is no collision in BlaFT-only traffic.
    Blame proof: BlaFT is blame-free against other drivers’ misbehavior.
  SUMO-based hybrid traffic simulation
  Experiments: more BlaFT AVs reduce collisions, and can be more efficient.
Future works
  Blame should be clear with other participants: emergency vehicles, pedestrians, etc.
  It needs vehicular dynamics to be more realistic
Notes: Throughout the presentation, I showed four contributions.
  First, I proposed a blame-free motion planning algorithm which works in hybrid traffic.
  Second, I proved by induction that BlaFT-only traffic is safe, and AV equipped with BlaFT is blame-free,
  Third, I showed the hybrid traffic simulation setup based on SUMO,
  And experimental results that more BlaFT AVs not just reduce collisions, but also can make the traffic to be efficient.
However, there are more works to be done in the future that
  Blame should also be clear with prioritized participants like emergency vehicles and pedestrians
  And it also needs more realistic dynamics so that the algorithm gets more accurate in physical world.
The other application is distributed cameras to take synchronized photos. In fact, 3D image reconstruction based on multiple 2D images taken from different angles of a scene has application in many fields, including entertainment, autonomous driving, and sports.
In this application, we had two cameras to take the images at the same time with tolerance of 100𝜇𝑠. Also, they should have taken the images at most 30 seconds after issuing the command. Therefore, we had two timing specifications: One as simultaneity for the events at which the photos are taken, and the other is the latency between the command and the actuation.
Obviously, they are not inconsistent, but we examined them by the deduction system.
The monitoring system was NI-9035 chassis with NI-9232 that had 14.8𝜇𝑠 as measurement uncertainty that is small enough to monitor a system with 100𝜇𝑠 tolerance.