## Slide 1: CHITIN: A Comprehensive In-thread Instruction Replication Technique Against Transient Faults
Hwisoo So*, Moslem Didehban&, Jinhyo Jung*, Aviral Shrivastava#, Kyoungwoo Lee*
*Dependable Computing Lab, Yonsei University, Seoul, Korea &Cadence Design Systems #Compiler Microarchitecture Lab, Arizona State University, Tempe, AZ
Presented by Hwisoo So
Notes: Hello everyone, I'm Hwisoo So.
I feel honored to speak at DATE conference.
Today, I want to present CHITIN, a comprehensive in-thread instruction replication technique against transient faults.

## Slide 2: Soft error: a main threat to the reliability
Reliability becomes one of the most important design concerns
Soft error is one of the main threats to the reliability
  Software-level redundancy can provides flexible soft error detection without hardware modification
Photo-illustration: iStockphoto
Photo-source:SpaceX Dragon
Photo-source:ULAN group
Notes: In modern applications such as autonomous driving, operating system for the space shuttle, and healthcare,
a minor malfunction can lead to catastrophic damage to human life.
Naturally, reliability has emerged as one of the most important design concerns.
Soft error, as known as transient fault, is one of the main threats to the reliability.
Software-level solution, which does not require hardware modification and the following costs, can be an alternative of traditional hardware approaches due to their flexibility.

## Slide 3: How software-level redundancy works?
Instruction replication: fundamental software-level redundancy
이거 알아보기 쉽게 R0 = R0 + 3 이런식으로
소프트 에러도 넣어야 될듯?
A = A + 1
B = B + 4
Store A  [B]
A = A + 1
A* = A* + 1
B = B + 4
B* = B* + 4
Check (A == A*) Check (B == B*)
Store A  [B]
Replicable
Non-replicable: should be checked
Original code
Protected code
B is corrupted
Notes: Instruction replication is a fundamental software-level solution against soft error.
In this example, original code calculates A and B, and uses them for a memory store.
For arithmetic instructions, (ANIM1) instruction replication replicates them, so it provides redundancy of calculations.
On the other hand, some instructions cannot be replicated. In this case, instruction replication should guarantee their correctness. (ANIM2) Therefore, checking instructions are added for non-replicable instructions.
Now, (ANIM3) if a soft error corrupts a calculation of B, (ANIM4) the replicated instance of B is still correct, and therefore (ANIM5) the presence of soft error can be detected at the checking instruction.

## Slide 4: Previous work: SWIFT
SWIFT: SoftWare Implemented Fault Tolerance [Reis 2005]
Arithmetic
Logical
Memory Load
Control-flow
Replicable
Instruction
Instruction duplication
Memory Store
Non-Replicable
Checking register operands before the store instruction
Signature-based checking
Previous work (nZDC) already resolved its weakness [Didehban 2016]
Domain of our work
[Reis 2005] REIS, George A., et al. SWIFT: Software implemented fault tolerance. In: International Symposium on Code Generation and Optimization. IEEE, 2005.
[Didehban 2016] DIDEHBAN, Moslem; SHRIVASTAVA, Aviral. nZDC: A compiler technique for near zero silent data corruption. In: 2016 53nd ACM/EDAC/IEEE Design Automation Conference (DAC). IEEE, 2016.
Notes: The most cited instruction replication for error detection is SWIFT.
SWIFT considers arithmetic, logical, and memory load instructions as replicable, [ANIM2] and duplicates them.
On the other hand, SWIFT does not replicate the memory store, and to guarantee the correctness of store, [ANIM2] SWIFT checks the register operands of the store right before its execution. [ANIM3] This solution has a vulnerable period, and previous work, nZDC, already resolved this problem.
SWIFT also does not replicate control-flow instructions such as jump and branch, [ANIM4] and protects these instruction with signature-base checking.
[ANIM5] Since control-flow protection is the domain of our work, I’m going to talk about the control-flow checking of SWIFT.

## Slide 5: SWIFT: protection for control-flow instruction
Initial passport: X
Initial passport: X
SWIFT adopts control-flow checking by software-signature[Oh 2002]
Block X
Block Y
Jump Y
Block X
Block Y
Set_passport (X  Y)
Check_passport (Y)
Updated passport: Y
Block Z
Check_passport (Z)
Jump Y
Original code
Protected code
[Oh 2002] OH, Nahmsuk; SHIRVANI, Philip P.; MCCLUSKEY, Edward J. Control-flow checking by software signatures. IEEE transactions on Reliability, 2002, 51.1
Mismatch can be detected
Notes: SWIFT adopts control-flow checking by software-signature to protect jump and branch instructions.
This solution is similar to publish and check the one-time passport before and after the movement between basic blocks.
Before the jump instruction to the block Y, (ANIM1) SWIFT publishes the passport to block Y.
And after it enters to the block Y, (ANIM2) SWIFT checks whether current control-flow has the right passport.
(ANIM3) Now, assume a soft error corrupts the jump instruction to incorrectly jump to block Z.
(ANIM4) Since it has the passport to the block Y, SWIFT can detects the presence of soft error.

## Slide 6: SWIFT: problem of control-flow protection
SWIFT cannot detect specific wrong-direction errors (Taken  Not-Taken)
SWIFT does not provide any information to protect function calls & returns
Block X
Block T
If (A==B) jump T
jump NT
Block NT
Block X
Block T
If (A*==B*) set_passport (XT)
If (A==B) jump T
Block NT
Original code
Protected code
Check_passport (T)
Check_passport (NT)
A=0, B=0, A*=0, B*=0
Set_passport (XNT)
jump NT
Updated passport: T
B=01
Updated passport: NT
Previous passport: T
SWIFT cannot detect such error since the passport looks valid
Notes: However, the control-flow protection of SWIFT has two problems.
At first, SWIFT can not detect specific wrong-direction errors at the branch instructions.
In this example, the control-flow branches to block T if A is equal to B. Otherwise, it jumps to block NT.
SWIFT applies signature-based checking (ANIM1) for the branch taken side, (ANIM2) and not-taken side.
(ANIM3) For an example, assume that variable A, B, and their copies are all 0.
(ANIM4) Then SWIFT publishes passport to block T.
(ANIM5) Now, soft error corrupts the variable B, and control-flow does not take the branch.
(ANIM6) Then, SWIFT publishes the passport to block NT, (ANIM7) and control-flow incorrectly moves to the block NT. (ANIM8) Since control-flow has passport to block NT, SWIFT cannot detect this error. (ANIM9) Furthermore, SWIFT does not provide any information to protect function calls and returns, even though these instructions also alter the control-flow.

## Slide 7: CHITIN: Summarization
CHITIN: a CompreHensive In-Thread INstruction replication technique against transient faults
Memory store
Load-back checking (adopted from nZDC)
Replicable
Instruction duplication (same to SWIFT)
Jump & branch
Improved signature-based checking
Function call & return
signature-based checking with redundant link register
Redundant link register
Contribution 1
Contribution 2
Notes: To resolve the vulnerabilities of the previous solutions, we want to propose CHITIN as a new instruction replication scheme.
CHITIN concentrates to improve the control-flow protection of SWIFT.
(ANIM1) At first, CHITIN improves the branch protection of SWIFT by separating the checking instruction from the effect of wrong-direction error.
(ANIM2) Secondly, CHITIN extends the control-flow protection to protect function call and returns, with redundant link register.
Now, I’m going to introduce each contribution of CHITIN.

## Slide 8: CHITIN: improved branch protection
CHITIN completely separates branch and its checking instructions
Block X
Block T
If (A*==B*) set_passport (XT)
If (A==B) jump T
Block NT
SWIFT-Protected code
Check_passport (T)
Check_passport (NT)
Set_passport (XNT)
Jump NT
Block X
Block T
If (A*==B*) set_passport (XT) else set_passport (XNT)
Block NT
CHITIN-Protected code
Check_passport (T)
Check_passport (NT)
If (A==B) jump T
Jump NT
Protection code depends on the
Protected code
Independent!
A=0, B=0, A*=0, B*=0
Current passport: T
B=01
The corruption of branch cannot be propagated to the passport
CHITIN can detect such error by invalid passport
Notes: The previous vulnerability of SWIFT branch protection originates from the fact that (ANIM1) the checking instruction depends on the result of the branch, which should be protected by the checking.
Therefore, (ANI3) CHITIN completely separates the checking instructions and the actual branches, (ANIM3) by adding opposite condition to the passport publication for the not-taken side.
(ANIM4) Now, similar to the previous example, assume all variables are 0 and CHITIN publishes passport to T. (ANIM5) A soft error corrupts the variable B, (ANIM6) but it cannot propagates the corruption to the passport publication.
(ANIM7) After the control-flow wrongly moves to block NT, (ANIM8) CHITIN can detect the error since it has invalid passport.

## Slide 9: CHITIN: function calls and returns protection
CHITIN extends its control-flow protection to protect function calls & returns by exploiting redundant link register
Function call
Function return
Jump to callee function
Update of link register (lr)
Special branch based on lr
Block A_X
Call Function_B
lr* = address(next(A_X))
Block B_Y
Return lr
if (lr* == return_candidate_0)
Set_passport (B_Y  candidate_0)
Set_passport (A_X  B_top)
Replication
`
Jump protection
`
Branch protection
based on redundant lr
elif (lr* == return_candidate 1)
Set_passport (B_Y  candidate_1)
Notes: To protect a function call instruction, (ANIM1) CHITIN treats it as a combination of link register update and jump to the top basic block of callee function.
Therefore, for a function call, (ANIM2) CHITIN replicates the update of link register, (ANIM3) and applies signature-based jump protection.
On the other hand, (ANIM4) CHITIN treats a function return instruction as a special branch instruction in which the target and direction are decided by link register.
Therefore, (ANIM5) CHITIN applies signature-based branch protection to the function return to publish the passport to the return point if the value of redundant link register indicate the possible return point.
Since a function can has multiple return point, (ANIM6) CHITIN should repeat such sequences for all possible return points.

## Slide 10: CHITIN: experimental results
Fault injection environment
  Failure classification: undetected output corruption
Verilog code of OpenRISC processor
7 components for injection
7
10,800
Injected 10,800 faults per benchmark/version
Chart: Total # of failure (log-scale)
| Original | SWIFT | nZDC | CHITIN
Failure Rate | 6173 | 849.4 | 534.3 | 53.6
Chart: Average of execution time
| Original | SWIFT | nZDC | CHITIN
Failure Rate | 1 | 2.6 | 3.84 | 3.31
7 benchmarks from miBench [Guthaus 20001]
7
[Reis 2005] GUTHAUS, Matthew R., et al. MiBench: A free, commercially representative embedded benchmark suite. In: Proceedings of the fourth annual IEEE international workshop on workload characterization. WWC-4 (Cat. No. 01EX538). IEEE, 2001.
1/10 failures
1/15 failures
Notes: To test the fault coverage of CHITIN, we conducted fault injection experiments with the Verilog code of OpenRISC processor.
We selected 7 benchmarks from the miBench, and 7 hardware components for fault injection.
For a benchmark and each protection, we injected total ten thousands eight hundreds faults.
We considered undetected output corruption as failure, and gathered the number of failures and the execution time overhead.
(ANIM1) Consequently, CHITIN shows just one tenth failure cases compared to the state-of-the-art nZDC.
Although CHITIN accompanies additional runtime overhead compared to the most-cited work SWIFT, (ANIM2) CHITIN shows just one fifteenth failure cases compared to SWIFT.

## Slide 11: CHITIN: conclusion
Branch
T
NT
Passport (signature)
T
NT
A fault on branch cannot corrupt the checking
Redundant link register
Applies signature checking to function call and return instructions
Function call
Function return
CHITIN: summary
CHITIN: result
compared to SWIFT (most-cited work)
Failure cases
compared to nZDC (state-of-the-art work)
Failure cases
Notes: Now, I’m going to summarize the CHITIN.
At first, CHITIN improves the branch protection of SWIFT by separating the checking instruction from the effect of branch corruption.
Secondly, CHITIN extends the control-flow protection to protect function calls and returns with redundant link register.
Experimental result shows that CHITIN shows one fifteenth and one tenth failure cases compared to SWIFT and nZDC, respectively. Thank you for listening my presentation, and please ask me if you have any questions