## Slide 1: Efficient & Effective Code Management for Software Managed Multicores CODES+ISSS 2013, Montreal, Canada
Ke Bai, Jing Lu, Aviral Shrivastava, and Bryce Holton
Compiler Microarchitecture Lab
Arizona State University

## Slide 2
Memory Scaling Challenge
Cache coherency protocols do not scale well
One option is Non-Coherent Cache Architectures
  Intel 48-core Single-chip Cloud Computer
  8-core DSP from Texas Instruments, TI 6678
Caches still consume too much power
  44% power, and greater than 34 % area [1]
Intel 48 core chip
[1] Segars et al., International Solid-State Circuits Conference Tutorial 2001

## Slide 3: SPM based Multicore Architecture
Data Array
Tag Array
Tag Comparators, Muxes
Cache
SPM
Address Decoder
Fast and low-power memory close to the core
30% less area and power than a direct mapped cache of the same effective capacity [2]
SPM based Multicore
  A truly distributed memory architecture on-a-chip
[2] Banakar CODES’02.
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Interconnect Bus
DMA
DMA
DMA
DMA
DMA
DMA
Main Memory
Main Processor
DMA
[2] Banakar CODES’02.

## Slide 4: Need Data Management in Software
int global;
f1(){
int a,b;
global = a + b;
f2();
}
int global;
f1(){
int a,b;
DMA.fetch(global)
global = a + b;
DMA.writeback(global)
DMA.fetch(f2)
f2();
}

## Slide 5: Data Management in SMM multicores
Manage any amount of heap, stack and code, in the core of an SMM manycore
  Global data
    If small, can be permanently located in the local memory
  Stack data
    ‘liveness’ depends on call path
    Function stack size know at compiler time, but not stack depth
  Heap data
    dynamic and size can be unbounded
  Code
    Statically linked
Our strategy
  Partition local memory into regions for each kind of data
  Manage each kind of data in a constant amount of space
code
global
stack
heap
heap
heap
stack

## Slide 6: Problem Context
If all code fits into SPM – very efficient execution
In general - Dynamic Code management is needed
All code must be managed
ARM
SPM
Global
Memory
DMA
ARM Memory Architecture
SPE
SPM
Global
Memory
DMA
IBM Cell Memory Architecture
SPM is for Optimization
SPM is Essential

## Slide 7: Code Management: Problem
Static Compilation
  Functions need to be linked before execution
Divide code part of SPM in regions
Map functions to these SPM regions
Functions in the same region placed at the same address
F1
F3
F6
F5
F7
F4
F2
REGION
REGION
REGION
•
•
•
Local Memory Code Section

## Slide 8: Code Management: Solution
(c) Local Memory
F2
F3
F1
Code
region
# of Regions and Function-To-Region Mapping
    Two extreme cases
Need careful code placement – Problem is NP-Complete
    Minimum data transfer with given space
(d) Global Memory
heap
global
stack
F2
F1
F3
F1
F2
F3
F1
F2
F3
(a) Application call graph
SECTIONS {
OVERLAY {
F1.o
F3.o
}
OVERLAY {
F2.o
}
}
(b) Linker script
Notes: I haven’t mentioned that the architecture is the Cell processor

## Slide 9: Optimizing Code Management
Previous attempts
  [Pabalkar08HIPC], [Baker10CODES+ISSS], [Jung10ASAP]
4 problems in interference calculation
1. Interference cost is not updated
2. Incorrect calculation, when a function is called at multiple places
3. Incorrect interference cost calculation in some cases
4. Do not consider branches
1KB
1.5KB
0.5KB
2KB
1.5KB
1KB
F1
F2
F3
F4
F5
F6
F2
1.5KB
1.5KB
F3
F4
F6
0.5KB
2KB
1KB
F1,F5
1.5KB
1.5KB
F3
0.5KB
F4
2KB
(a) Start
(b) Next step
(c) Final
F1
F5
F2
F6
Maximum (7.5KB)
Given (5.5KB)

## Slide 10: Update Interference Cost
Previous works
  Computed interference cost between functions before the start of the algorithm, and did not update it
However
  Where intermediate functions are mapped matters
main(), 3KB
F1(), 2KB
F2(), 1KB
F3(), 0.5KB
Main()
F1()
Region 0
3KB
Region 1
2KB
F3()
F2()
14KB Data Transfer
11.5KB Data Transfer
9.5KB Data Transfer

## Slide 11: Correct Interference Cost Calculation
Estimate interference between
  F3 and F5
Suppose
  F3 and F5 are mapped to the same region.
  Nothing else is mapped to the region
Previous techniques
  Estimate: 15*(size(F3) + size(F5))
  Min execution count of F3 and F5
Correct
  3*(size(F3)+size(F5))
main: 1
F1: 1
F2:
F3:
F4:
F5:
Loop
Loop
Loop
0
0
0
0
1
15
5
1
2
30
10
2
3
45
15
3

## Slide 12: Consider Branch Probabilities
Previous works
  Assume that both branches taken
If F4 is called 90% of the time
  Mapping F2, F1 in same region may be better than mapping F2, F4, F5 in same region
main: 1
F2: 1
F3: 1
F4: 9
F1: 1
condition
F5: 9
Loop

## Slide 13: Features of Our Technique
Update interference costs after mapping each function
Allow multiple instances of a function call
Correct interference cost calculation
  Proof is provided in the paper
Consider branch probabilities
  Estimate branch probabilities statically [Smith81ISCA]

## Slide 14: Effective Technique
Hardware
  Cell Processor in Sony PS3, running Linux
Chart: String_Search
| 632.0 | 760.0 | 888.0 | 1016.0 | 1144.0 | 1272.0 | 1400.0 | 1528.0 | 1656.0 | 1784.0 | 1912.0 | 2040.0 | 2168.0 | 2296.0 | 2424.0 | 2552.0 | 2680.0 | 2808.0 | 2936.0 | 3064.0 | 3192.0 | 3320.0 | 3448.0 | 3576.0 | 3704.0 | 3832.0 | 3960.0 | 4088.0 | 4216.0 | 4344.0 | 4472.0 | 4600.0 | 4728.0
CMSM | 9866472.08 | 9847813.2 | 9835170.8 | 8511191.02 | 8483268.66 | 8226609.22 | 8079626.52 | 7946914.08 | 7800467.84 | 7752742.72 | 7789979.66 | 7842976.66 | 7817717.28 | 7887195.88 | 7855349.7 | 7907315.32 | 7881079.44 | 7835993.66 | 7848142.66 | 7809638.26 | 7850111.86 | 7808198.78 | 7850838.02 | 7813866.32 | 7858426.12 | 7841351.26 | 7776379.18 | 7698014.82 | 7613597.48 | 7668733.06 | 7615671.66 | 7639777.36 | 7681056.4
FMUM | 9850460.04 | 9851475.12 | 9845395.3 | 9837726.26 | 9863853.74 | 9859480.24 | 9852920.08 | 9878320.7 | 9860396.46 | 8898426.58 | 8878131.56 | 8596060.76 | 8543335.72 | 8504845.86 | 8105305.66 | 8163739.62 | 8160306 | 8373584.8 | 8470088.5 | 8257175.46 | 8110856.58 | 8121365.26 | 8112480.52 | 8152053.2 | 8107747.92 | 7877259.94 | 7887887.98 | 7852499.36 | 7859939.58 | 7836835.74 | 7826100.72 | 7794037.06 | 7788180.38
FMUP | 9825659.68 | 9814935.64 | 8738900.04 | 8730800.12 | 8316310.64 | 8300037.78 | 8110505.88 | 8189434.46 | 8417743.78 | 8113551.92 | 8469488.6 | 8599729.24 | 8665321.44 | 9035131.84 | 8387915.18 | 8725609.28 | 8355140.98 | 8705379.66 | 8310782.72 | 8112901.76 | 8710253.6 | 8774770.3 | 8779882.14 | 8593985.8 | 8178456.76 | 8182699.24 | 8190877.02 | 8127295.48 | 8008701.26 | 8082211.3 | 8011150.78 | 8022488.86 | 8042112.76
Compiler modifications in
  GCC 4.6
Benchmarks
  Mibench
Effective
  Performance improvement from cost calculation
CMSM gives a better result than other two algorithms 89% of time

## Slide 15: Accurate Cost Calculation
Chart: Normalized runtime
| Adpcm_decoding | Adpcm_encoding | Susan_Edges | Susan_Smoothing | String_Search | BasicMath | Dijkstra | FFT | FFT_inverse
FMUM | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FMUM_accurate | 0.9957 | 0.99817 | 1.0559 | 1.001 | 0.96314 | 0.8826 | 0.91716 | 0.87121 | 0.87122
FMUP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FMUP_accurate | 1.0059 | 1.0003 | 1.0054 | 0.99788 | 0.97141 | 0.90803 | 0.92916 | 0.86821 | 0.86722
12% performance improvement when previous techniques use accurate cost estimation

## Slide 16: Comparison with Caches
Cache Miss penalty = # misses * miss latency
SPM miss overhead = # API function calls * no. of instructions in API function + # times DMA is called * delay of the DMA (dep. on DMA size)
Cache is better when miss latency < 260 ps
260 ps = 0.86 * cycle time

## Slide 17: Scalability
Running identical benchmarks on each core
Chart: Number of cores
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0
Adpcm_decoding | 1 | 1.08 | 1.1214 | 1.1771 | 1.2571 | 1.3257
Adpcm_encoding | 1 | 1.0008 | 1.0017 | 1.0027 | 1.0037 | 1.0046
BasicMath | 1 | 1.124 | 1.23 | 1.31 | 1.44 | 1.59
Dijkstra | 1 | 1.0001 | 1.0002 | 1.0004 | 1.0005 | 1.0006
FFT | 1 | 1.0014 | 1.0031 | 1.0043 | 1.0056 | 1.0071
FFT_inverse | 1 | 1.0007 | 1.0019 | 1.0026 | 1.0037 | 1.0047
String_Search | 1 | 1.0003 | 1.0007 | 1.0011 | 1.0015 | 1.0022
Susan_Edges | 1 | 1.0007 | 1.0015 | 1.0022 | 1.003 | 1.0039
Susan_Smoothing | 1 | 1.0007 | 1.0015 | 1.0022 | 1.003 | 1.0039

## Slide 18: Summary
SPM based multicore architectures are scalable and power-efficient
However need to perform code and data management
Code Management
  We identified 4 shortcomings in previous techniques
Our approach
  Correctly calculates interference between functions
  Considers branch probabilities
  Better mapping 89% of time
  Accuracy improves performance by 12%