## Slide 1: Automatic and Efﬁcient Heap Data Management for Limited Local Memory Multicore Architectures
Ke Bai and Aviral Shrivastava
Presented by Bryce Holton
Compiler Microarchitecture Lab
Arizona State University, USA
C
M
L

## Slide 2: Outline of my Presentation
Why Scratchpad based Multicore Architecture
The Need to Manage Heap Data
Comparison with Software Cache
State of the Art Heap Management
Our Approach
Results
Summary
References

## Slide 3: Why Scratchpad based Multicore Architectures?
Memory scaling becomes a major problem when designing multicore/many core architecture
  H/W cache consumes too much power
Limited Local Memory (LLM) multicore architecture is scalable
  Local memory is a scratchpad memory, which is power efﬁcient
    “un-cached” raw memory; 30% less area and power than a direct mapped cache of the same effective capacity [3]
  One example of such architecture is IBM Cell processor
    Execution core (EC) has only scratchpad, no cache; can directly access SPM
    Main core has a global memory, which requires EC using DMA to access it
Processor | Fab | Frequency | GFlops | Power | Power Efficiency
Cell/B.E. | 45nm | 3.2 GHz | 230 | 50 W | 4.6
Intel i7 4-core Bloomfield 965 XE | 45nm | 3.2 GHz | 70 | 130 W | 0.5

## Slide 4: The Need to Manage Heap Data
Programming on LLM architecture requires code and data of the mapped task must fit in SPM
In many cases, memory requirement is larger than SPM (e.g., SPM on Cell processor is only 256KB large)
  Explicit data management through DMA is needed [4]-[7]
This presentation focuses on heap data
  It is dynamic in nature
  Can be unbounded
code
global
stack
heap
heap
heap
stack
main() {
for (i=0; i<N; i++) {
item[i] = malloc(sizeof(Item));
}
F1();
}
The task mapped to the core
Stack/heap

## Slide 5: Comparison with Software Cache
Software cache
  Need to change the structure of the original program
Code on main core
Code on execution core
Execution Thread
Contains malloc() Call
Execution Thread
spu_write_out_mbox(sizeof(data));
Heap Management Thread
spe_out_mbox_read(id, size, …);
ppuAdd = malloc(size);
spe_in_mbox_write(id, &gAddr…);
Main Thread
pthread_create ( …ID …);
pthread_create(…&heapManage…)

## Slide 6: State of the Art [8]: Heap Management … CODE+ISSS 2010
HeapPtr = malloc();
HeapPtr->val = val;
…
val_rd = HeapPtr->val;
free(HeapPtr);
Original Code
Transformation by programmer
HeapPtr = _malloc();
HeapPtr = _g2l(HeapPtr);
HeapPtr->val = val;
HeapPtr = _l2g(HeapPtr);
…
HeapPtr = _g2l(HeapPtr);
val_rd = HeapPtr->val;
HeapPtr = _l2g(HeapPtr);
_free(HeapPtr);
Problems
  Semi-automatic
  Quite high performance overhead
    manages heap data in a highly associative data structure with LRU (Least Recently Used) replacement policy.
    overhead = DMA overhead + extra instructions
    has to manage both heap data and heap management table , which only adds to the overhead.
 | _malloc | _free | _g2l |  | _l2g
 |  |  | hit | miss | 
[8] | 948 | 50 | 280 | 373 | 243
Dynamic instructions per library function

## Slide 7: This Approach
This approach
HeapPtr = _malloc();
T = _g2l(HeapPtr);
T->val = val;
…
T = _g2l(HeapPtr);
val_rd = T->val;
_free(HeapPtr);
HeapPtr = malloc();
HeapPtr->val = val;
…
val_rd = HeapPtr->val;
free(HeapPtr);
Original Code
Previous Approach[8]
Advantages
  Removes _l2g
  Compiler automatically inserts _g2l
  Multilevel pointers are also supported.
HeapPtr = _malloc();
HeapPtr = _g2l(HeapPtr);
HeapPtr->val = val;
HeapPtr = _l2g(HeapPtr);
…
HeapPtr = _g2l(HeapPtr);
val_rd = HeapPtr->val;
HeapPtr = _l2g(HeapPtr);
_free(HeapPtr);

## Slide 8: Overview of our Approach
.c
Runtime
Library
.a
Modified Compiler
.o
Linker
Executable
_malloc(size) allocates space in global memory and returns a global address.
_free(global addr) deallocates space in global memory
_g2l(global addr) translates the global address to a local address and fetches the object pointed by global address if it is not in local memory
Transformed Code
IP = _malloc(sizeof(item));
…
T = _g2l(IP);
…
T->val = val;
…
val_rd = T->val;
IP = malloc(sizeof(item));
…
IP->val = val;
…
val_rd = IP->val;
Original Code
 | _malloc | _free | _g2l |  | _l2g
 |  |  | hit | miss | 
[8] | 948 | 50 | 280 | 373 | 243
Ours | 60 | 20 | 51 | 117 | 0
Much less !
Dynamic instructions per library function

## Slide 9: Automatic and Efficient Technique
Hardware
  IBM Cell processor
    1 PPE + 6 SPE
Benchmarks
  Mibench – modified to multi-threaded
  Other possible applications
Chart: Number of Nodes
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 6800 | 8192 | 16384 | 32768 | 65536 | 131072
No Management | 1031.3032 | 1179.2607 | 1405.6767 | 1815.6328 | 2680.3728 | 4454.0602 | 8146.3597 | 15297.0864 | 29713.8442 | 58424.4209 | 118237.6484 | 230202.6133 | 459534.0156 | 780794.0781
Previous Approach | 1364.787 | 1555.2913 | 1936.2782 | 2703.2801 | 4243.3303 | 7383.5056 | 14407.8794 | 26854.1011 | 52566.5391 | 104645.6133 | 210602.2695 | 431196.3125 | 894247.6406 | 1557250.4062 | 1914115.5625 | 4312032 | 9462475.5 | 18937654.5 | 25486216.1
Our Approach | 1035.4772 | 1194.4346 | 1499.8506 | 1979.8068 | 2837.5467 | 4709.2341 | 8960.5337 | 18141.2604 | 35718.0182 | 63428.5948 | 149741.8224 | 293209.7872 | 569538.1896 | 864798.2521 | 934236.5101 | 1171252.9476 | 1432596.4476 | 1897775.4476 | 2288633.0476
N0 = 6800

## Slide 10: More Experimental results
Chart: Normalized Runtime
| 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
DFS | 1 | 0.99324 | 0.98368 | 0.97322 | 0.97098 | 0.96901 | 0.97326 | 1.026 | 1.0358
dijkstra | 1 | 0.62877 | 0.44859 | 0.36107 | 0.32249 | 0.30403 | 0.29201 | 0.28306 | 0.28046
fft | 1 | 0.98202 | 0.97033 | 0.95617 | 0.95882 | 0.95731 | 0.96744 | 0.98548 | 1.0481
invfft | 1 | 0.9772 | 0.96024 | 0.95106 | 0.95308 | 0.95304 | 0.96295 | 0.98921 | 1.0508
MST | 1 | 0.90742 | 0.85302 | 0.81318 | 0.79299 | 0.75715 | 0.7458 | 0.83226 | 0.93345
rbTree | 1 | 0.97131 | 0.95033 | 0.93117 | 0.91782 | 0.92931 | 0.94444 | 0.97148 | 1.0331
stringsearch | 1 | 0.80471 | 0.70326 | 0.6569 | 0.63112 | 0.6178 | 0.60234 | 0.59486 | 0.59854
Chart: 
| DFS | dijkstra | fft | invfft | MST | rbTree | stringsearch | Average
direct mapped | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2-way associative | 1.0221 | 1.0598 | 0.89383 | 0.88196 | 0.99684 | 0.99402 | 1.0385 | 0.98387
4-way associative | 1.0063 | 1.0518 | 0.82848 | 0.81181 | 0.86439 | 0.96755 | 1.0554 | 0.85253
8-way associative | 1.0679 | 1.1987 | 0.84736 | 0.83308 | 0.99404 | 1.0086 | 1.1196 | 1.0099
Chart: Normalized Runtime
| DFS | dijkstra | fft | invfft | MST | rbTree | stringsearch
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1.1762 | 1.0989 | 1.0367 | 1.0667 | 1.0499 | 1.0674 | 1.0398
2 | 1.1686 | 1.0988 | 1.0177 | 1.0675 | 1.0531 | 1.0701 | 1.0477
3 | 1.1729 | 1.0996 | 1.0358 | 1.0666 | 0.97319 | 1.0698 | 1.0435
4 | 1.1702 | 1.2052 | 1.0359 | 1.0147 | 1.0585 | 1.0771 | 1.0491
Chart: Number of Cores
| 1 | 2 | 3 | 4 | 5 | 6
basicmath | 1 | 1.0017 | 1.0021 | 1.0034 | 1.0041 | 1.0059
DFS | 1 | 1.0107 | 1.0151 | 1.0234 | 1.0287 | 1.0336
dijkstra | 1 | 1.0099 | 1.0211 | 1.0374 | 1.0411 | 1.0493
fft | 1 | 1.0107 | 1.0211 | 1.0364 | 1.0429 | 1.0513
invfft | 1 | 1.011 | 1.0209 | 1.0357 | 1.0469 | 1.056
MST | 1 | 1.0117 | 1.0213 | 1.0294 | 1.0397 | 1.0438
rbTree | 1 | 1.0117 | 1.0191 | 1.0264 | 1.037 | 1.0481
sha | 1 | 1.0017 | 1.0024 | 1.0032 | 1.0046 | 1.0056
stringsearch | 1 | 1.0017 | 1.0021 | 1.0024 | 1.0031 | 1.0043
Impact of victim buffer

## Slide 11: Summary
Our compilation and runtime system can manage unlimited size of heap data for LLM multi-core architectures.
We explored different block sizes, set associativities and victim buffer sizes.
  Our results indicate that a 4-way associative heap cache without victim buffer is the best overall design
Our system is scalable.
Heap cache should be simple
  Complex cache architecture and replacement policy will only make extra library instruction bigger, but the space locality of heap data is insignificant.

## Slide 12: References
[1] http://en.wikipedia.org/wiki/List_of_Intel_microprocessors#Core_i7
[2] http://www.tomshardware.com/charts/desktop-cpu-charts-2010/Raw-Performance-SiSoftware-Sandra-2010-Pro-GFLOPS,2409.html
[3] R. Banakar, et al. “Scratchpad Memory: Design Alternative for Cache on-chip Memory in Embedded Systems”
[4] S. C. Jung, et al. “Dynamic Code Mapping for Limited Local Memory Systems”
[5] K. Bai, et al. “Stack Data Management for Limited Local Memory (LLM) Multi-core Processors”
[6] J. Lu, et al. “SSDM: Smart Stack Data Management for Software Managed Multicores (SMMs) ”
[7] K. Bai, et al. “Vector Class on Limited Local Memory (LLM) Multi-core Processors”
[8] K. Bai, et al. “Heap Data Management for Limited Local Memory (LLM) Multi-core Processors”