## Slide 1: Scratchpad Management in Software Managed Manycore Architectures
Jian Cai
Compiler Microarchitecture Lab
Arizona State University

## Slide 2: Challenges of Scaling Manycore Processors
Scaling memory hierarchy in multi-/many-core processors poses challenges due to the increased cost of maintaining cache coherence
  Area and power overhead of implementing cache coherence increases rapidly as the number of cores grows
Potential solutions
  Hardware solution
    Keep improving cache coherence mechanisms
  Software solution (our approach)
    Explore software-managed memories, such as scratchpad memories (SPMs)

## Slide 3: Scratchpad Memory
Simple hardware design and verification
  Remove tag arrays, comparators and muxes
  Remove cache coherence logics
  ~30% less area and power compared to the cache of same size
Data Array
Tag Array
Tag Comparators, Muxes
Address Decoder
Cache
SPM
Banakar et al, CODES 2002

## Slide 4: Software Managed Manycore (SMM)
Core
SPM
Main Memory
DMA
Core
SPM
DMA
Core
SPM
DMA
Core
SPM
DMA
SPM-only architecture
  Cores have scratchpad memories instead of caches
  Software managed data movements
  Used in various areas
    Embedded computing: Qualcomm coprocessors, ARM processors, TI C66x processors
    High performance: REX Neo, Intel Traleika Glacier
    Network on a chip: Epiphany-V
    Gaming and multimedia: IBM cell

## Slide 5: Challenges in Utilizing SMM
(b) With Management Code
(a) Original Code
int global;
f1() {
int a,b;
global = a + b;
f2();
}
int global;
f1() {
int a,b;
DMA.loadVar(global);
global = a + b;
DMA.storeVar(global);
DMA.loadCode(f2);
f2();
DMA.loadCode(f1);
}
Insert explicit data movements
    SPM is typically physically addressed, and mapped to a fixed virtual address range different from main memory's
Different approaches causes drastically different performance

## Slide 6: The Novelty of My Work
Static
      PandaEDTC1997, SjodinCASES2001, AvissarCASES2001, AvissarTECS2002, NguyenCASES2005, VermaASPDAC2003, SteinkeDATE2002
Dynamic
    EggerTECS2008, EggerITC2010, IshitobiJSPS2010, KandemirDAC2001, PandaTODAES2000, LiPACT2005, JiaTECS2015, UdayakumaranCASES2003, DominguezJEC2005, UdayakumaranDATE2006, UdayakumaranTECS2006, DominguezCASES2007, VermaVLSI2006, ChakrabortyCASES2012
Our
work
Profile-driven
Our approach does not rely on profile information and applies to a wider range of applications

## Slide 7: The Objective of My Work
Main Memory
SPM
shared data
stack
heap
ASAP2011
DAC2013
ASAP2016
CODES+ISSS 2010
DATE 2013
VLSID2016
SPM
Core 2
Develop techniques for managing data on SPM
  Not profile-driven
  Manage different types of data efficiently
code
ASAP 2010
CODES+ISSS 2013
RTAS 2014
ICCAD 2016
DATE 2016
Core 1
shared data
stack
heap
code
Task 1: Code Management
Task 2: Stack Data Management
Task 3: Heap Data Management

## Slide 8: Code Management: General Solution
Divide SPM space into regions and map each function to one of the regions
Insert code around each function call to manage function code
Overhead consists of memory transfers (communication) and extra instructions (computation)
int main() {
for (i = 0; i < 100; ++i) {
f1(i);
}
f2();
}
int main() {
spm_main=cget(main);
spm_main();
}
int spm_main() {
for (i = 0; i < 100; ++i) {
spm_f1=c_get(f1);
spm_f1(i);
cget(main);
}
spm_f2=cget(f2);
spm_f2();
cget(main);
}
main
f1
f2
SPM
memory
(a) original code
(b) code management
main
f1
f2
memory
r1
r0

## Slide 9: The Previous Approach
Refine mapping to reduce minimum memory transfer
Lu Et al., Efficient Code Assignment Techniques for Local Memory on Software Managed Multicores, TECS2015

## Slide 10: Our Approach
Remove unnecessary management functions
r0: main
r1: F1,F3
r2: F0, F2
call F1
cget(main)
cget(F0)
call F0
cget(main)
cget(F2)
call F2
cget(main)
cget(F3)
call F3
cget(main)
cget(F0)
call F0
cget(main)
overlaying
cget(F1)
Cai et al., Reducing Code Management Overhead in Software-Managed Multicores, DATE2017

## Slide 11: Steps of Our Approach
Given the function-to-region mapping, perform data-flow analyses to identify
  Always-hit function calls
    Performed once to each program
  First-miss function calls
    Performed loop by loop
Overlaying Scheme
AH & FM locations
Compiler
Our analyses
Program
CFGs
Executable with management functions

## Slide 12: First-miss Analysis
A data flow value is a map ss : R → F, where
  R = {r 1 ,...,r n } is the set of regions the SPM space is divided into
  F consists of the set of functions called in the program {f 1 ,...,f m }, UNDEF, and NAC
Meet operator
  evicts any function that is not the only possible function being called among the functions that are mapped to the same region within the loop

## Slide 13: First-miss Analysis Example
Analysis of loop L2 in main function
Assume F0, F1 and F2 do not call any other function
call F1
call F2
call F0
{main},{F1},{UD}
{main},{UD},{UD}
{main},{UD},{UD}
{main},{F1},{F2}
main
{main},{UD},{UD}
{main},{UD},{UD}
{main},{F1},{F0}
{main},{F1},{F0}
{main},{F1},{NAC}
{main},{F1},{NAC}
{main},{F1},{NAC}
r0: main
r1: F1
r2: F0, F2
L2
L1
overlaying
{main},{F1},{NAC}
{main},{F1},{F2}

## Slide 14: Experimental Setup
LLVM
  Inserts code management instructions at IR
Gem5
  CPU
    X86 ISA
    frequency = 1.2 GHz
  L1 SPM
    Code is managed on SPM
    The rest memory accesses are all assumed to be hits
  DMA [1]
    cost = startup cost + size / transfer rate
      startup cost = 150 ns (180 cycles)
      transfer rate = 12800 MB/s (10.67 B/cycle)
[1] Texas Instrument., Throughput Performance Guide for KeyStone II Devices
Core
Main Memory
L1 SPM

## Slide 15: Comparison with The State of The Art
Normalized to the execution time with the state of the art [1]
SPM Size = min code size + percentage * (max code size – min code size)
Improve 7% performance on average, and improvement becomes more as size increases
Chart: Normalized Execution Time
| adpcm.decode | adpcm.encode | basicmath | CRC32 | dijkstra | FFT | IFFT | patricia | rijndael.decode | rijndael.encode | sha | stringsearch | susan.corners | susan.edges | susan.smoothing | average
25% | 0.99835 | 0.99875 | 0.65979 | 1 | 0.95554 | 0.84755 | 0.86754 | 0.95143 | 0.90108 | 0.8933 | 0.96306 | 0.9155 | 0.99956 | 0.99979 | 1 | 0.93008
50% | 0.99835 | 0.99875 | 0.65979 | 1 | 0.95554 | 0.84757 | 0.86754 | 0.44883 | 0.90108 | 0.91316 | 0.9417 | 0.9155 | 0.99937 | 0.99974 | 0.99998 | 0.89646
75% | 0.99835 | 0.99875 | 0.65979 | 1 | 0.94915 | 0.81842 | 0.83044 | 0.2737 | 0.90718 | 0.91316 | 0.94603 | 0.9155 | 0.99936 | 0.99966 | 0.99998 | 0.88063
[1] Lu Et al., Efficient Code Assignment Techniques for Local Memory on Software Managed Multicores, TECS2015

## Slide 16: The Objective of My Work
Main Memory
SPM
shared data
stack
heap
ASAP2011
DAC2013
ASAP2016
CODES+ISSS 2010
DATE 2013
VLSID2016
SPM
Core 2
Develop techniques for managing data on SPM
  Not profile-driven
  Manage different types of application data efficiently
code
ASAP 2010
CODES+ISSS 2013
RTAS 2014
ICCAD 2016
DATE 2016
Core 1
shared data
stack
heap
code
Task 1: Code Management
Task 2: Stack Data Management
Task 3: Heap Data Management

## Slide 17: Stack Management: General Solution
Redirect stack pointer to an SPM address at the beginning of execution and restore at the end
Manage stack frames
  Allocate SPM space for the stack frames of incoming function calls , and evict the oldest stack frames when necessary
Manage pointers
  Stack accesses via pointers may be affected by the movement of stack frames and must be managed accordingly
int f2(int *p){
*p = rand();
}
int f1(){
int a = 5;
for(i=0; i < 100;i++) {
f2(&a);
}
}
int main(){
f1();
}
int f2(int *p){
*g2l(p) = rand();
}
int f1(){
int a = 5;
for(i=0; i < 100;i++) {
sstore();
f2(l2g(&a));
sload();
}
}
int main(){
sstore();
f1();
sload();
}
(a) original code
(b) stack management
f2
spm
mem
f1
f1
main
main
f2
mem
f1
main

## Slide 18: Stack Management: Our Solution
Minimize management overhead
  Manage multiple stack frames of consecutive function calls at a time
  Avoid unnecessary pointer management
int f2(int *p){
*g2l(p) = rand();
}
int f1(){
int a = 5;
for(i=0; i < 100;i++) {
sstore();
f2(l2g(&a));
sload();
}
}
int main(){
sstore();
f1();
sload();
}
*p = rand();
f2(&a);
f1
f2
spm
f2
spm
spm
f1
spm
main
Cai Et al., Efficient Pointer Management of Stack Data for Software Managed Multicores, ASAP2016
spm
f1
spm
main
Lu Et al., Efficient Code Assignment Techniques for Local Memory on Software Managed Multicores, TECS2015
Stack Management: Previous Solution

## Slide 19: Steps of Our Approach
Identifying Stack Data Pointers at Function Calls
Group stack frames of adjacent function calls
Inserting Pointer Management Functions

## Slide 20: Experimental Setup
LLVM
  Inserts stack management instructions at IR
Gem5
  CPU
    X86 ISA
    frequency = 1.2 GHz
  L1 SPM
    Stack data is managed on SPM
    The rest memory accesses are all assumed to be hits
  DMA [1]
    cost = startup cost + size / transfer rate
      startup cost = 150 ns (180 cycles)
      transfer rate = 12800 MB/s (10.67 B/cycle)
[1] Texas Instrument., Throughput Performance Guide for KeyStone II Devices
Core
Main Memory
L1 SPM

## Slide 21: Comparison with The State of The Art
Normalized to the execution time with the state of the art
SPM Size = min stack size + percentage * (max stack size – min stack size)
Reduce execution time by 49% on average
Chart: Normalized Execution Time
| adpcm.decode | adpcm.encode | basicmath | CRC32 | dijkstra | FFT | IFFT | patricia | rijndael.decode | rijndael.encode | sha | stringsearch | susan.corners | susan.edges | susan.smoothing | average
25% | 1.0169 | 0.99677 | 0.90719 | 0.13699 | 0.95734 | 0.26954 | 0.26538 | 0.75941 | 0.2883 | 0.19118 | 0.799 | 0.59494 | 0.15824 | 0.13162 | 0.32131 | 0.51961
50% | 1.0169 | 0.99677 | 0.35454 | 0.08547 | 0.94355 | 0.28085 | 0.27692 | 0.75439 | 0.1929 | 0.19118 | 0.799 | 0.59494 | 0.15824 | 0.13162 | 0.32131 | 0.47324
75% | 1.0169 | 0.99677 | 0.35454 | 0.08547 | 0.94355 | 0.28085 | 0.27692 | 0.75439 | 0.1929 | 0.19118 | 0.48344 | 0.59494 | 0.15824 | 0.13162 | 0.32131 | 0.4522

## Slide 22: The Objective of My Work
Main Memory
SPM
shared data
stack
heap
ASAP2011
DAC2013
ASAP2016
CODES+ISSS 2010
DATE 2013
VLSID2016
SPM
Core 2
Develop techniques for managing data on SPM
  Not profile-driven
  Manage different types of application data efficiently
code
ASAP 2010
CODES+ISSS 2013
RTAS 2014
ICCAD 2016
DATE 2016
Core 1
shared data
stack
heap
code
Task 1: Code Management
Task 2: Stack data Management
Task 3: Heap Data Management

## Slide 23: Heap Management: General Solution
int main() {
int *a;
a = malloc(20);
a[3] = 5;
}
int main() {
int *a;
a = malloc(20);
*g2l(&a[3]) = 5;
}
DMA
Main Memory
SPM
&a[3]
g2l(&a[3])
example code
example code with
heap management
Use SPM as a software-managed cache
Insert code around each memory access to manage (potential) heap accesses
Overhead consists of memory transfers (communication) and extra instructions (computation)

## Slide 24: Previous Approach
Get Set Index
Memory Address
Sequential Search
Replacement Policy
Data Movement
SPM Address Calculation
yes
Runtime Address Check
n sets
4 Entries
SPM
hit
no
int *p1, *p2;
int a = 10;
p1 = malloc(20);
p2 = &a;
*p1 = 8;
*p2 = *p2 + 5;
int *p1, *p2;
int a = 10;
g2l(p1) = malloc(20);
g2l(p2) = &a;
*g2l(p1) = 8;
*g2l(p2) = *g2l(p2) + 5;
Intercept all the memory accesses with g2l calls
Filters non-heap accesses at runtime
Emulates the mechanism of a 4-way set-associative cache

## Slide 25: Our Approach: Reduce g2l Calls
int *p1, *p2, *p3;
int a = 10;
p1 = malloc(20);
p2 = p1;
*p2 = 10;
*p3 = *p3 + 5;
int *p1, *p2;
p1 = malloc(20);
p2 = p1;
*g2l(p2) = 10;
*p3 = *p3 + 5;
Identify heap accesses at compile time (thus eliminating runtime check in g2l)
  Find heap allocations
  Find aliasing pointers (aka. heap pointers)
  Insert g2l only at data accesses through heap pointers
malloc(20)
p1
p2
alias
int *p1, *p2;
g2l(p1) = malloc(20);
g2l(p2) = g2l(p1);
*g2l(p2) = 10;
*g2l(p3) = *g2l(p3) + 5;

## Slide 26: Our Approach: Reduce g2l Steps
Get Set Index
Memory Address
Sequential Search
Replacement Policy
Data Movement
SPM Address Calculation
yes
Runtime Address Check
hit
no
Emulates the mechanism of a direct-mapped cache to simplify g2l functions
SPM
Sets
1 Entry
Sets
4 Entries
SPM

## Slide 27: Our Approach: Inline and Combine g2l Calls
void *g2l(void *addr) {
common_steps();
return get_spm_addr(addr);
}
int main() {
int *a = malloc(80);
*g2l(&a [0]) = 2;
*g2l(&a[1]) = 4;
for(i = 2; i < n; i++)
*g2l(&a[i]) = i;
}
int main() {
common_steps();
* get_spm_addr(&a[0]) = 2;
* get_spm_addr(&a [1]) = 4;
for(i = 2; i < n; i++)
* get_spm_addr(&a[i]) = i;
}
(b) Basic heap management
(c) Inlining and combining calls
int main() {
int *a = malloc(80);
a0] = 2;
a[1] = 4;
for(i = 2; i < n; i++)
a[i] = i;
}
(a) Sample code
Inline g2l calls and remove redundant steps

## Slide 28: Experimental Setup
LLVM
  Inserts heap management instructions at IR
Gem5
  CPU
    X86 ISA
    frequency = 1.2 GHz
  L1 SPM
    Heap data is managed on SPM
    The rest memory accesses are all assumed to be hits
  DMA [1]
    cost = startup cost + size / transfer rate
      startup cost = 150 ns (180 cycles)
      transfer rate = 12800 MB/s (10.67 B/cycle)
[1] Texas Instrument., Throughput Performance Guide for KeyStone II Devices
Core
Main Memory
L1 SPM

## Slide 29: Reduced Execution Time
Chart: A: Reduce g2l calls B: Reduce g2l steps C: Inline and combine g2l Calls
| ADPCM Dec. | ADPCM Enc. | Dijkstra | FFT | iFFT | Patricia | SHA | String Search | Susan Corner | Susan Edge | Susan Smoothing | Typeset | Average
A | 0.098603 | 0.08622 | 0.53919 | 0.74584 | 0.74582 | 0.74256 | 0.083329 | 0.15001 | 0.56977 | 0.58038 | 0.44037 | 0.28468 | 0.42223
A+B | 0.098603 | 0.086221 | 0.23129 | 0.48273 | 0.48266 | 0.51559 | 0.083325 | 0.15006 | 0.22965 | 0.22242 | 0.17383 | 0.22118 | 0.24813
A+B+C | 0.098603 | 0.086221 | 0.15584 | 0.38613 | 0.38605 | 0.46512 | 0.083325 | 0.15006 | 0.12723 | 0.12127 | 0.10705 | 0.21686 | 0.19865
Normalized to the execution time of the state of the art

## Slide 30: Normalized Execution Time as SPM Size Increases
Chart: Normalized Execution Time
| 4.0 | 8.0 | 16.0 | 32.0 | 64.0
ADPCM Dec. | 0.098603 | 0.098603 | 0.098603 | 0.098602 | 0.098601
ADPCM Enc. | 0.086221 | 0.086221 | 0.086219 | 0.086217 | 0.086212
Dijkstra | 0.15584 | 0.17666 | 0.21104 | 0.27778 | 0.35303
FFT | 0.38613 | 0.38901 | 0.38064 | 0.34336 | 0.3426
iFFT | 0.38605 | 0.38894 | 0.38058 | 0.3433 | 0.34255
Patricia | 0.46512 | 0.44553 | 0.41801 | 0.3996 | 0.38041
SHA | 0.083325 | 0.08164 | 0.078507 | 0.072931 | 0.063694
String Search | 0.15006 | 0.13099 | 0.10428 | 0.073664 | 0.045814
Susan Corner | 0.12723 | 0.12866 | 0.12826 | 0.1424 | 0.1399
Susan Edge | 0.12127 | 0.12406 | 0.12191 | 0.13336 | 0.137
Susan Smoothing | 0.10705 | 0.10625 | 0.098336 | 0.11835 | 0.118
Typeset | 0.21686 | 0.20453 | 0.19335 | 0.18715 | 0.18356

## Slide 31: The Objective of My Work
Main Memory
SPM
shared data
stack
heap
ASAP2011
DAC2013
ASAP2016
CODES+ISSS 2010
DATE 2013
VLSID2016
SPM
Core 2
Develop techniques for managing data on SPM
  Not profile-driven
  Manage different types of application data efficiently
code
ASAP 2010
CODES+ISSS 2013
RTAS 2014
ICCAD 2016
DATE 2016
Core 1
shared data
stack
heap
code
Task 1: Code Management
Task 2: Stack data Management
Task 3: Managing code, stack and global data on SPM+Cache System

## Slide 32: Summary
SPM is capable of delivering good performance, but requiring efficient data management on software
Each type of data has its unique character, therefore we developed different techniques to manage different type of data
  Code
  Stack
  Heap
Our techniques reduce overhead and improves performance significantly, compared to the previous SPM management approaches

## Slide 33: My Publications
Book Chapters
  [Springer 2017] Aviral Shrivastava, and Jian Cai, “Hardware-Aware Compilation”, Handbook of Hardware/Software Codesign, 2017
Conference Publications
  [DATE 2017] Jian Cai, Yooseong Kim, Youngbin Kim, Aviral Shrivastava, and Kyoungwoo Lee, “Reducing Code Management Overhead in Software-Managed Multicores”
  [ASAP 2016] Jian Cai, and Aviral Shrivastava, “Efficient Pointer Management of Stack Data for Software Managed Multicores”
  [VLSID 2016] Jian Cai, and Aviral Shrivastava, “Software Coherence Management on Non-Coherent Cache Multi-cores”, in Proceedings of VLSID, 2016
  [ICCAD 2016] Youngbin Kim, Jian Cai, Yooseong Kim, Kyoungwoo Lee, and Aviral Shrivastava, “Splitting Functions in Code Management on Scratchpad Memories”
  [RTAS 2014] Yooseong Kim, David Broman, Jian Cai, and Aviral Shrivastava, "WCET-Aware Dynamic Code Management on Scratchpads for Software-Managed Multicores”
  [DATE 2018] , Jinn-Pean Lin, Jian Cai, Jing Lu, and Aviral Shrivastava, "Optimizing Heap Data Management on Software Managed Manycore Architectures” (Under review)
Journals
  [IET Computers & Digital Techniques 2016] Aviral Shrivastava, Nikil Dutt, Jian Cai, Majid Shoushtari, Bryan Donyanavard, and Hossein Tajik, “Automatic Management of Software Programmable Memories in Manycore Architectures”
Workshop
  [ESLsyn 2013] David Broman, Michael Zimmer, Yooseong Kim, Hokeun Kim, Jian Cai, Aviral Shrivastava, Stephen A. Edwards, and Edward A. Lee, "Precision Timed Infrastructure: Design Challenges”

## Slide 34: Backup slides

## Slide 35: Limitation
Code
  Cannot handle function pointers
Stack
  Cannot handle complicated pointer operations, such as pointer arithmetic after casting pointers to integer types
Heap
  Alias analysis is not sophisticated enough to handle more complex aliasing, such as pointers in structures

## Slide 36: Code Management

## Slide 37: Reduce Computation Overhead
Inserting management functions everywhere is costly, even when SPM size is larger than code size
Chart: Normalized Dynamic Instruction Counts
| dijkstra | stringsearch | rijndael.enc | rijndael.dec | sha | IFFT | FFT | basicmath | adpcm.dec | adpcm.enc | AVERAGE
Original program without code mangement | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Management overhead | 0.64415 | 0.29335 | 0.33664 | 0.27636 | 0.48505 | 0.10207 | 0.06223 | 0.039169 | 0.0061435 | 0.004659 | 0.22498

## Slide 38: Experimental Setup
LLVM
  Inserts code management instructions
Gem5
  CPU
    X86 ISA
    frequency = 1.2 GHz
  L1 Instruction Cache [1]
    Direct-mapped
    32B cache lines
    The rest memory accesses are all assumed to be hits
  DMA [2]
    cost = startup cost + size / transfer rate
      startup cost = 150 ns (180 cycles)
      transfer rate = 12800 MB/s (10.67 B/cycle)
[1] Texas Instrument., C66x DSP Cache User's Guide
[2] Texas Instrument., Throughput Performance Guide for KeyStone II Devices

## Slide 39: Comparison with Caches
Normalized to the execution time of caching
SRAM size is the smallest power of 2 that is equal or greater than the 50% of code size
Chart: Normalized Execution Time
| adpcm.decode | adpcm.encode | basicmath | CRC32 | dijkstra | FFT | IFFT | patricia | rijndael.decode | rijndael.encode | sha | stringsearch | susan.corners | susan.edges | susan.smoothing | average
 | 0.99994 | 0.99995 | 0.99688 | 0.99991 | 1 | 0.98778 | 0.99056 | 1.0796 | 0.99799 | 0.99804 | 0.99973 | 0.90883 | 0.97283 | 0.97098 | 0.99954 | 0.99351

## Slide 40: Management Overhead
 |  | cache |  |  | spm |  |  |  | 
benchmark | isram size | #insts | #imisses | imiss rate | #insts | #dma | #bytes | #cget | #ccall
adpcm.decode | 512 | 31523645 | 13 | 0 | 31523885 | 2 | 438 | 2 | 0
adpcm.encode | 512 | 41569033 | 16 | 0 | 41569273 | 2 | 532 | 2 | 0
basicmath | 2048 | 3166915 | 60 | 0.000013 | 3167274 | 3 | 1902 | 3 | 1
CRC32 | 512 | 13688720 | 10 | 0.000001 | 13688960 | 2 | 326 | 2 | 0
dijkstra | 1024 | 33744143 | 27 | 0.000001 | 33748756 | 6 | 925 | 82 | 60
FFT | 4096 | 2065101 | 60 | 0.000022 | 2049453 | 6 | 2433 | 6 | 4
IFFT | 4096 | 4485846 | 64 | 0.000011 | 4453814 | 6 | 2433 | 6 | 4
patricia | 2048 | 4026447 | 38 | 0.000008 | 4353618 | 5 | 1595 | 12242 | 900
rijndael.decode | 8192 | 18284483 | 211 | 0.000007 | 18284979 | 4 | 7196 | 4 | 3
rijndael.encode | 8192 | 16802821 | 192 | 0.000008 | 16803469 | 5 | 6952 | 6 | 4
sha | 1024 | 7093878 | 45 | 0.000005 | 7098589 | 8 | 1623 | 86 | 6
stringsearch | 512 | 19034 | 16 | 0.000752 | 19376 | 3 | 514 | 3 | 0
susan.corners | 8192 | 1083565 | 181 | 0.000115 | 1084561 | 7 | 6085 | 7 | 6
susan.edges | 16384 | 2049574 | 355 | 0.000123 | 2050705 | 8 | 12060 | 8 | 7
susan.smoothing | 4096 | 23934483 | 74 | 0.000002 | 23935469 | 7 | 3432 | 7 | 6

## Slide 41: Stack Management

## Slide 42: Experimental Setup
LLVM
  Inserts heap management instructions at IR
Gem5
  CPU
    X86 ISA
    frequency = 1.2 GHz
  L1 Data Cache [1]
    Two-way set associative
    64B cache lines
    The rest memory accesses are all assumed to be hits
  DMA [2]
    cost = startup cost + size / transfer rate
      startup cost = 150 ns (180 cycles)
      transfer rate = 12800 MB/s (10.67 B/cycle)
[1] Texas Instrument., C66x DSP Cache User's Guide
[2] Texas Instrument., Throughput Performance Guide for KeyStone II Devices

## Slide 43: Comparison with Caches
Normalized to the execution time of caching
SRAM size is the smallest power of 2 that is equal or greater than the 50% of stack size
Execution time 7% longer on average
Chart: 
| adpcm.decode | adpcm.encode | basicmath | CRC32 | dijkstra | FFT | IFFT | patricia | rijndael.decode | rijndael.encode | sha | stringsearch | susan.corners | susan.edges | susan.smoothing | average
 | 1.0435 | 1.033 | 1.0234 | 0.99996 | 1.0074 | 1.0352 | 1.0199 | 1.2716 | 0.987 | 1.0636 | 0.99329 | 1.5603 | 1.0125 | 1.009 | 1.0102 | 1.0713

## Slide 44: Heap Management

## Slide 45: Heap Management is Important
Chart: Percentage of Heap Accesses
| ADPCM Dec. | ADPCM Enc. | Dijkstra | FFT | iFFT | Patricia | SHA | String Search | Susan Corner | Susan Edge | Susan Smoothing | Average
 | 0 | 0 | 0.17039 | 0.65864 | 0.67602 | 0.42596 | 0 | 0 | 0.42129 | 0.57251 | 0.94045 | 0.35139
Heap accesses may account for a significant portion of overall memory accesses

## Slide 46: Reduced Instruction Count
Chart: A: Statically Detect Heap Access B: Simplifying Management Framework C: Inlining and Combining Management Calls
| ADPCM Dec. | ADPCM Enc. | Dijkstra | FFT | iFFT | Patricia | SHA | String Search | Susan Corner | Susan Edge | Susan Smoothing | Typeset | Average | Benchmarks
A | 0.098603 | 0.08622 | 0.53843 | 0.74579 | 0.74577 | 0.74232 | 0.083329 | 0.15001 | 0.56976 | 0.58037 | 0.44037 | 0.28465 | 0.42214
A+B | 0.098603 | 0.086221 | 0.22999 | 0.48024 | 0.48016 | 0.51514 | 0.083325 | 0.15006 | 0.22954 | 0.2223 | 0.17368 | 0.22115 | 0.24753
A+B+C | 0.098603 | 0.086221 | 0.15441 | 0.38362 | 0.38354 | 0.46462 | 0.083325 | 0.15006 | 0.12712 | 0.12115 | 0.1069 | 0.21683 | 0.19803
Normalized to dynamic instruction count of the state of the art