## Slide 1: Scalable Register File Architectures for CGRA Accelerators
Shail Dave
Compiler Microarchitecture Lab
Arizona State University
http://aviral.lab.asu.edu/cgra/

## Slide 2: Need for Power-Efficient Acceleration
Ubiquitous problem of computing
  Required power-efficiency cannot be provided by multicores alone.
  Need some form acceleration.
Possible Alternatives
  ASICs – Poor usability
  FPGAs – Reconfigurable but, less power efficient (fine-grained)
  SIMDs/Vector Processors - Hard to program. Inefficient if parallelism is irregular
  GPUs – Popular. Unable to accelerate loops that {are non-parallel, incurs conditionals, have low trip-counts}
Need a technology that can achieve more acceleration with much higher power-efficiency!

## Slide 3: CGRAs: A Promising Technology
Coarse Grained Reconfigurable Array (CGRA) is array of Processing Elements (PEs). Each PE has a functional unit that works on an operation on every cycle.
4x4 CGRA with local RF and 2-D mesh interconnect. PE computes fixed point logic.
Array configurations very in terms of –
  Array Size
  Functional Units
  Interconnection N/w
  Register File Architectures
Quick Facts
  Can achieve power-efficiency of several 10s of GOPS/sec per watt!
  Popular in Embedded Systems and Multimedia. (Samsung SRP processor)
Notes: Recent works* also demonstrate that CGRAs are 2x more energy-efficient than SIMDs for imaging applications; FPGA takes 1.4 times more energy than CGRAs.
*Vasilyev et al., MICRO 2016 (Stanford)

## Slide 4: Mapping Applications On CGRAs
for (i=2; i<1000; i++) {
A[i] = B[i-2] – 4;
B[i] = A[i] + 5;
C[i] = B[i] * 3;
}
a Critical Loop
1x2 CGRA with local rotating RF (1 register, depth = 2)
Data Dependency Graph
b
c
2
a
a:
b:
c:
R
1
R
R
2
R
Compiler Provides Mapping of DDG to CGRA
Rotating RF employs shift registers, Values are shifted at some cycles.
A[i] = B[i-2] – 4;
B[i] = A[i] + 5;
C[i] = B[i] * 3;
Notes: - RFs are rotating and with a depth.

## Slide 5: Mapping Applications On CGRAs
b
b
b
Data Dependency Graph
II = 2
time
0
1
2
3
Software Pipelining– Array can execute operations from two iterations simultaneously. This empowers to accelerate even non-parallel loops through the CGRAs.
Initiation Interval aka II is performance metric.
b
c
2
a
a
i = 2
b
a
i = 3
b
4
b
c
i = 4
a
Registers are rotated at every 2 cycles.
Let’s assume that B[1000] = {2, 4, -3, 29, …..}
R
1
R
R
2
R
A[2] will use B[0] = 2 (initial)
A[3] will need B[1] = 4 (initial)
A[4] gets prior computed B[2]
c
b
b
Iterative Modulo Scheduling – Every operation is executed at II cycles.

## Slide 6: Not All Variables are Recurring
Recurring (Repeatedly Written and Read)
  Generated during kernel execution (for intermediate use)
  Stored in the rotating registers.
Nonrecurring
  Constants in program (e.g., base address of an array)
  Immediate (constants in instructions) CGRA instructions has to deal with more fields and complexity, meaning immediate bits can be about 10 bits.
for(i=0; i < 1000; i++) { sum += series[i]; count += 1; 16bitLSB = sum & a;
}
recurring
immediate
constant

## Slide 7: Why I Cannot Store Constants in Rotating RF?
If the constants are stored into rotating RF, they must undergo rotation.
So, incorrect values can be accessed or values can be easily overwritten. This results into incorrect output!!!
const
Read constant from index 0
RF is rotated at each II cycles.
After rotation at II cycles
const
Rotating RF

## Slide 8
How to manage both recurring and non-recurring variables in an efficient and scalable manner?

## Slide 9: Prior Approaches
Recurring variables (repeatedly read and written) are frequently accessed. Hence, are stored into local rotating RF.
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Local Data Memory
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Global RF
Nonrecurring variables (constants) can be accessed via –
  1) On-Chip Memory 2) Global Register File

## Slide 10: Limitations of Using Memory for Constants
Although simple, accessing on-chip memory results in extra load operations, which reduces potential performance because-
Few works* considered issue of increased pressure on memory.
  Solution? Use registers of global RF.
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Local Data Memory
  In most of CGRAs, only few PEs (green) can perform memory operation.
  Often the load/store bandwidth is limited in CGRAs.
Can do Memory Operation
* Park et al., PACT 2008 & LCTES 2009 (Univ. of Michigan)

## Slide 11: Limitations of Using Global RF for Constants
A CGRA with Global RF
Global RF may not Scale; Degrades Performance
  Prior RF explorations* demonstrated need of connecting as much as PEs to global RF. However, it is also shown and evident that increasing R/W ports to connect more PEs can certainly degrade performance.
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Global RF
Increases Instruction Width
  Example: Need about 64 registers for a 4x4 CGRA
  Each PE need 6 bits; PE has two inputs from RF, and an output to be written to RF. We need 18 (3*6) bits just to access global RF, in 32-bit instruction.
  Increasing ISA width results in increased memory bus width and consequently, increase in area and power.
1
2
3
A PE with a RF
* Kwok et al., FCCM 2005 (Univ. of British Columbia)

## Slide 12: Local Unified RF: A SW/HW Hybrid Approach
Local
  Not global/within each PE
  Better Performance, Scalable
Unified
  Will manage both recurring and non-recurring variables in the RF
  Each PE has flexibility to use different number of rotating and nonrotating registers, for each loop!)
Hybrid
  Software/Hardware mixed approach to manage the register lookup
Local Unified RF
PE
Constant (Nonrotating Section)
sum0
sum1
totalCount
Recurring Values (Rotating Section)

## Slide 13: Modulo Addition Based Indexing for Rotating RF
Example: We need to store loop-carried values of variable d across four different iterations.
32
Iteration 0
0
Ri = 0
d0
Virtual Register Index
32
0
d0
1
d1
Iteration 1
1
d1
2
Iteration 2
d2
2
d2
3
Iteration 3
d3
3
d3
Regular or Nonrotating Register File
4
0
d4
Iteration 4
d4
(Log4) = 2 bit adder for modulo operation
Modulo 4 Results Into Register 0
Overflow from addition results in modulo operation!
We need to still merge registers for constants!
Example: We need to store loop-carried values of variable d across four different iterations. We can do so by implementing rotation through modulo addition based indexing.

## Slide 14: Unified RF and Its Configuration
32
Compiler generates value ‘c’ to configure the boundary
‘c’ is max. register index inside rotating section.
Example: RF size = 6, c =3 (4 rotating registers)
Generate s = 1
Case 2: Reg index = 0 Iteration = 4
Generate s = 0
Case 1: Reg index = 5
5
c = 3
0
4
4
3
0

## Slide 15: Key Contributions
Proposal of Local Unified RF as an efficient and scalable solution
Compiler management of unified RF
  Register calculations/reservations
  Generation of configuration boundary
  Integration with any CGRA compiler technique

## Slide 16: What a Compiler Must Do?
For each operation being mapped on a PE, calculate and reserve –
  Nonrotating registers required (based on constant predecessor or live-in data)
  Rotating registers required (based on the dependency with successor node)
  Maintain the configuration boundary to separate rotating and nonrotating section of RF.
Recurring Values (Rotating Section)
Constants (Nonrotating Section)
Unified RF
Pre-load the constants into nonrotating registers of the RF
Produce final configuration boundary for each PEs
If PE does not have enough registers, it should try other PEs or increase II. (Integration of solution with a mapping technique enables such flow.)
Pre-Load
boundary

## Slide 17: SW Management of Unified RF

## Slide 18: Integration with a Mapping Technique
Generate Configurations
Mapping Succeeded
Yes
Map All Nodes
Mapping
Input Data Dependency Graph
Generate Edge Set/Clusters/Cliques
II ← MII
Calculate Costs/Reserve Resources
II > Total Attempts?
II ← II + 1
Mapping Failed
Yes
No
Retry
Initialization
No
No
Select Target Node & PE
All Nodes Mapped?
Reserve Registers
Success?
Update Costs/Resources
Another PE Available?
No
Yes
Yes
Success?
Yes
No
No

## Slide 19: Experimental Setup
Compiler
  LLVM v3.6
Mapping Technique
  Register-Aware Mapping (REGIMap)
Validation
  Gem5 processor simulator
Benchmarks
  MiBench (Important, Performance-critical kernels)
RTL Validations
  32 nm (Cadence Library)
  PrimeTime (power)
Baseline
  4x4 Homogeneous CGRA
  Operation Latency: 1 cycle
  Memory bus is shared with each row of array
  On-chip Memory (4 kB)

## Slide 20: Experiments
Accessing constants from memory, local rotating RF for recurring values
  Comparing performance (in terms of mapping, number of cycles required)
Accessing constants from global RF, local rotating RF for recurring values
  Global RF can certainly be beneficial in terms of sharing same data to multiple PEs and avoiding data duplication. However, local RF can provide performance at par of global RF.
  Hence, comparison is made on basis of a cycle time (scalability).

## Slide 21: Unified RF Performs Better than On-chip Memory
Chart: Initiation Interval (II)
| ghostscript | gsm | jpeg | mad | pgp | rijndael | rsynth | sha | sphinx | stringsearch | susan | typeset | Average
Local Unified RF | 2 | 3 | 4 | 2 | 3 | 3 | 3 | 3 | 2 | 3 | 3 | 2 | 2.75
Constant Memory | 2 | 5 | 5 | 2 | 3 | 3 | 5 | 4 | 2 | 3 | 4 | 2 | 3.3333
Lower the better
18%

## Slide 22: Unified RF Reduces Mapped Nodes By 22.4%
Chart: Nodes To Be Mapped
| ghostscript | gsm | jpeg | mad | pgp | rijndael | rsynth | sha | sphinx | stringsearch | susan | typeset | Average
Local Unified RF | 14 | 22 | 30 | 17 | 15 | 14 | 32 | 27 | 17 | 19 | 28 | 11 | 20.5
Constant Memory | 19 | 30 | 37 | 20 | 17 | 18 | 42 | 43 | 19 | 23 | 34 | 15 | 26.4167
Proposed approach reduces memory accesses!
Notes: (it’s all about extra loads)

## Slide 23: Local Unified RF Scales Better than Global RF
Chart: CGRA Size
| 4x4 | 8x8 | 16x16 | 32x32
CGRA with Local RF | 1085 | 1095 | 1160 | 1200
CGRA with Global RF | 1300 | 1320 | 1380 | 1500
CGRA with Local Unified RF
Notes: RTL validation achieves about 30 GOPS per sec per watt. 17.38% better cycle time

## Slide 24: RF Configuration Improves Register Utilization than Separate RFs for Recurring Values and Constants
Chart: Number of Registers
| ghostscript | gsm | jpeg | mad | pgp | rijndael | rsynth | sha | sphinx | stringsearch | susan | typeset | Average
Unified RF | 5 | 3 | 2 | 5 | 2 | 3 | 3 | 5 | 4 | 2 | 4 | 1 | 3.25
Separate RFs with Fixed Hardware | 5 | 3 | 4 | 5 | 3 | 3 | 3 | 5 | 5 | 3 | 6 | 1 | 3.8333
~ 3
~ 4

## Slide 25: Summary
Advocated for a scalable solution of local unified RF.
  Improves performance, compared to accessing on-chip memory.
  Also scales better than global RF.
Managed all variables in a single register file; Compiler tackles the complexity -
  Determines register requirements, allocate registers, and configures the boundary of the unified RF, which results in the effective register utilization.
  Preloads the constants into RF
  Can be integrated with any mapping technique.

## Slide 26: Thank you !

## Slide 27
FAQ

## Slide 28
Q: Why I cannot completely manage register rotation/indexing in software?
A:
Yes, it can be definitely managed. However, to do so, you need to access different register index due to loop carried dependence or software pipelining. This means that if there is a loop-carried dependence of 5 or 10, you need to have kernel enrolled for 5 iterations.
This implies that for a 8x8 CGRA, now 5 times more instructions should be generated and provided for each PE, means instruction memory size should increase by 5X, meaning increased area and power.
So, there is a design trade-off, depending on applications. Here, proposed solution is very general, targeting management of both variables in a single register file and proposed compiler solution does that successfully.

## Slide 29
Q: Why it is hybrid approach (HW role vs. software role)
A:
Hardware manages both the variables (recurring values and constants) in a single regular register file. To do so, it adopts modulo addition based indexing to correctly access recurring values. Hardware has flexibility through configuration to access different number of registers in both – rotating and nonrotating sections.
Compiler tackles all sort of complexity to generate such configuration for hardware, depending on the applications. It efficiently allocates registers and also preloads the constants in the prologue. Proposed software approach is generic for any CGRAs and can be well integrated with any CGRA mapping technique.

## Slide 30
Q: What are the limitations of your work?
A:
Work faces few limitations -
1) due to incorporation of modulo based indexing
  Modulo addition based indexing requires the number of rotating registers (to store recurring values) must be some power of 2 and it is trade-off between simple hardware design vs. modulo 2 operation. This work targets managing both the variables and so has to adopt such indexing mechanism.
2) CGRA compilers cannot break down register requirements
  CGRA compilers can map an operation only if a processing element (PE) can accommodate register requirement in register file. This is also applicable to this work.

## Slide 31
Q: Future Work
A:
1) Register allocations in case of different RF structures for CGRAs
  CGRA design can choose to have both local and global RF. In such case, registers should be allocated in which register file first, by the compiler? Such decisions can affect the design cost and the performance, leaving a room for such optimizations. Well designed scheme can achieve better management and power-efficient acceleration.
2) CGRA compilers cannot break down register requirements
  CGRA compilers can map an operation only if a processing element (PE) can accommodate register requirement in register file. Hence, approach of breaking down register requirements and distributing allocations through multiple RF can certainly be a good optimization.

## Slide 32
Q: Why not compare against shift registers?
A: Firstly, NO Prior Works Can Manage BOTH recurring values and constants altogether.
Implementing rotation through modulo based indexing is intuitive and well adopted now-a-days by in place of shift registers, by CGRA chip designers and few other research groups*. Still, they cannot manage both variables together. In case of global RF, RTL results already show that cycle time increases in case of using global RF. So, certainly local unified RF is a better choice.
Accessing memory increases load operations, degrades performance (with much higher cycles; generates bus contention) and again not the best approach. (Imagine 18% extra cycles or 18*II extra cycles). * essen et. al , FPL 2010 (Univ. of Washington), Mei et al. (Springer)
Notes: It incurs little higher area (12%) but better energy savings (34%)

## Slide 33
Q: How this work is different than prior works on RFs or RF explorations?
A: Prior works have been RF explorations, where they do not compare on basis of scalability. Mainly, they do not provide information on how register management can be done at compiler level.
Scalability experiment and comparison with prior approaches make this work unique to establish as an efficient solution. Besides, whole idea is based on transferring the complexity at compiler level to correctly calculate and allocate registers needed. It also provides correct configuration to hardware for flexibly allocate different registers for both variables, depending on application kernel. Finally, the proposed software approach can be well integrated with any CGRA mapping technique.