## Slide 1: UnSync: A Soft Error Resilient Redundant Multicore Architecture
Reiley Jeyapaul1, Fei Hong1, Abhishek Rhisheekesan1,
Aviral Shrivastava1, Kyoungwoo Lee2
1Compiler Microarchitecture Lab,
Arizona State University, Tempe, Arizona, USA
2Dependable Computing Lab,
Yonsei University, Seoul, South Korea

## Slide 2: Scaling Drives Technology Advancement
Scaling: The Transistor Gate
shrinks in size every year
Smaller device dimensions improve on performance and reduce power consumption

## Slide 3: Reliability - a consequence: Transient Faults induce Soft Errors
Electrical disturbances can disrupt the operation causing Transient Faults

## Slide 4
Charge carrying particles induce Soft Errors
  Alpha particles
  Neutrons
    High energy (100KeV -1GeV)
    Low energy (10meV – 1eV)
Soft Error Rate
  Is now 1 per year
  Exponentially increases with technology scaling
  Projected1 per day in a decade
Soft Errors - an Increasing Concern with Technology Scaling
Toyota Prius: SEUs blamed as the probable cause for
unintended acceleration.
Performance is useless if not correct !

## Slide 5: Chip Multi-Processors and Redundancy
CMPs : Good candidates for redundancy based techniques
  Cores and hardware, available for use with low performance impact
  Redundancy can be implemented at larger granularity
  Effective performance overhead can be reduced
Popular redundancy based techniques:
  Triple Modular Redundancy – error in data is voted out
  Dual Modular Redundancy – detection by comparing two identical executions
  Checkpointing – check execution at regular intervals and save state for recovery (when error is detected)
Tilera
TILE64
ARM11 MPCore

## Slide 6: Soft Error Resilience in Chip Multi-Processors
Cost of redundancy based soft error resilience is high
  Redundancy reduces performance by 50%
    Cannot afford more loss
  Hardware overhead is amplified with core count
  Inter-core communication overhead is amplified with scaling
  Power cost per effective computation ratio is low
    Cannot afford increased power overhead (hardware or software)
Requirements for efficient error resilience in CMPs
  Effective Performance ~ 50%
  Low hardware overhead
  Low inter-core communication overhead
  Smart use of available power efficient resources (hardware or software)
Tilera
TILE64
ARM11 MPCore

## Slide 7: Relevant Previous Work
Checkpointing
  At periodic intervals, perform system integrity check
  Store architectural state at this point = checkpoint
  If error detected, recover from previous checkpoint
  Checking requires synchronization
  Storage of architecture state requires hardware
Lock-step [Meaney2005]
  Redundant executions compared to detect errors
  Observe identical cache accesses, and interrupts
  100% penalty in performance and hardware
Redundant Multi-Threading [Reinhardt2000]
  SMT architecture where store and load values are checked
  Load Value Queue (LVQ) for consistent replication
  Inter-thread synchronization, and performance overheads

## Slide 8: State-of-the-art Soft Error Resilient Redundant Multicore Architecture
Error Detection and Recovery:
Reunion [Smolens2006]
  Physically tagged vocal and mute cores executing redundantly
  Fingerprint (hash of instructions and output) compared before commit
  Instruction + output buffered till fingerprints compared on both cores
  Execution state check-pointed, on every fingerprint comparison
  Hardware overheads and inter-core synchronization penalty
Mute Core
L1
Vocal Core
L1
Shared L2
For fingerprint transfer
ECC
protected
ECC
protected

## Slide 9: UnSync Architecture Construction
Core 1
(a)
L1
Core 2
(b)
L1
L2 Cache
(ECC Protected)
Redundant Cores:
- identical architecture
- execute same thread
Communication Buffer:
- ECC protected
a b
Communication
Buffer (CB)
Multi-Core Architecture:
- private L1 cache
- shared L2 cache
- independent memory bus
Existing memory bus is bypassed when executing redundantly

## Slide 10: UnSync Architecture Working: Error-free execution
Core 1
(a)
L1
Core 2
(b)
L1
a b
L2 Cache
(ECC Protected)
L1-L2 data writeback:
to respective
CB sections
cache-line address compared:
to ensure completion on both cores
One cache-line written to L2:
Data written is guaranteed correct
Identical cores execute the same thread

## Slide 11: Communication Buffer: Working
Core 1
L1
Core 2
L1
OX0001 D1
OX0002 D2
OX0001 D1
OX0003 D3
OX0001 D1
Shared L2
Instruction completed execution on both cores
OX0003 D3
Faster core
Slower core
Commit: OX0001 D1
Wait for “OX0002” to execute in core 2

## Slide 12: UnSync Architecture Working: Error-detection
Core 1
(a)
L1
Core 2
(b)
L1
a b
L2 Cache
(ECC Protected)
Power efficient hardware-only error detection
EIH
Error detected in a core is reported to the
Error Interrupt Handler (EIH)
DMR
- Program counter
- Pipeline register
1-bit Parity
- L1 cache
- Register file
- Queuing structures
RECOVERY
EIH
UnSync feature:
Hardware based error-detection and handling eliminates the need for inter-core communication
a

## Slide 13: UnSync Architecture Working: “Always forward execution” Recovery
Core execution and L1-L2 traffic are STOPPED
Core 1
(a)
L1
Core 2
(b)
L1
a b
L2 Cache
(ECC Protected)
EIH
fault in a
fault in b
Architectural state of correct core copied over faulty core
CB content of one core copied over the other
After Recovery:
Both cores resume execution
from PC of correct core
Re-execution (if any) occurs only
in faulty core

## Slide 14: Salient Features of UnSync
Power-efficient error detection in Hardware
Parity for detection in cache, instead of ECC for correction
Detection techniques (DMR, TMR) with reduced hardware
Eliminates the need for inter-core communication
No Inter-Core Synchronization
Detection does not require data comparison between cores
CB at L1-L2 interface, prevents error leakage into memory
Commit only one copy of data to memory, ensure data consistency
Always Forward Execution (After Recovery)
Both cores resume execution from PC of correct core
Repeat execution after recovery, if correct core was faulty
Correct core execution pattern is not disturbed.

## Slide 15: Experimental Setup: H/w Synthesis
Compare and contrast area and power of single core
  RTL of the MIPS processor is implemented
  Synthesize at 300MHz, 65nm using Cadence Encounter
  Perform place-and-route (PNR) to incorporate datapaths
  For cache power we use CACTI cache simulator.
Hardware components added for Reunion
  fingerprint size = 16bits
  fingerprint interval = 10 instructions
  CHECK stage buffer = 17 entries (each of 66 bits)
Hardware components added for UnSync
  L1 cache is write-through
  Communication buffer = 10 entries

## Slide 16: UnSync : Low Power Overhead
Increased power consumption in Reunion
  Large storage buffers within the core
  Fingerprint generation on every cycle
  CHECK stage to perform inter-core fingerprint comparisons
  SECDED on L1 Cache
Power overhead in UnSync by error detection blocks
  can be reduced by advanced power-efficient methods

## Slide 17: UnSync : Low Area Overhead
UnSync Hardware added
  Error detection components
    1-bit parity (L1 cache, RF, Queues)
    DMR (PC, pipeline registers)
  ECC protected Communication buffer

## Slide 18: Experimental Setup: Simulation
Cycle-accurate M5 simulator with the above configuration.

## Slide 19: Salient Features of UnSync
Power-efficient error detection in Hardware
Parity for detection in cache, instead of ECC for correction
Detection techniques (DMR, TMR) with reduced hardware
Eliminates the need for inter-core communication
No Inter-Core Synchronization
Detection does not require data comparison between cores
CB at L1-L2 interface, prevents error leakage into memory
Commit only one copy of data to memory, ensure data consistency
Always Forward Execution (After Recovery)
Both cores resume execution from PC of correct core
Repeat execution after recovery, if correct core was faulty
Correct core execution pattern is not disturbed.

## Slide 20: Synchronization Affects Performance
Vocal Core
Mute Core
Fingerprint comparison and memory synchronization
Reunion
Core 2
Core 1
UnSync
No Synchronization  Improved Performance

## Slide 21: Improved Performance Without Synchronization

## Slide 22: Larger CB removes resource occupancy bottleneck

## Slide 23: Limitations
If a SEU manifests into error on both cores simultaneously, execution cannot be recovered
  Hardware based interrupt handling provide immediate recovery activation
If error is detected in a register file when copying from correct (during recovery)
  Execution cannot be recovered
  Probability of such undetected errors in RF is very low
Recovery subroutine will use the shared L2 to transfer architectural state (RF+ PC) from correct core to erroneous core.

## Slide 24: Summary
Soft Errors are soon to become a major concern even in terrestrial computing systems
CMPs are good candidates for redundancy based methods for soft error resilience
UnSync is an efficient, soft error resilient CMP architecture
  Power efficient hardware based detection reduces overheads
    13.32% reduced area, 34.5% less power consumption
  Always forward execution based recovery improves performance
    20% improved performance over Reunion
  Larger Region of Error Coverage improving reliability of core
Architecture framework allows for possible customization
  Achieve varied degrees of redundancy/resilience tradeoffs

## Slide 25: Thank you !