## Slide 1: WCET-Aware Dynamic Code Management on Scratchpads for Software-Managed Multicores
Yooseong Kim1,2, David Broman2,3, Jian Cai1, Aviral Shrivastava1,2
1Arizona State University
2University of California, Berkeley
3Linköping University

## Slide 2: Timing is important
Timing constraints – meet the deadline!
For absolute timing guarantees,
  System-level timing analysis
  Worst-Case Execution Time (WCET) analysis for individual tasks
Reducing the WCET can help meet deadlines
τ1
τ3
τ2
0
D
time
τ1
τ2
τ3
This work is about analyzing and optimizing the WCET of a program
Notes: I guess everyone in this room know that timing is important in real-time systems. It is important because they have timing constraints, so the timing is a correctness factor, and not just a performance factor. Because deadlines are so important, people do system-level timing analysis where they check all deadlines are met in the whole application. This involves calculating safe upper bounds of execution times of individual task, which is called WCET analysis.
Also if we can reduce the WCETs of tasks, we can make more tasks to meet their deadlines.
So, it is important to be able to analyze the WCETs of tasks and to be able to reduce them, and this work is about analysis and software optimization for WCET of a task running on an architecture equipped with … scratchpads!

## Slide 3: Software-Managed Multicores (SMM)
SPM
Core
DMA
Main Memory
No direct access to main memory
  All code and data must be loaded into SPM at the time of execution
Isolation among cores – good for real-time systems
ex. IBM Cell BE
SPM
Core
SPM
Core
SPM
Core
Main Memory
SPM
Core
DMA
DMA
DMA
DMA
Software-Managed Multicores cannot directly access main memory
Notes: This is out target architecture, called software-managed multicores. This architecture uses SPMs instead of caches.
What’s unique about this is that the cores can only access the SPMs and cannot directly access main memory. So, if the program needs to access anything from the main memory, it needs to bring it into the SPM by DMA operations.
Except for the accesses to the main memory, cores are completely isolated unless they are communicating each other. So, this kind of architecture can be a good alternative to cache coherent multicores in real-time applications, if we assign each task to a core. IBM Cell processor is a good example of SMM architecture. From now on in this talk, we will call this kind of architectures SMMs.

## Slide 4: SPM Management: Static vs. Dynamic
Static management
  Load data only at loading time
  Good: When everything fits in the scratchpad
  Bad: When it doesn’t. – limited locality
Dynamic management
  Bring data in and out in runtime
  by DMA operations
  DMA transfers take time
Main
Memory
SPM
0x0
0xFFFFFFFF
0x0
0xFFFFF
Dynamic management involves DMA transfers
We try to minimize the impact of DMA transfers on the WCET
Notes: In general, there are two ways of using scratchpads. Static management and dynamic management.
Using a scratchpad involves creating a mapping between main memory addresses and scratchpad addresses. After we bring something into the SPM, we will keep accessing it using its SPM address, but its actual identity is determined by its global address. In static management, this mapping is created at loading time, and does not change.
This means that we use this fast on-chip memory for only those things that we bring at loading time. This is good when everything fits in the SPM. We can load the entire program and data into the SPM, and execute from the SPM. But when it doesn’t, some things have to be accessed from this slow main memory. At this point, dynamic management comes into the picture. In dynamic management, we bring data in and out in runtime by DMA operations.

## Slide 5: Dynamic Management on Traditional Setups vs. SMMs
Traditional architectures with scratchpads
  To exploit more locality
  It’s for optimization
SPM
Core
DMA
Main Memory
A
B
C
D
Not-frequently accessed
Frequently accessed
SPM
Core
DMA
Main Memory
SMM architectures
  Anything that is accessed must be loaded on the SPM
  It’s a MUST
A
B
C
D
B
D
A
B
C
D
A
B
C
D
time
Dynamic management is essential to execute a program on SMMs
Notes: So, why is dynamic management so good? It’s because we can exploit more amount of locality in a program. Let’s say a task accesses some data, these A, B, C, and D. Unfortunately, this scratchpad is too small to fit all these, so we have to decide which ones we should bring in the scratchpad.
Let’s say B and D are accessed in the loop, so they are frequently accessed. Then, normally in traditional architectures with scratchpads, we will put only those frequently accessed data into the SPM to optimize performance.
But how is it different on SMMs?
Earlier, I said that Software-managed multicores do not have direct access to the main memory. So, everything must be brought into the scratchpad and access from there. This means that dynamic management is a must. Without dynamic management, we can not even execute a program on SMMs.

## Slide 6: Dynamic Code Management
Load program code on demand in runtime
Granularity: basic blocks or functions?
All previous approaches on
optimizing WCET are in basic block-level
  Some basic blocks are left in main memory
  Thus, not applicable to SMMs
Function-level approaches are
applicable to both SMMs and traditional
architectures
v0
v1
v2
v5
v4
v3
f0
f1
f2
f3
All previous techniques on WCET optimizations are not usable on SMMs
whereas our approach is usable on any architecture
Notes: This work is about code management, so we focus on managing program code. Dynamic code management techniques bring program code on demand in runtime, and there are two main streams of research in terms of granularity of management. Basic blocks or functions. All state-of-the-art code management techniques for optimizing WCET are in basic block-level. What they do is to figure out which basic blocks should be loaded in the SPM to optimize the WCET.
Unfortunately, they are not applicable to SMMs, because inherently they leave some basic blocks behind in main memory.
On the other hand, function-level approaches loads the whole function at the time a function is called, so every function that is executed is loaded into the scratchpad. So, function-level approaches are applicable to both traditional architectures and SMMs. In this paper, we use function-level management.

## Slide 7: Function-Level Dynamic Code Management
Load the callee at a call (and the caller at a return)
Function-to-Region Mapping
  M: F  R
  Region
    An abstraction of SPM address space
    Each region represents a unique SPM address range
  The size of a region is the size of the largest function in it
  |R| ≤ |F|
f3
f2
f1
f0
SPM
f2
f1
f3
Functions
Mapping
M(f1) = R1
M(f2) = R2
M(f3) = R3
SPM
R1
R2
R3
This mapping is not feasible!
M(f3) = R2
R1
R2
This mapping is feasible
Function-level management needs a function-to-region mapping
Notes: Function-level dynamic code management techniques load the callee at a call or the caller at a return.
And when loading a function, we need to decide the scratchpad address at which we load the function.
We do it by finding a function-to-region mapping
Region is just another abstraction level we introduce here for scratchpad memory addresses. Each region covers a unique scratchpad address range.
And when the code size is larger than the size of the scratchpad, some functions have to share the same region, so the number of regions is less than or equal to the number of functions. And, the size of a region is the size of the largest function that is mapped to it.
Let’s see an example here.

## Slide 8: Mapping for ACET ≠ Mapping for WCET
f1
IF
f2
f3
Path 1
Path 2
(0.3)
(0.7)
Mapping B
f1,f3
f2
load f2
Path 1
load f3
Path 2
reload f1
R1
R2
10+1=11
6+2+3=11
Path 1
Path 2
10
6
f1
f2
3
1
f3
2
Each path cost
(without DMA)
DMA cost
Mapping A
10+1+3=14
f1,f2
f3
load f3
Path 2
load f2
Path 1
reload f1
R1
R2
6+2=8
A
B
14*0.3 + 8*0.7 = 9.8
11*0.3 + 11*0.7 = 11
max(14,8) = 14
max(11,11) = 11
ACET
WCET
A mapping affects the execution time by changing function reloadings.
In this paper, we find a mapping for WCET.

## Slide 9: Overview of Our Approach
Interference analysis
  What is the worst-case scenario of function reloadings
Integer linear programming (ILP)
  Optimal, but not scalable
A heuristic
  Sub-optimal, but scalable
Notes: So, this is an overview of our approach.
What we just observed is that a mapping affects the number of function reloadings on each path, which in turn affects the WCET.
So we have an algorithm called interference analysis to find out the worst-case scenario of function reloadings. And what I mean by that, I’m going to show you on the next slide.
Using the results of the interference analysis, we formulate an ILP to find out an optimal function-to-region mapping and the WCET of a program using the mapping.
This ILP is good because it can find an optimal solution, but it can take a very long time for a large program.
So we have a heuristic also, which finds sub-optimal solutions but is scalable.
I’m going to give a sketch of each these from now on.

## Slide 10: Notation: func(v) and ccv
f0
f1
…
call f1
…
ret
v0
v1
v3
…
ret
v2
func(v0) = f0
func(v1) = f0
func(v2) = f1
func(v3) = f0
ccv0 = 0
ccv1 = 0
ccv2 = 1
ccv3 = 1
func(v) – function that v belongs to

## Slide 11: Interference Analysis
What causes a function to be reloaded?
  Loading of other functions (in the same region)
IS(v) – the set of all functions that may have been loaded since the last time func(v) was loaded
IS(v3) = {f1}
If f0 and f1 share the same region, f0 could have been evicted by f1
 Assume f0 has to be reloaded
…
call f1
…
ret
v0
v1
v3
…
ret
v2
Using a mapping and interference sets, we can find out the worst-case function reloading scenario
Notes: When do we need to reload a function?
It’s when a function is loaded into the scratchpad before, but then is evicted by loading another function that is mapped to the same region. So, the history of loading functions matters in predicting reloading of functions.
To find this about, we find interference sets, IS(v) at each v, which is the set of all functions that may have been loaded since the last time func(v) is loaded.

## Slide 12: ILP Formulation (1): Finding WCEP
For all (v,w) in E
  Wv ≥ Ww + Cv
  Cv = nv·comp(v) + Lv
WCET from v to the end of the program
Cost of v
Computation cost of v
If a loading occurs at v, Lv is the DMA cost of loading func(v). Otherwise, Lv = 0
Objective function
  minimize Wvs
Function loading cost of v
The source node
: Take the max of the sum of costs of all vertices starting from w on a path
Cv = Computation Cost + Function Loading Cost
The objective is to minimize the sum of Cv’s of vertices on WCEP

## Slide 13: ILP Formulation (2): Function Loading Cost
For all f in F and r in R,
Lv ≥ nv · ccv · if,v · Mfunc(v),f,r · DMAfunc(v)
DMA cost of loading func(v)
1 only when func(v) needs to be reloaded at v
if both f and g are mapped to r
ILP explores all possible mapping choices using Mf,g,r
The minimizing objective function finds the mapping that minimizes function loading cost on WCEP

## Slide 14: Our Heuristic
The number of mapping solutions increases exponentially as the number of functions increases
Search a reasonably-limited solution space instead
  By Merging and Partitioning
  Cost function: The cost of the longest path (WCET)
  Iterative, sub-optimal – No optimal substructure
f0
f1
f2
Merge
Merge
Partition
Partition
Our heuristic finds the best mapping within a limited solution space
iteration 0
iteration 1
iteration 2

## Slide 15: Implementation Overview
Program
Inlined CFG
Generation
Inlined CFG
Interference Analysis
Interference Sets
ILP1
WCET Estimate
ILP Solver
Mapping Solution
DMA Instructions
Insertion
Final
Program
Loop Bounds
SPM Size
Function Size
Heuristic
ILP Generation
ILP2
ILP1 – For finding a mapping
ILP2 – For finding the WCET only

## Slide 16: Experimental Setup
Comparison with three previous mapping techniques
  FMUM & FMUP+, SDRM*
  All optimized for average-case
Benchmarks from MiBench suite and Mälardalen WCET suite
Loop bounds obtained by profiling
Verified by simulation with gem5 simulator
+Jung et al., ASAP, 2010
*Pabalkar et al., HiPC, 2008

## Slide 17: Results: WCET Estimates
The heuristic performs as well as the ILP
Elapsed time
  Heuristic: < 1sec for all benchmarks
  ILP: ~ 100 min for susan, >10 days for adpcm
The solution of the ILP did not improve after a few minutes
  Time-limited ILP (< 20 min.) can also be a heuristic
Due to its call pattern, no reload occurs regardless of a mapping

## Slide 18: Summary
SMMs are a promising architecture for real-time systems
  But need a comprehensive dynamic management
Function-level dynamic management
  Function-to-region mapping
Mapping for ACET ≠ mapping for WCET
  The first mapping technique tuned for WCET
  Up to 80% improvement
Future work
  Prefetching by asynchronous DMA
  Comparison with cache

## Slide 19
Thank you!

## Slide 20: Scratchpads, an Alternative to Caches
The number of cores keeps increasing
Caches
  Coherence does not scale well to many cores
  Transparency – easy programming, difficult WCET analysis
Scratchpads (SPM)
  Simple, so scalable
  ~30% less area and power+
  Explicitly-managed – more predictable behavior
+Banakar et al. CODES+ISSS 2002
SPM
Core
DMA
Main Memory
Scratchpads can be a good fit for real-time embedded systems
Notes: So, what is scratchpad? Scratchpad is an on-chip storage, which is explicitly managed in software by executing DMA transfers. Scratchpads began to gain attention as computer architecture paradigm shifted to multicores since caches coherence logic does not scale well to many number of cores.
A study showed that replacing caches with scratchpads can reduce about 30% of area and power. This was on a single-core, so for more number of cores, the difference may be larger. Caches are transparent to programmers, so programmers do not need to care about caches, but this makes WCET analysis difficult because we need to predict what is happening inside the cache. On the other hand, scratchpads are explicitly-managed, so they only do what you tell them to do. It makes WCET analysis simpler.
So scratchpads can be a good alternative to caches in real-time systems.