## Slide 1: WCET-Aware Scratchpad Memory Management for Hard Real-Time Systems
Yooseong Kim
PhD Dissertation Defense
Jan 10th, 2017

## Slide 2: Hard Real-time Systems
Strict timing constraints
  Tasks have deadlines to finish execution
Timing determines correctness, not just performance
Missing a deadline can be catastrophic!
Image credit: JasonParis@Flickr
Actuation
Sensing
Deadlines!

## Slide 3: Ensuring Timing Correctness
Guarantee the absence of missed deadlines
  Worst-case execution time (WCET) analysis
  How?
    Testing based on measurement
    Static analysis
WCET
Execution Times
Frequency of occurrence

## Slide 4: Challenges in WCET Analysis
Incomprehensive testing (underestimation)
Pessimistic static timing analyses (overestimation)
WCET
Execution Times
Frequency of occurrence
WCET calculated
by static analysis
WCET observed by testing
Analysis pessimism
All execution scenarios
Observed by testing

## Slide 5: What Causes the Pessimism? (1/2)
Software uncertainties
  Loop bounds, branch directions, pointer resolutions, …
  Becoming less significant thanks to
    User annotations
    Safety standards and coding guidelines
      e.g. MISRA-C, DO-178C, ISO26262
        Limit recursions, pointer arithmetic, dynamic memory allocation, …
Significance

## Slide 6: What Causes the Pessimism? (2/2)
Microarchitectural state uncertainties
  Cache, branch predictors, pipelines, …
  Becoming more significant due to
    Complex modern hardware highly-optimized to the average case
      Growing gap between the average-case and the worst-case performance
    Resource sharing in multi-cores
Memory access times are especially important in memory-bound applications
Significance

## Slide 7: The Impact of Caches on the WCET
High impact
  Accessed by every instruction execution
  Growing gap between core and memory speed
Pessimistic analysis
  Implicit, uncontrolled space sharing
  Especially hard for non-LRU or multi-level caches
τ1
τ2
τ3
τ1
τ2
time
Unpredictable preemption delays
Notes: So what?
This imact causes what
cbc
--Scalabiliy?

## Slide 8: The Implications of the Pessimism
Relying on testing with an arbitrary safety-margin
  Typically of 20% * * Wartel et al. [SIES13]
  No safety-guarantee!
Using pessimistic analysis
  Limited HW utilization  Poor performance and high-cost system design
WCET
Execution Times
Frequency of occurrence
WCET observed by testing
Unsafe WCET estimate
Pessimistic WCET estimate

## Slide 9: The Objective of My Research
WCET Reduction
Based on Static Analysis
With Scalability for Large Applications
Improve Performance or Service Quality
Scheduling Flexibility
Low Cost System Design
Timing Correctness Guarantee
Correct-by-Construction
System Design
4
8
12
16
t
0

## Slide 10: Scratchpads (SPM): A Promising Alternative
Raw directly-addressable SRAM
Predictable timing through explicit and controlled space sharing
Goal:
  Develop management techniques for improving the WCET
0
1
A
A
B
C
B
SPM
…
DMA load A to 0
…
DMA load B to 1
…
DMA load C to 0
…
τ1
τ2
τ3
τ1
τ2
time
Can completely avoid preemption delay

## Slide 11: Overview - Architecture-awareness in SW
Software-managed memory hierarchy
  WCET-aware scratchpad memory management [1-7]
Software Branch Hinting
  20% branch penalty reduction in CELL BE over a heuristic in GCC [9]
Programming GPGPUs
  Analytical CUDA memory performance model with over 90% accuracy [8, 10]
Publications
TECS (under review)
TACO (under review)
DAC17 (under review)
DATE17 (accepted)
ICCAD16
RTAS14
ESLSyn13
TECS11
CODES+ISSS11
DAC11
Code management
  WCET analysis [1,6]
  Optimal function-to-region allocation [1,6]
  Optimal region-free allocation [1]
  Splitting functions into partitions [2,5]
  Comparison with other management granularities [2]
Stack management
  WCET analysis [3]
  Optimal stack management scheduling [3]
WCET-Aware SPM Management

## Slide 12: Code Management
Load a function before it’s called
Good for large applications
Key question is SPM space allocation
  Optimal allocation reduces the WCETs by
SPM
Functions
F1
F2
F4
F3
F5
Main memory
main() {
…
if (F1 not loaded)
load F1;
update SPM status;
call F1;
…
}
DMA
10% avg., up to 96% compared to previous techniques
39% avg., up to 87% compared to the static analysis results for LRU caches

## Slide 13: Stack Management
To avoid stack overflow, evict the stack frames in the SPM before a call and restore afterwards
Key question is to decide when (where) to evict and restore
  Optimal solutions reduces the WCETs by:
    7% avg., up to 49% compared to the static analysis for caches
    9% avg., up to 48% compared to previous techniques
main() {
…
Evict stack frames;
call F1;
Restore stack frames;
…
}
main
F1
F2
Main memory stack
SPM stack
DMA

## Slide 14: A Comparison of Code Management Techniques with Different Management Granularities

## Slide 15: Motivation
The literature on code management is divided into two domains according to their granularities
  No comparison has been done between them
Steinke et al.
[ISSS02, DATE02]
Janapsatya et al.
[ASPDAC06]
Puaut and Pais* [DATE07]
Falk et al* [DAC09]
Wu et al.* [EMSOFT10]
Prakash et al.* [DATE12]
Luppold et al.* [SCOPES16]
Basic-block-level
Pabalkar et al. [HiPC08]
Jung et al. [ASAP10]
Baker et al. [CODES+ISSS10]
Bai et al. [CODES+ISSS13]
Kim et al.* [RTAS14]
Function-level
* WCET-optimizing techniques

## Slide 16: Overview
Comparison of three different granularities
bb2
bb3
bb4
bb5
bb1
bb5
F1
F2
F3
F4
F5
F6
F11
F2
F3
F4
F5
F61
F12
F62
Functions
Regions
with function-splitting
Basic blocks
vs.
vs.

## Slide 17: Related Work
WCET impact of different instruction memories
  Wehmeyer and Marwedel [DATE05]
    Static SPM vs. cache (dm)
  Metzlaff and Ungerer [JSA14]
    Static SPM vs. D-ISP vs. cache (fa, LRU)
  Whitham and Schoeberl [ISORC14]
    Dynamic SPM vs. Method cache
Program partitioning
  Whitham and Audsley [ECRTS12]
    Optimal for one nominal case

## Slide 18: BL: Basic-Block-Level
Instruction fetch from both SPM and main memory
  Non-loop basic blocks – main memory
  Selected loop basic blocks - SPM
    Loaded at loop pre-header
How to select the basic blocks to be loaded?
  Heuristic from Puaut and Pais [DATE07]
bb2
bb3
bb4
bb5
bb1
bb5
load bb2,
bb3,
bb5
* Assume that SPM
can only hold 3 basic blocks

## Slide 19: FL: Function-Level
Fetch only from the SPM
Conditional loading operation
How to allocate functions to the SPM space?
  Heuristic from [RTAS14]
main() {
…
if (F1 not loaded)
load F1;
update SPM status;
call F1;
…
}
SPM
Functions
F1
F2
F4
F3
F5
Main memory
DMA

## Slide 20: RL: Region-Level
Function-level approach with function-splitting
  Not optimal, only to demonstrate the granularity between basic blocks and functions
Which functions to split?
  Starting from the largest function, split each function. Roll back if the WCET increases.
How to split a function?
  Make each loop level into a partition ≈ loop outlining or loop extraction
A
B
C
D
E
F
Partition 1
A
F
B
E
Partition 2
C
D
Partition 3

## Slide 21: Qualitative Comparison (1/2)
Timing-Predictability
  BL – Fully deterministic
  FL/RL – Requires separate static analyses
SPM Size Limitations
  FL/RL – The SPM must be at least as large as the largest function (partition)
main() {
…
if (F1 not loaded)
load F1;
update SPM status;
call F1;
…
}
F1 (3kB)
SPM (2kB)
Can’t be loaded

## Slide 22: Qualitative Comparison (2/2)
Management Efficiency
  BL – Struggles with large loops
    Some loop basic blocks can be left in the main memory
  FL – Struggles with large functions
Load A,B
…
…
…
A
B
C
A
B
SPM
NOT loaded
A
B
E
C
D
A
B
E
C
D
A
B
E
A
B
E
B
E
C
D
F1
F2
Before function splitting
After function splitting
SPM
SPM
Reload F1 and F2 in every iteration
No reloading

## Slide 23: Quantitative Comparison Setup
Benchmarks
  5 from WCET suite, 2 from MiBench suite, and 3 proprietary real-world control applications
  CFGs are constructed from ARMv4 binaries
All mem accesses except instruction fetches take 1 cycle (no stall cycle)
WCETs are statically calculated
DMA cost for loading x bytes:
Setup cost
Bandwidth

## Slide 24: Baseline Results
SPM Size: 40% of code size
DMA cost:
Stress testing
Models typical embedded microprocessors
BL suffers from large loops
FL suffers from size limitations
BL’s greedy heuristic stops prematurely
FL/RL: reloading in loops
BL: small loop bodies can entirely fit in the SPM
FL/RL: high overhead with SPM state checking
Best-case scenario for all: Small function with a loop with a high iteration count

## Slide 25: Changing Memory Access Times
Modeling different types of processors
Small microcontroller with a slow core clock (<100 MHz) and on-chip main memory based on SRAM or flash
More advanced system with faster core speed and off-chip DRAM main memory
With 3 real-world applications,
RL greatly outperforms BL

## Slide 26: Changing Memory Organizations
BL vs. RL when both SPM and cache are present
  Fetches from main memory in BL are now cached
  4-way LRU, 32B lines, miss latency of 20 cycle
  Static cache analysis from Cullmann [TECS13]
  Different ratios of SPM and caches like in NVIDIA GPUs
    C1S3 is overall the best configuration
  Loading a basic block can increase cache misses in another basic block

## Slide 27: Summary
Allocation granularity
  Regions performed the best
Management scheme
  Cache-like sophistication can increase management efficiency while still being predictable
Memory organization
  Using both SPMs and caches can be helpful if
    Inter-task conflicts can be managed
    Management technique is cache-aware
Notes: No evaluation

## Slide 28: The Significance of My Research
Significant WCET Reductions (vs. Caches)
  39% for code and 9% for stack
Based on Static Analysis
With Scalability for Large Applications
  SPMs provide per-task access privatizations  No preemption delays
Reduced Cost
Scheduling Flexibility
Improved Performance
Guaranteed Timing correctness
Correct-by-Construction
System Design
Notes: example

## Slide 29: Overview
Code management
  WCET analysis [1,6]
  Optimal function-to-region allocation [1,6]
  Optimal region-free allocation [1]
  Splitting functions into partitions [2,5]
  Management overhead reduction [4]
  Comparison with other management granularities [2]
Stack management
  WCET analysis [3]
  Optimal stack management scheduling [3]
Publications
TECS (under review)
TACO (under review)
DAC17 (under review)
DATE17 (accepted)
ICCAD16
RTAS14
ESLSyn13
TECS11
CODES+ISSS11
DAC11
Notes: Significance - contributions!
Overview - what I did.
spend more time in overview slide

## Slide 30
----- End of the presentation

## Slide 31: Static vs. Dynamic Management
Static management
  Load only at loading time before execution
  Good: When everything fits in the SPM
  Bad: When it doesn’t
Dynamic management
  Load on demand at runtime
  Good: Able to exploit locality better
  Bad: Runtime overhead

## Slide 32: Splitting Non-loop Code Region
Form single-entry and single-exit regions
  To form a function-like code structure
A
B
C
D
Splitting points that do not make SESE partitions
Splitting point that makes SESE partitions

## Slide 33: Larger SPM Sizes
With a larger SPM, partitions from RL can be better allocated
SPM Size: 80% of code size
BL loads almost all loop code