## Slide 1: Optimizing Heap Data Management on Software Managed Many-core Architectures
By: Jinn-Pean Lin

## Slide 2: Challenges of Cache-Based Memory Architecture
Caches as On-chip Memories
  Universal application
  Data management done by hardware logic
Challenges
  Large area
    50% chip area [1]
  High energy consumption
    50% energy consumption [1]
  Coherency unscalable with core count [2]
[1] Niar et al., ICM 2004, pp. 244-247.
[2] Xu et al., ICS 2011.
[3] www.itjungle.com/2014/02/17/tfh021714-story01/
IBM Power8 [3]
Notes: [1] S. Niar, S. Meftali and J. L. Dekeyser, "Power consumption awareness in cache memory design with SystemC," Proceedings. The 16th International Conference on Microelectronics, 2004. ICM 2004., 2004, pp. 244-247.
[2] Y. Xu, Y. Du, Y. Zhang, and J. Yang, “A Composite and Scalable Cache Coherence Protocol for Large Scale CMPs,” in Proc. of ICS, 2011.
[3] www.itjungle.com/2014/02/17/tfh021714-story01/

## Slide 3: Software Managed Many-core (SMM) Architectures
Data Array
Tag Array
Tag Comparators, Muxes
Address Decoder
Cache
SPM
[4] Banakar et al, CODES2002, pp. 73-78.
[5] Flachs et al, SSC2006, pp.63-70. [6] REX Computing, 2014.
Instead of Caches use Scratchpad Memories (SPM)
  SPM is Software Managed Memory
    Data management explicitly controlled by instructions
  Less Hardware Required
    46% lower area overhead than cache [4]
    40% less energy consumption than cache [4]
Examples
  IBM Cell BE [5]
  The NEO CHIP [6]
core
Main Memory
SPM
core
SPM
SMM Architecture
DMA
DMA
Notes: [4] R. Banakar, S. Steinke, Bo-Sik Lee, M. Balakrishnan and P. Marwedel, "Scratchpad memory: a design alternative for cache on-chip memory in embedded systems," Proceedings of the Tenth International Symposium on Hardware/Software Codesign. CODES 2002 (IEEE Cat. No.02TH8627), Estes Park, CO, USA, 2002, pp. 73-78.
[5] B. Flachs at el., “The Microarchitecture of the Synergistic Processor for A Cell Processor,” IEEE Solid-state circuits, vol. 41, no. 1, pp. 63–70, 2006.
[6] REX Computing, Inc., “THE NEO CHIP,” http://rexcomputing.com/, 2014.

## Slide 4: Insertion of Management Instructions
int global;
f() {
int a, b;
DMA.fetch(global);
global = a + b;
DMA.writeback(global);
DMA.fetch(f2);
f2();
}
Core can only access the SPM
SPM and Main Memory have separate address ranges
Data can be transferred between SPM and Main memory through explicit direct memory access (DMA) instructions
Initially the application is loaded in the main memory
How can the application execute?
  Instructions to bring data into SPM before it is needed, and push it out after its use must be inserted in the application
core
Main Memory
SPM
DMA
int global;
f() {
int a, b;
global = a + b;
f2();
}

## Slide 5: Why Heap Data Management?
All data must be managed on the SPM
  Code Data
    Several works [7][8][9]
    Code management overhead comparable/better than caches
  Stack Data
    Several works [10][11][12]
    Stack management overhead comparable/better than caches
  Global Data
    Several works [13][14][15]
    Global management overhead comparable/better than caches
  Heap Data?
    Some applications use heap data very significantly
      In MiBench, susan smoothing, 94% of all data access are heap accesses
Global Data
Code Data
Stack Data
Heap Data
[7] Cai et al, DATE2017. [8] Lu et al, TECS2015.
[9] Kim et al, ICCAD2016. [10] Cai et al, ASAP2016.
[11] Lu et al, DAC2013. [12] Bai et al, ASAP2011.
[13] Liu et al, JCSE2015, [14] Cho et al, SIGPLAN2007
[15] Udayakumaran et al, TECS2006.
Notes: [7] Jian Cai, Yooseong Kim, Youngbin Kim, Aviral Shrivastava and Kyoungwoo Lee, “Reducing Code Management Overhead in Software-Managed Multicores,” 2017 International Conference on Design Automation and Test in Europe (DATE), 2017.
[8] Jing Lu, Ke Bai and Aviral Shrivastava, “Efficient Code Assignment Techniques for Local Memory on Software Managed Multicores,” In ACM Transactions on Embedded Computing Systems (TECS), 2015.
[9] Youngbin Kim, Jian Cai, Yooseong Kim, Kyoungwoo Lee and Aviral Shrivastava, “Splitting Functions in Code Management on Scratchpad Memories,” In Proceedings of the IEEE/ACM International Conference on Computer-Aided Design (ICCAD), 2016.
[10] Jian Cai and A. Shrivastava, "Efficient pointer management of stack data for software managed multicores," 2016 IEEE 27th International Conference on Application-specific Systems, Architectures and Processors (ASAP), London, 2016, pp. 67-74.
[11] Jing Lu, Ke Bai and Aviral Shrivastava, “SSDM: Smart Stack Data Management for Software Managed Multicores (SMMs),” In Proceedings of the 50th Design Automation Conference (DAC), 2013.
[12] Ke Bai, Aviral Shrivastava and Saleel Kudchadker, “Stack Data Management for Limited Local Memory (LLM) Multi-core Processors,” In Proceedings of the International Conference on Application Specific Systems, Architectures and Processors (ASAP), 2011.
[13] Y. Liu and W. Zhang. "Scratchpad Memory Architectures and Allocation Algorithms for Hard Real-Time Multicore Processors," Journal of Computing Science and Engineering, v.9, 2015.
[14] Hyungmin Cho, Bernhard Egger, Jaejin Lee, and Heonshik Shin, “Dynamic data scratchpad memory management for a memory subsystem with an MMU,” SIGPLAN Not. 42, 7 (June 2007), 195-206.
[15] S. Udayakumaran, A. Dominguez, and R. Barua, “Dynamic allocation for scratch-pad memory using compile-time decisions,” Trans. on Embedded Computing Sys., 5(2):472{511, 2006.

## Slide 6: Related Works on Heap Data Management
[16] Dominguez et al, JEC2005.
  Only maps frequently used heap data on SPM
  Not applicable to SMM architectures
[17] Bai et al, CODES+ISSS2010.
  Manages heap data with full associative software cache having least recently used replacement policy
  Implements programmer inserted heap management function
  High management overhead
[18] Bai et al, DATE2013. (State-of-the-art work)
  Manages heap data with set associative software cache having round robin replacement policy
  Implements compiler inserted heap management function
  43% less runtime than [17]
Notes: [16] A. Dominguez, S. Udayakumaran, and R. Barua, “Heap Data Allocation to Scratch-pad memory in Embedded Systems,” J. Embedded Comput., vol. 1, no. 4, pp. 521–540, 2005.
[17] K. Bai and A. Shrivastava, “Heap Data Management for Limited Local Memory (LLM) Multi-core Processors,” in Proc. CODES+ISSS, 2010, pp. 317–326.
[18] K. Bai and A. Shrivastava, "Automatic and efficient heap data management for Limited Local Memory multicore architectures," 2013 Design, Automation & Test in Europe Conference & Exhibition (DATE), Grenoble, France, 2013, pp. 593-598.

## Slide 7: [Bai 2013] uses Heap Management Function: g2l
Raw Code:
int *p;
p = malloc(20);
*p = 10;
SPM
Main Memory
p
core
Without g2l
0x00000000
0x000FFFFF
0x000FFFFF
0xFFFFFFFF
SPM
Main Memory
g2l(p)
p
DMA
core
With g2l
0x00000000
0x000FFFFF
0x000FFFFF
0xFFFFFFFF
Converted Code:
int *p;
p = malloc(20);
*g2l(p) = 10;
Notes: Demo: Running code with and without g2ls on SMM architectures

## Slide 8: g2l Implementation
Get Set Index with Hash
Main Memory Address
Sequential
Search in Set
Replacement Policy
Data Movement
SPM Address Calculation
Entry Offset
Set Index
Entry Index
Entry Index
Address Check
S Sets
4 Entries
Modified Bit
Tag
Heap Block
SPM

## Slide 9: [Bai2013] calls too many g2l
Raw Code:
int *p1, *p2;
p1 = malloc(20);
p2 = p1;
*p2 = 10;
Converted Code:
int *p1, *p2;
*g2l(&p1) = malloc(20);
*g2l(&p2) = *g2l(&p1);
*g2l(*g2l(&p2)) = 10;
Why are g2ls inserted at every data access?
  Heap accesses are identified at runtime

## Slide 10: [Bai2013] g2l implementation is complex
Get Set Index with Hash
Main Memory Address
Sequential
Search in Set
Replacement Policy
Data Movement
SPM Address
Calculation
Case | g2l Instructions
Hit | 56
Miss | 145
Miss with Write-back | 172
Entry Offset
Set Index
Entry Index
Entry Index
Address Check
S Sets
4 Entries
Modified Bit
Tag
Heap Block
SPM
Notes: Haswell L1 cache hit latency: 4 cycles

## Slide 11: Our Optimizations to Lower Management Overhead
Objectives
  Reduce g2l insertions
  Reduce dynamic instruction of each g2l
Optimizations
  Static Detection of Heap Access
    Identify heap accesses at compile-time
    Insert g2l only at heap accesses – not on all accesses
    Eliminate run-time checking for definite heap accesses
  Simplifying Management Framework
    Implement direct map software cache instead of set associative software cache
    Simplify SPM address calculation
  Inlining and Combining Management Code
    Inline g2ls
    Combine common steps and place them before any heap access
  Adjusting Block Size
    Compiler selects block size according to heap access pattern
    Optional optimization for embedded applications

## Slide 12: Static Detection of Heap Access
Steps:
Find heap allocations
Find aliasing pointers (aka. heap pointers)
Insert g2l only at data accesses through heap pointers
Sample Code:
int* p1, *p2;
p1 = malloc(20);
p2 = p1;
*p2 = 10;
malloc
p1
p2
*g2l(p2) = 10;

## Slide 13: Static Detection of Heap Access
Prior Work:
int* p1, *p2;
*g2l(&p1) = malloc(20);
*g2l(&p2) = *g2l(&p1);
*g2l(*g2l(&p2)) = 10;
Our Work:
int* p1, *p2;
p1 = malloc(20);
p2 = p1;
*g2l(p2) = 10;
Raw Code:
int *p1, *p2;
p1 = malloc(20);
p2 = p1;
*p2 = 10;

## Slide 14: Demo: Static Detection of Heap Access
Benchmark | Peak Heap Size (KB) | Number of g2l calls |  | Reduction
 |  | Before | After | 
Adpcm Decode | 0 | 116,702,082 | 0 | 100%
Adpcm Encode | 0 | 10,211,280 | 0 | 100%
Dijkstra | 6.43 | 149,209,166 | 19,077,784 | 87%
FFT | 32 | 336,608 | 90,188 | 73%
iFFT | 32 | 336,671 | 90,204 | 73%
Patricia | 766 | 3,114,668 | 893,184 | 71%
SHA | 0 | 8,350,153 | 0 | 100%
String Search | 0 | 2,198,090 | 0 | 100%
Susan Corner | 92.16 | 1,238,553 | 273,717 | 78%
Susan Edge | 42.81 | 2,628,207 | 579,221 | 78%
Susan Smoothing | 17.35 | 37,252,034 | 4,891,730 | 87%
Notes: Demo: Number of g2ls inserted before and after optimization

## Slide 15: Uncertainties of Static Detection of Heap Access
int main() {
int a[10], *b, *c;
b = malloc(40);
if(rand() % 2)
c = b;
else
c = a;
a[2] = 25;
b[3] = 20;
c[4] = 15;
}
(a) Sample code
int main() {
int a[10], *b, *c;
b = malloc(40);
if(rand() % 2)
c = b;
else
c = a;
a[2] = 25;
*g2l(&b[3]) = 20;
*g2l_rc(&c[4]) = 15;
}
(b) Insert g2l at definite heap accesses. Otherwise insert g2l_rc to first check if an access is to heap at runtime

## Slide 16: Static Detection of Heap Access
Get Set Index
with Hash
Main Memory Address
Sequential
Search in Set
Replacement Policy
Data Movement
SPM Address
Calculation
Entry Offset
Set Index
Entry Index
Entry Index
Address Check
Case | g2l Instructions | 
 | Prior Opt | Prior + Current Opt
Hit | 56 | 50
Miss | 145 | 139
Miss + Write-back | 172 | 166
S Sets
4 Entries
Modified Bit
Tag
Heap Block
SPM
Notes: Demo: Code difference of new and old g2l

## Slide 17: Results of Static Detection of Heap Access
Chart: Runtime Normalized to Prior Work
| ADPCM Dec. | ADPCM Enc. | Dijkstra | FFT | iFFT | Patricia | SHA | String Search | Susan Corner | Susan Edge | Susan Smoothing | Average
Statically Detect Heap Access | 0.098603 | 0.08622 | 0.53972 | 0.74588 | 0.74585 | 0.74273 | 0.083329 | 0.15001 | 0.56978 | 0.58039 | 0.44037 | 0.43481

## Slide 18: Our Approach to Lower Management Overhead
Objectives
  Reduce g2l insertions
  Reduce dynamic instruction of each g2l
Optimizations
  Static Detection of Heap Access
    Identify heap accesses at compile-time
    Insert g2l only before heap accesses
    Eliminate run-time checking for definite heap accesses
  Simplifying Management Framework
    Implement direct map software cache instead of set associative software cache
    Simplify SPM address calculation
  Inlining and Combining Management Code
    Inline g2ls
    Combine common steps and place them before any heap access
  Adjusting Block Size
    Compiler selects block size according to heap access pattern
    Optional optimization for embedded applications

## Slide 19: Simplifying Management Framework
Get Set Index with Hash Function
Main Memory Address
Sequential
Search in the Set
Replacement Policy
Data Movement
SPM Address
Calculation
Entry Offset
Set Index
Entry Index
Entry Index
SPM Offset
Get Entry Index with Hash
Case | g2l Instructions | 
 | Prior Opt | Prior + Current Opt
Hit | 50 | 21
Miss | 139 | 43
Miss + Write-back | 166 | 58
S Sets
4 Entries
Modified Bit
Tag
Heap Data
SPM
SPM
S Sets
1 Entry
Modified Bit
Tag
Heap Block
Notes: Demo: Show code implementation of g2l in prior work vs after optimization

## Slide 20: Results of Simplifying Management Framework
Chart: A: Static Detection of Heap Access B: Simplifying Management Framework
| ADPCM Dec. | ADPCM Enc. | Dijkstra | FFT | iFFT | Patricia | SHA | String Search | Susan Corner | Susan Edge | Susan Smoothing | Average
A | 0.098603 | 0.08622 | 0.53972 | 0.74588 | 0.74585 | 0.74273 | 0.083329 | 0.15001 | 0.56978 | 0.58039 | 0.44037 | 0.43481
A+B | 0.098603 | 0.086221 | 0.23221 | 0.48448 | 0.48441 | 0.51591 | 0.083325 | 0.15006 | 0.22973 | 0.2225 | 0.17393 | 0.25103

## Slide 21: Our Approach to Lower Management Overhead
Objectives
  Reduce g2l insertions
  Reduce dynamic instruction of each g2l
Optimizations
  Static Detection of Heap Access
    Identify heap accesses at compile-time
    Insert g2l only before heap accesses
    Eliminate run-time checking for definite heap accesses
  Simplifying Management Framework
    Implement direct map software cache instead of set associative software cache
    Simplify SPM address calculation
  Inlining and Combining Management Code
    Inline g2ls
    Combine common steps and place them before any heap access
  Adjusting Block Size
    Compiler selects block size according to heap access pattern
    Optional optimization for embedded applications

## Slide 22: Inlining and Combining Management Code
spm_addr g2l(mem_addr):
G2L_COMMON;
spm_addr =
G2L_SPECIFIC(mem_addr);
return spm_addr;
int main() {
*g2l(&heap[0]) = 2;
*g2l(&heap[1]) = 4;
for(i = 2; i < n; i++)
*g2l(&heap[i]) = i;
}
int main() {
G2L_COMMON;
*G2L_SPECIFIC(&heap[0]) = 2;
*G2L_SPECIFIC(&heap[1]) = 4;
for(i = 2; i < n; i++)
*G2L_SPECIFIC(&heap[i]) = i;
}
(b) Management calls with prior technique
(c) Inlining management calls and eliminate common operations
int main() {
heap[0] = 2;
heap[1] = 4;
for(i = 2; i < n; i++)
heap[i] = i;
}
(a) Sample code
Notes: G2L_COMMON: Access invariant instructions
G2L_SPECIFIC(): Access dependent instructions

## Slide 23: Demo and Results
Case | g2l Instructions | 
 | Prior Opt | Prior + Current Opt
Hit | 21 | 9
Miss | 43 | 37
Miss + Write-back | 58 | 45
Notes: Demo: Show g2l inserted before and after optimization

## Slide 24: Results of Inlining and Combining Management Code
Chart: A: Static Detection of Heap Access B: Simplifying Management Framework C: Inlining and Combining Management Code
| ADPCM Dec. | ADPCM Enc. | Dijkstra | FFT | iFFT | Patricia | SHA | String Search | Susan Corner | Susan Edge | Susan Smoothing | Average
A | 0.098603 | 0.08622 | 0.53972 | 0.74588 | 0.74585 | 0.74273 | 0.083329 | 0.15001 | 0.56978 | 0.58039 | 0.44037 | 0.43481
A+B | 0.098603 | 0.086221 | 0.23221 | 0.48448 | 0.48441 | 0.51591 | 0.083325 | 0.15006 | 0.22973 | 0.2225 | 0.17393 | 0.25103
A+B+C | 0.098603 | 0.086221 | 0.15683 | 0.38789 | 0.38781 | 0.46547 | 0.083325 | 0.15006 | 0.12731 | 0.12135 | 0.10715 | 0.19746

## Slide 25: Our Approach to Lower Management Overhead
Objectives
  Reduce g2l insertions
  Reduce dynamic instruction of each g2l
Optimizations
  Static Detection of Heap Access
    Identify heap accesses at compile-time
    Insert g2l only before heap accesses
    Eliminate run-time checking for definite heap accesses
  Simplifying Management Framework
    Implement direct map software cache instead of set associative software cache
    Simplify SPM address calculation
  Inlining and Combining Management Code
    Inline g2ls
    Combine common steps and place them before any heap access
  Adjusting Block Size
    Compiler selects block size according to heap access pattern
    Optional optimization for embedded applications

## Slide 26: Adjusting Block Size
hp1[i]
hp2[i]
Cacheline
Cacheline
Cold Miss Prevention
Conflict Miss Prevention
Reduce block size when multiple heap allocations accessed in innermost loop
hp1 = malloc(…);
hp2 = malloc(…);
for(i = 0; i < n; i++)
hp1[i] = i ^ hp2[i];
Increase block size when only one heap allocations accessed in innermost loop
hp = malloc(…);
for(i = 0; i < n; i++)
hp[i] = rand();
hp[i]
hp[i + 1]

## Slide 27: Adjusting Block Size – Compiler Heuristic
Multiple heap objects accessed within innermost loop?
Heap access pattern
Increase set count
Increase block size
No
Yes
Reduce conflict misses
Reduce cold misses
Profiling
Static detection of heap access
Heap access location
Heap allocation size
Notes: Demo: Block size before and after optimization

## Slide 28: Results of Adjusting Block Size
Chart: A: Static Detection of Heap Access B: Simplifying Management Framework C: Inlining and Combining Management Code D: Adjusting Block Size
| ADPCM Dec. | ADPCM Enc. | Dijkstra | FFT | iFFT | Patricia | SHA | String Search | Susan Corner | Susan Edge | Susan Smoothing | Average
A | 0.098603 | 0.08622 | 0.53972 | 0.74588 | 0.74585 | 0.74273 | 0.083329 | 0.15001 | 0.56978 | 0.58039 | 0.44037 | 0.43481
A+B | 0.098603 | 0.086221 | 0.23221 | 0.48448 | 0.48441 | 0.51591 | 0.083325 | 0.15006 | 0.22973 | 0.2225 | 0.17393 | 0.25103
A+B+C | 0.098603 | 0.086221 | 0.15683 | 0.38789 | 0.38781 | 0.46547 | 0.083325 | 0.15006 | 0.12731 | 0.12135 | 0.10715 | 0.19746
A+B+C+D | 0.098603 | 0.086221 | 0.12577 | 0.35218 | 0.35211 | 0.35185 | 0.083325 | 0.15006 | 0.12073 | 0.11503 | 0.095477 | 0.17558

## Slide 29: Scalability Results Without Adjusting Block Size
Chart: SPM Size (KB)
| 4 | 8 | 16 | 32 | 64
Patricia | 0.46547 | 0.44553 | 0.41801 | 0.3996 | 0.38041
Dijkstra | 0.15683 | 0.17666 | 0.21104 | 0.27778 | 0.35303
FFT/iFFT | 0.38789 | 0.38901 | 0.38064 | 0.34336 | 0.3426
Average | 0.19908 | 0.19676 | 0.19164 | 0.18973 | 0.19095
Susan Corner | 0.12731 | 0.12866 | 0.12826 | 0.1424 | 0.1399
Susan Edge | 0.12135 | 0.12406 | 0.12191 | 0.13336 | 0.137
Susan Smoothing | 0.10715 | 0.10625 | 0.098336 | 0.11835 | 0.118
ADPCM Dec. | 0.098603 | 0.098603 | 0.098603 | 0.098602 | 0.098601
ADPCM Enc. | 0.086221 | 0.086221 | 0.086219 | 0.086217 | 0.086212
SHA | 0.083325 | 0.08164 | 0.078507 | 0.072931 | 0.063694
String Search | 0.15006 | 0.13099 | 0.10428 | 0.073664 | 0.045814

## Slide 30: Scalability Results With Adjusting Block Size
Chart: SPM Size (KB)
| 4 | 8 | 16 | 32 | 64
FFT/iFFT | 0.35218 | 0.35802 | 0.35914 | 0.3492 | 0.34905
Susan Corner | 0.12073 | 0.13297 | 0.14196 | 0.14881 | 0.15357
Susan Edge | 0.11503 | 0.12587 | 0.1309 | 0.13748 | 0.14522
Average | 0.17558 | 0.16984 | 0.16062 | 0.15099 | 0.1429
Susan Smoothing | 0.095477 | 0.10716 | 0.11017 | 0.12036 | 0.11861
ADPCM Dec. | 0.098603 | 0.098603 | 0.098603 | 0.098602 | 0.098601
ADPCM Enc. | 0.086221 | 0.086221 | 0.086219 | 0.086217 | 0.086212
Patricia | 0.35185 | 0.2763 | 0.19697 | 0.12992 | 0.081137
Dijkstra | 0.12577 | 0.11254 | 0.10098 | 0.094509 | 0.080963
SHA | 0.083325 | 0.08164 | 0.078507 | 0.072931 | 0.063694
String Search | 0.15006 | 0.13099 | 0.10428 | 0.073664 | 0.045814
Notes: Impact of spm flushing decreases as added optimization increases block size and thereby decreasing set count for benchmarks such as dijkstras

## Slide 31: Summary
Problem
  Heap data is common and thus should be managed on SMM architectures
Prior work
  Inefficiently manages heap data on SMM architectures with software caching
Our Work
  Reduced g2l calls
  Reduced g2l overhead
Result
  Reduced prior work’s runtime by 83%