## Slide 1: Application-aware Performance Optimization for Software Managed Manycore Architectures
Jing Lu
Computer Science, ASU
Supervisory Committee:
Prof. Aviral Shrivastava (Chair)
Prof. Hessam Sarjoughian
Prof. Carole-jean Wu
Prof. Adam Doupé

## Slide 2: Power efficiency – key in architecture design
Adding Intelligent?
  Heat (too much, hard to dissipate)
  Power (too high)
Parallelism
  Number of cores
  Operating frequency
Performance
power consumption
Intel’s Knights Corner is a many-core chip

## Slide 3: Challenge of scaling
Power cap
  Intel Core i7-7700, 4-core consumes 91W at 4.2GHz
  91 ∗ 100/4 = 2275W >> 250W
Coherence maintenance challenge
  Snooping
    Broadcasting
    Shared bus
    Not scalable
  Directory-based
    Additional storage
    Increase memory access latency
    Network traffic
AMD’s Bulldozer is an example of how bolting more cores together can result in a slower end product
Share logic/caches
Power consumption limits clock speed

## Slide 4: Software Managed Manycore Architecture
Shifting intelligence from hardware to software to simplify hardware
  Intel SCC (2011)
  Kalray MPPA-256 (2013)
Challenges:
  Which hardware component to remove?
  How to minimize the software overhead?
Our exploration:
  Caching mechanism -> Software managed SPM
  Branch prediction -> Software branch hinting

## Slide 5: Thesis Overview
Stack data management
  [DAC 2013] SSDM: Smart Stack Data Management for Software Managed Multicores (SMMs)
Code management
  Conference paper: [CODES+ISSS 2013] CMSM: An Efficient and Effective Code Management for Software Managed Multicores
  Journal Article: [TECS 2015] Efficient Code Assignment Techniques for Local Memory on Software Managed Multicores
Heap management
  [VLSID 2019] Efficient Heap Data Management on Software Managed Manycore Architectures
Software branch hinting
  [CODES+ISSS 2011] Branch Penalty Reduction on IBM Cell SPUs via Software Branch Hinting
SPM: scratchpad memory
DMA Engine
Main Memory
Simple Core
SPM
Instruction
memory
Hint Target
Buffer
Inline Prefetch
Buffer
1
0
branch address
target address
IR
Instruction Fetch

## Slide 6: Caching -> Software Managed SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Interconnect Bus
DMA
Data Array
Tag Array
Tag Comparators, Muxes
Address Decoder
Cache
SPM
SPM based Multicore
  A truly distributed memory architecture on-a-chip
Data transfer
  Managed in software

## Slide 7: Data Management Challenges
Make it work!
  Software needs to be aware of :
    Local memory availability
    Task requirement at every point of time
Minimize overhead
  Minimize management code size
    Each management instruction is an overhead!
  Perform management only when necessary
  Minimize data transfer
    Size
    Frequency
int global;
f1(){
int a;
global = global + a;
f2();
}
int global;
f1(){
int a;
DMA.fetch(global)
global = global + a;
DMA.writeback(global)
DMA.fetch(f2)
f2();
}

## Slide 8: Stack Data Management is Important
Stack data management is important
  Stack data accesses account for a significant portion of all the memory accesses
Stack data is dynamic
  Execution time allocation & de-allocation
    Function call & return
  Function stack size is known at compilation time, but not stack depth
    Recursive functions

## Slide 9: Stack Data Management is Challenging
Local scratchpad memory has fixed size
  When stack size larger than available memory
    Explicit management is required
    Or stack data will overwrite heap data which may cause program crash
F1() {
int a,b;
F2();
}
F2() {
F3();
}
F3() {
int j=30;
}
(a) Example
(b) State of scratchpad memory before F3 is called
Stack Pointer
F1 (50 bytes)
F2 (20 bytes)
global
heap
…...
code
F3 (30 bytes)
Crash!

## Slide 10: Circular Stack Data Management
Scratchpad Memory Size = 128 bytes
Scratchpad Memory
Global Memory
F1
F2
F3
32
68
128
Start
End
F4
54
Global SP
[ASAP 2011] Stack Data Management for Limited Local Memory (LLM) Multi-core Processors
Function | Frame Size (bytes)
F1 | 28
F2 | 40
F3 | 60
F4 | 54
F1
F2
F3
F4
Intuitive solution –
  Evict some stack data in the stack space to main memory
  Bring them back to stack space when the evicted frame is needed

## Slide 11: How to Manage Stack Data?
Dynamic software technique
  fci(func_stack_size)
    Check for available space in scratchpad memory
    Move old frame(s) to global memory if needed
  fco(func_stack_size)
    Check if the caller frame exists in scratchpad memory!
    Fetch from global memory, if it is absent
F1() {
int a,b;
F2();
}
F2() {
F3();
}
F3() {
int j=30;
}
(a) Example
(b) State of scratchpad memory before F3 is called
Stack Pointer
F1 (50 bytes)
F2 (20 bytes)
F3 (30 bytes)
code
global
heap
…...
F1() {
int a,b;
fci(F2);
F2();
fco(F1);
}
F2() {
fci(F3);
F3();
fco(F2);
}
F3() {
int j=30;
}

## Slide 12: Drawbacks of Circular Stack Data Management
Scratchpad Memory Size = 128 bytes
Scratchpad Memory
Global Memory
F1
F2
F3
68
128
Start
End
F4
54
Global SP
[ASAP 2011] Stack Data Management for Limited Local Memory (LLM) Multi-core Processors
Stack memory fragmentation
Book-keeping of complicated information
  Stack size of each function
  Start & end address of the free slots
  Information need to be checked & updated in each management
Better to make small number of large requests than large number of small requests
  Memory pipeline is becoming longer
  Waiting time to get the chance to access memory
Management function is inserted even when it is not necessary
  Every function call

## Slide 13: Motivation of Optimizing Stack Management (1)
Opportunities to reduce repeated API
F0() {
  fci(F1);
  F1();
  fco(F0);
  fci(F2);
  F2();
  fco(F0);
}
F0(){
  fci(F1);
  F1(){
  fci(F2);
  F2();
  fco(F1);
  }
  fco(F0);
}
Sequential Calls
Nested Call
F0(){
while(<condition>){
fci(F1)
F1();
fco(F0)
}
}
Call in a loop
F0() {
  fci(max(F1,F2));
  F1();
  fco(F0);
  F2();
  fco(F0);
}
F0(){
fci(F1+F2);
  F1(){
  F2();
  }
  fco(F0);
}
F0(){
fci(F1);
while(<condition>){
F1();
}
fco(F0);
}
F0() {
  F1();
  F2();
}
F0() {
  F1(){
  F2();
  }
}
F0(){
while(<condition>){
F1();
}
}
Original code
Circular Stack Management Outcome
Possible optimization
Notes: The state-of-the-art circular stack management is more like a brute force solution and has a lot of unnecessary management overhead. Here are some examples of reducing stack data management overhead by increasing the management granularity.
In the first example, there are two sequential functions F1 and F2. Instead of managing F1 and F2 separately, we can manage them all together and reduce management overhead
In the second example, there are nested function calls. Similarly, instead of managing F1 and F2 separately, we can first reserve space for F1 and F2 together, and make sure the stack frame of F0 is in local memory before returning to F0.
The third example is even more interesting. Since F1 is being called in a loop, instead of performing stack data management in every iteration, we hoist the management functions outside of the loop so that those functions will be called by only once.

## Slide 14: Motivation of Optimizing Stack Management (2)
F1
F2
F3
32
68
128
SP
F4
54
Opportunities to simplify management logic
  Frequent API calls
  Complicated book-keeping
Avoiding thrashing is critical – When to evict the stack frame?
Scratchpad Memory Size = 128 bytes
Scratchpad Memory
Global Memory
F1
F2
F3
F4

## Slide 15: Optimizing Stack Management
Not performing management when not absolutely needed
  Fewer DMA calls
    Memory latency of a task will be very strongly dependent on the number of memory requests
Performing minimal work each time management is performed
  Transfer stack data at the whole stack space granularity
  Management library (_sstore and _sload) becomes simpler
Avoiding thrashing
  Place management functions judiciously

## Slide 16: Smart Stack Data Management
.c
Runtime
Library .a
Weighted Call Graph
compiler
Executable
SSDM
Place info about where to perform management
Formulate the optimization problem of where to insert the management functions so as to minimize the management overhead
  Finding an optimal cutting of a weighted call graph
  A cutting of the graph is defined as a set of cuts on graph edges, indicating a pair of stack management functions to be inserted respectively before and after a function call.
10
5
50
25
F0
32
F1
128
F2
32
F3
20
F4
32
Cut 1
Cut 0
Cut 0
Cut 0
A new runtime library with less management complexity
An effective heuristic (SSDM)
  Takes Weighted Call Graph as input
  Generates an effective management function placement scheme

## Slide 17: Cutting of Weighted Call Graph
main: 128
print: 32
stream: 1936
init: 0
update: 1600
final: 80
transform: 352
0
1
1
1
10
1
1
100
0
0
0
Cut 1
Cut 2
Cut 3
Cut 4
artificial edge
Cut 5
main
stream
SP
final
transform
Scratchpad Memory
Global Memory

## Slide 18: Stack: Problem Formulation
Formulate library placement as a problem of optimal cutting of a weighted call graph (WCG)
main: 128
print: 32
stream: 1936
init: 0
update: 160
final: 80
Transform: 352
0
1
1
1
10
1
1
100
0
0
0
Cut 1
Cut 2
Cut 3
Cut 4
artificial edge
Cut 5
Notes: With the idea of placing cutting on the weighted call graph, we formulated the stack data management problem as a problem of optimal cutting of a weighted call graph.

## Slide 19: Stack: Management Constraint
main: 128
print: 32
stream: 1936
init: 0
update: 160
final: 80
Transform: 352
0
1
1
1
10
1
1
100
0
0
0
Cut 1
Cut 5

## Slide 20: Stack: Overhead Estimation

## Slide 21: Illustration of Heuristic SSDM[1]
10
5
50
25
F0
32
F1
128
F2
32
F3
20
F4
32
Cut 1
Cut 2
Cut 3
Cut 4
Cut | 1 | 2 | 3 | 4
Removing benefit | 2104 | 12080 | 5920 | 1256
Segment: <F0>,<F1>,<F1>,<F2>,<F3>,<F4>
10
5
50
25
F0
32
F1
128
F2
32
F3
20
F4
32
Cut 1
Cut 3
Cut 4
Cut | 1 | 3 | 4
Removing benefit | 2224 | 6400 | 1256
Segment: <F0>, <F1,F2>, <F1>,<F3>,<F4>
Cut 0
Cut 0
Cut 0
Cut 0
Cut 0
Cut 0
iteration 1

## Slide 22: Illustration of Heuristic SSDM[2]
10
5
50
25
F0
32
F1
128
F2
32
F3
20
F4
32
Cut 1
Cut | 1 | 4
Removing benefit | x | 1256
Segment: <F0>, <F1,F2,F3>,<F1>,<F4>
Cut 0
Cut 0
Cut 0
Cut 4
10
5
50
25
F0
32
F1
128
F2
32
F3
20
F4
32
Cut 1
Cut | 1
Removing benefit | x
Segment: <F0>, <F1,F2,F3>,<F1,F4>
Cut 0
Cut 0
Cut 0
iteration 2
iteration 3

## Slide 23: Experiment Setup
Hardware
  IBM Cell BE
    1 PPE @ 3.2 GHz
    6 SPE @ 3.2 GHz
Benchmarks
  Mibench – modified to run on SPEs

## Slide 24: Overall Performance
Chart: 
| BasicMath | Dijkstra | FFT | FFT_inverse | SHA | String_Search | Susan_Edges | Susan_Smoothing | Average
ILP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SSDM | 1 | 1 | 1 | 1 | 1.0011 | 1 | 1 | 1 | 1
CSM | 1.1 | 1.1791 | 1.1319 | 1.1358 | 1.1134 | 1.073 | 1.0763 | 1.0256 | 1.1053
11%

## Slide 25: Reduction of Management Overhead
Chart: 
| BasicMath | Dijkstra | FFT | FFT_inverse | SHA | String_Search | Susan_Edges | Susan_Smoothing | Average
SSDM | 0 | 0.0089723 | 0.0010279 | 0.001267 | 0.020432 | 0.03007 | 0.00094761 | 0.0024773 | 0.0081492
CSM | 0.099993 | 0.18968 | 0.13306 | 0.13722 | 0.13492 | 0.10525 | 0.077341 | 0.028125 | 0.1132
13X

## Slide 26: Code Management: Problem
Designated code region in the local scratchpad memory
Divide code part of SPM in regions
Map functions to these SPM regions
Functions in the same region placed at the same address
F1
F3
F6
F5
F7
F4
F2
REGION
REGION
REGION
•
•
•
Local Memory Code Section

## Slide 27: Code Management
  Identify shortcomings in previous techniques
  Update interference costs after mapping each function
    Overhead that two functions were mapped in the same region
  Correct interference cost calculation
  Consider branch probabilities
  Better mapping 89% of time
  Accurate cost calculation improves performance by 12% even with previous mapping techniques

## Slide 28: Heap Data Management: Problem
Heap data management is important
  Heap data accesses may account for a significant portion of data accesses of an application
    susan smoothing from MiBench – 94% of data accesses
Heap data management can be challenging
  Dynamic nature of heap data
Global Data
Code Data
Stack Data
Heap Data

## Slide 29: State-of-the-art: [Bai2013]
Raw Code:
int *p1, *p2;
p1 = malloc(20);
p2 = p1;
*p2 = 10;
Converted Code:
int *p1, *p2;
*g2l(&p1) = malloc(20);
*g2l(&p2) = *g2l(&p1);
*g2l(*g2l(&p2)) = 10;
Heap management functions are inserted at every data access
  Heap accesses are identified at runtime
K. Bai and A. Shrivastava, "Automatic and efficient heap data management for Limited Local Memory multicore architectures," 2013 Design, Automation & Test in Europe Conference & Exhibition (DATE), Grenoble, France, 2013, pp. 593-598.

## Slide 30: Optimized Heap Data Management
Objectives
  Reduce management invocation
  Reduce execution time of management library functions
Optimizations
  Statically Detect Heap Access
    Identify heap accesses at compile-time
    Insert management functions only at heap accesses – not on all accesses
  Simplifying Management Framework
    Implement direct map software cache instead of set associative software cache
    Simplify SPM address calculation
    De-duplicate management functions
  Adjusting Block Size Dynamically
    Compiler selects block size according to heap access pattern
    Optional optimization for embedded applications

## Slide 31: Results of Optimized Heap Management
Chart: A: Statically Detect Heap Access B: Simplifying Management Framework C: De-duplication and Combining Management Code D: Adjusting Block Size
| ADPCM Dec. | ADPCM Enc. | Dijkstra | FFT | iFFT | Patricia | SHA | String Search | Susan Corner | Susan Edge | Susan Smoothing | Average
A | 0.098603 | 0.08622 | 0.53972 | 0.74588 | 0.74585 | 0.74273 | 0.083329 | 0.15001 | 0.56978 | 0.58039 | 0.44037 | 0.43481
A+B | 0.098603 | 0.086221 | 0.23221 | 0.48448 | 0.48441 | 0.51591 | 0.083325 | 0.15006 | 0.22973 | 0.2225 | 0.17393 | 0.25103
A+B+C | 0.098603 | 0.086221 | 0.15683 | 0.38789 | 0.38781 | 0.46547 | 0.083325 | 0.15006 | 0.12731 | 0.12135 | 0.10715 | 0.19746
A+B+C+D | 0.098603 | 0.086221 | 0.12577 | 0.35218 | 0.35211 | 0.35185 | 0.083325 | 0.15006 | 0.12073 | 0.11503 | 0.095477 | 0.17558

## Slide 32: Data management publications
Stack data management
  [DAC 2013] SSDM: Smart Stack Data Management for Software Managed Multicores (SMMs)
Code management
  Conference paper: [CODES+ISSS 2013] CMSM: An Efficient and Effective Code Management for Software Managed Multicores
  Journal Article: [TECS 2015] Efficient Code Assignment Techniques for Local Memory on Software Managed Multicores
Heap management
  [VLSID 2019] Efficient Heap Data Management on Software Managed Manycore Architectures

## Slide 33: Branch Prediction
Improve performance in pipelined processors
  1. Reducing branch mis-prediction penalty
    Pipelines becoming longer
    Branch penalty ~ 10-20 cycles in modern processors
  2. Improve ILP
    Speculative, OOO execution can reorder instructions
    Without branch prediction – can only reorder inside BB
  Every 5-8th instruction is a branch
Consumes too much power
  As high as 10% of on-chip power dissipation[1]
[1] D.Parikh et.al., Power Issues Related to Branch Prediction. In Proc. Of HPCA, 2002

## Slide 34: Software Branch Hinting
Branch Hint Instruction
hbrr <branch address> <target address>
  Branch instruction at <branch address> jumps to <target address>
Inserted by Compiler/Programmer
  Negligible power consumption
Some branch targets are easily known
  Unconditional branches
  Loops branches
L4: shli $13,$11,2
selb $6,$6,$15,$8
rotqby $2,$12,$7
hbrr L14,L4
ai $6,$6,1
cgti $3,$6,2
a $5,$9,$2
lnop
selb $10,$5,$10,$8
L14: brz $3,L4
ai $11,$11,1
ceqi $18,$11,3

## Slide 35: Mechanism of Software Branch Hinting
Instruction
memory
Inline Prefetch
Buffer
PC
IR
Hint Target
Buffer
1
0
Comparator
branch address
target address
branch address
target address
branch address
target address
BH
BR
1

## Slide 36: Branch Hint Placement Problem
Only one hint target buffer
  One effective hint at any time
Branch hint needs some time to be recognized. Hint target buffer needs time to be filled.
  Distance requirement between hint and branch instruction
d=10
d=2
Too small!
L14:
brz $3 ,L5
brz $3 , L4
L4
L5
L16：
1 - p1
p2
1– p2
n1
p1
n2
hbrr L14, L4
hbrr L16, L5
Objective
  Minimize total branch penalty
Output:
  Where to insert hint?
  Which branches to hint?

## Slide 37: Branch Penalty Reduction Methods
Three basic techniques:
  NOP Padding
  Hint Pipelining
  Loop Restructuring
Architecture: IBM Cell processor
Performance measurement: SystemSim
  Cycle accurate simulator
Baseline: GCC compiler (O3)
Results:
  Reduce average 19.2% of the branch penalty more than GCC
  Average 10% speedup

## Slide 38: Thesis Overview
Software branch hinting
  [CODES+ISSS 2011] Branch Penalty Reduction on IBM Cell SPUs via Software Branch Hinting
Stack data management
  [DAC 2013] SSDM: Smart Stack Data Management for Software Managed Multicores (SMMs)
Code management
  Conference paper: [CODES+ISSS 2013] CMSM: An Efficient and Effective Code Management for Software Managed Multicores
  Journal Article: [TECS 2015] Efficient Code Assignment Techniques for Local Memory on Software Managed Multicores
Heap management
  [VLSID 2019] Efficient Heap Data Management on Software Managed Manycore Architectures
SPM: scratchpad memory
DMA Engine
Main Memory
Simple Core
SPM
Instruction
memory
Hint Target
Buffer
Inline Prefetch
Buffer
1
0
branch address
target address
IR
Instruction Fetch