## Slide 1
Enabling Multi-threaded Applications on
Hybrid Shared Memory Manycore Architectures
Tushar Rawat and Aviral Shrivastava Arizona State University, USA
C
M
L

## Slide 2: Port Multi-threaded Applications
Multicore
System
HSM
Manycore
System
?

## Slide 3: Threading and Shared Memory
Multicore
System
Process
Global Space
Thread
Threads have
Shared and Implicit
Access to Program
Data

## Slide 4: Processes and Shared Memory
HSM Manycore
System
Process
Global
Data is not implicitly
shared among
processes
Process
Global

## Slide 5: Convenience Hardware
Multicore
System
HSM
Manycore
System
Hardware-based cache coherence

## Slide 6: Convenience Hardware
Multicore
System
HSM
Manycore
System
Hardware-based cache coherence
Small scratchpad-like
on-chip memory
Lacks hardware
cache coherence

## Slide 7: Contribution
Identify shared data in multi-threaded program
Map identified shared data to shared memory
On-chip
Off-chip

## Slide 8: Five Stage Approach
Variable
Scope
Within
Threads
Pointers
Partition
Data
Thread
To
Process
Analysis
Translation

## Slide 9: Stage 1 – Variable Scope Analysis
Input: Multi-threaded program source code
Output: Name, size, type, read count and write count for each variable
int array[10];
array[0] = 6;
int foo = array[0];
Type: int array
Size: 10
Read Count: 1
Write Count: 1
array
Type: int
Size: 1
Read Count: 0
Write Count: 1
foo

## Slide 10: Stage 2 – Inter-thread Analysis
Input: A given variable (name) e.g. “total_threads”
Output: Result stating whether the given variable exists within 1 thread, 2+ threads or none
void thread
…
printf(“%d”,
total_threads);
…
pthread_exit(NULL);
Loop (or multiple threads launching same function)
Thread

## Slide 11: Stage 3 – Alias and Pointer Analysis
Variable w has a Definite relationship with ptr1
Variables x and y have Possibly a relationship with ptr2
ptr1 = &w
ptr2 = &x
ptr2 = &y
if-path
else-path

## Slide 12: Stage 4 – Data Partitioning
Off-chip shared memory (DRAM)
On-chip shared memory (SRAM)
Processing
Core(s)
RCCE_get
RCCE_put
array = (double *)RCCE_shmalloc(size * sizeof(double))
array = (double *)RCCE_malloc(size)

## Slide 13: Stage 5 – Program Translation
Convert Pthread source to RCCE application code
Add RCCE-specific instructions and libraries
Pthread | RCCE
pthread_self() | RCCE_ue()
pthread_mutex_lock() | RCCE_acquire_lock()
pthread_mutex_unlock() | RCCE_release_lock()
pthread_create(&thread, NULL, funcName, (void *)arg) | funcName((void *) arg)
RCCE_init(argc, argv) | RCCE_finalize()
RCCE.h | RCCE_lib.h
SCC_API.h | 
Any remaining pthread code is removed from the source

## Slide 14: Translator Development
Linux Mint 12
Java OpenJDK 1.6
CETUS 1.3
ANTLR 2.7.5

## Slide 15: HSM Architecture – 48-core Intel SCC
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
R
R
R
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
MC
MC
MC
MC
MC
Memory Controller
R
Router

## Slide 16: On-chip shared memory - MPB
MPB
CC
MIU
Message Passing Buffer
Cache Controller
Mesh Interface Unit
P54C
Pentium® processor core
P54C
Core
L1 cache
P54C
Core
L1 cache
256 KB
L2 cache
256 KB
L2 cache
MIU
[to router]
16 KB
MPB
CC
CC
Tile

## Slide 17: Intel SCC Experiment Configuration
Using 32 of 48 available cores
384 KB on-chip SRAM, up to 64 GB off-chip DRAM
One Linux operating system per core
800 MHz core frequency
1600 MHz network mesh frequency
1066 MHz off-chip DDR3 frequency

## Slide 18: Benchmarks
Both Core and Memory intensive programs
Originals developed for Pthread Multicore systems
Compiled using Intel C++ Compiler 8.1 (gcc 3.4.5), RCCE API version 2.0
Originals run on SCC for baseline
Translated into SCC RCCE applications
  Run with only off-chip shared memory
  Run with mix of on-chip and off-chip shared memory

## Slide 19: RCCE vs Pthread Performance

## Slide 20: Off-chip vs On-chip Mem. Performance

## Slide 21: Enabling Manycores – Performance

## Slide 22: Takeaways
Analyzer identifies all shared data within Pthread program
Translator maps data to both on-chip and off-chip memory
Enables execution of multi-threaded programs for HSM architecture after conversion to many-core applications
  Important to use fast on-chip memory when possible: 8x improvement on average for benchmarks when using on-chip SRAM (MPB) vs only off-chip DRAM

## Slide 23
Thank you
Questions

## Slide 24: Intel SCC and MCPC