## Slide 1: Enabling Multithreading on CGRAs
Aviral Shrivastava1, Jared Pager1, Reiley Jeyapaul,1
Mahdi Hamzeh12, Sarma Vrudhula2
Compiler Microarchitecture Lab,
VLSI Electronic Design Automation Laboratory,
Arizona State University, Tempe, Arizona, USA

## Slide 2: Need for High Performance Computing
Applications that need high performance computing
  Weather and geophysical simulation
  Genetic engineering
  Multimedia streaming
petaflop
zettaflop

## Slide 3: Need for Power-efficient Performance
Power requirements limit the aggressive scaling trends in processor technology
In high-end servers,
  power consumption doubles every 5 years
  Cost for cooling also increases in similar trend
2.3% of US Electrical Consumption
$4 Billion Electricity charges
ITRS 2010

## Slide 4: Accelerators can help achieve Power-efficient Performance
Power critical computations can be off-loaded to accelerators
  Perform application specific operations
  Achieve high throughput without loss of CPU programmability
Existing examples
  Hardware Accelerator
    Intel SSE
  Reconfigurable Accelerator
    FPGA
  Graphics Accelerator
    nVIDIA Tesla (Fermi GPU)
Notes: Technical Question:
How is IBM cell an accelerator?
Flow question:
Having presented the existing set of processor accelerators that help achieve power-efficient performance, what is the motivation for yet another solution in this direction ?
How do I highlight that CGRAs when used as accelerators help in this cause ?

## Slide 5: CGRA: Power-efficient Accelerator
Distinguishing Characteristics
  Flexible programming
  High performance
  Power-efficient computing
Cons
  Compiling a program for CGRA difficult
  Not all applications can be compiled
  No standard CGRA architecture
  Require extensive compiler support for general purpose computing
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Local Instruction Memory
Main System Memory
Local Data Memory
From Neighbors and Memory
To Neighbors and Memory
FU
RF
PEs communicate through an inter-connect network

## Slide 6: Mapping a Kernel onto a CGRA
Given the kernel’s DDG
Mark source and destination nodes
Assume CGRA Architecture
Place all nodes on the PE array
  Dependent nodes closer to their sources
  Ensure dependent nodes have interconnects connecting sources
Map time-slots for each PE execution
  Dependent nodes cannot execute before source nodes
Loop:
t1 = (a[i]+b[i])*c[i]
d[i] = ~t1 & 0xFFFF
Data-Dependency Graph:
1
2
3
4
5
6
7
8
9
Data-Dependency Graph:
1
2
3
4
5
6
7
8
9
Spatial Mapping
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
4
1
2
3
5
6
7
8
9
4i-2
1i
2i
3i-1
5i-2
6i-3
7i-4
8i-5
9i-6
Temporal Scheduling
&

## Slide 7: Mapped Kernel Executed on the CGRA
Loop:
t1 = (a[i]+b[i])*c[i]
d[i] = ~t1 & 0xFFFF
Data-Dependency Graph:
1
2
3
4
5
6
7
8
9
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Execution time slot:
(or cycle)
0
10
20
11
21
30
1
40
12
22
31
50
2
41
13
23
32
51
60
3
42
14
24
33
52
61
70
4
43
15
25
34
53
62
71
80
5
44
16
26
35
54
63
72
81
90
6
45
17
27
36
55
64
73
82
91
7
Iteration Interval (II) is a measure of mapping quality
Entire kernel can be mapped onto CGRA by unrolling 6 times
After cycle 6, one iteration of loop completes execution every cycle
Iteration Interval = 1

## Slide 8: Traditional Use of CGRAs
E0
E1
E2
E3
E4
E5
E6
E7
E8
E9
E10
E11
E12
E13
E14
E15
An application is mapped onto the CGRA
System inputs given to the application
Power-efficient application execution achieved
Generally used for streaming applications
  ADRES, MorphoSys, ADRES, KressArray, RSPA, DART
Application Input
Application Output

## Slide 9: Envisioned Use of CGRAs
Specific kernels in a thread can be power/performance critical
The kernel can be mapped and scheduled for execution on the CGRA
Using the CGRA as a co-processor (accelerator)
  Power consuming processor execution is saved
  Better performance of thread is realized
  Overall throughput is increased
E0
E1
E2
E3
E4
E5
E6
E7
E8
E9
E10
E11
E12
E13
E14
E15
Processor
co-processor
Program thread
Kernel to accelerate

## Slide 10: CGRA as an Accelerator
Application: Single thread
  Entire CGRA used to schedule each kernel of the thread
  Only a single thread is accelerated at a time
Application: Multiple threads
  Entire CGRA is used to accelerate each individual kernel
  if multiple threads require simultaneous acceleration
    threads must be stalled
    kernels are queued to be run on the CGRA
E0
E1
E2
E3
E4
E5
E6
E7
E8
E9
E10
E11
E12
E13
E14
E15
S1
S2
S3
Not all PEs are used in each schedule.
Thread-stalls create a performance bottleneck

## Slide 11: Proposed Solution: Multi-threading on the CGRA
E0
E1
E2
E3
E4
E5
E6
E7
E8
E9
E10
E11
E12
E13
E14
E15
Through program compilation and scheduling
  Schedule application onto subset of PEs, not entire CGRA
  Enable dynamic multi-threading w/o re-compilation
  Facilitate multiple schedules to execute simultaneously
Can increase total CGRA utilization
  Reduce overall power consumption
Increases multi-threaded system throughput
S1
S2
S2
S2
S3
S3
S2’
S2’
S3’
S3
S3
Threads: 1, 2
Maximum CGRA utilization
Threads: 1, 2, 3
Shrink-to-fit mapping maximizing performance
Threads: 2, 3
Expand to maximize CGRA utilization and performance

## Slide 12: Our Multithreading Technique
Static compile-time constraints to enable fast run-time transformations
  Has minimal effect on performance (II)
  Increases compile-time
Perform fast dynamic transformations
  Takes linear time to complete with respect to kernel II
  All schedules are treated independently
Features:
Dynamic Multithreading enabled in linear runtime
No additional hardware modifications
  Require supporting PE inter-connects in CGRA topology
Works with current mapping algorithms
  Algorithm must allow for custom PE interconnects
Notes: Confirm and clarify the features

## Slide 13: Hardware Abstraction: CGRA Paging
Page: conceptual group of PEs
A page has symmetrical connections to each of the neighboring pages
No additional hardware ‘feature’ is required.
Page-level interconnects follow a ring topology
Local Instruction Memory
Main System Memory
Local Data Memory
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
e0
e1
e2
e3
e4
e5
e6
e7
e8
e9
e10
e11
e12
e13
e14
e15
P0
P1
P2
P3
P0
P3
P2
P1
P0
P3
P2
P1
Notes: Page definition clarify and confirm

## Slide 14: Step 1: Compiler Constraints assumed during Initial Mapping
Compile-time Assumptions
  CGRA is collection of pages
  Each page can interact with only one topologically neighboring page.
  Inter-PE connections within a page are unmodified
These assumptions,
  in most cases will not effect mapping quality
  may help improve CGRA resource usage
e0
e1
e2
e3
e4
e5
e6
e7
e8
e9
e10
e11
e12
e13
e14
e15
P1
P0
P2
P3
4
1
2
3
5
6
7
8
9
4
1
2
3
5
6
7
8
9
Naïve mapping could result in under-used CGRA resources
Our paging methodology,
helps reduce CGRA resource usage

## Slide 15: Step 2: Dynamic Transformation enabling multiple schedules
Example:
  application mapped to 3 pages
  Shrink to execute on 2 pages
Transformation Procedure:
  Split pages
  Arrange pages in time order
  Mirror pages to facilitate shrinking
    Ensures inter-node dependency
  Shrunk pages executed on altered time-schedules
Constraints
  inter-page dependencies should be maintained
e0
e1
e2
e3
e4
e5
e6
e7
e8
e9
e10
e11
e12
e13
e14
e15
P3
P0
1
2
3
P1
4
5
6
7
8
9
P2

## Slide 16: Step 2: Dynamic Transformation enabling multiple schedules
Transformation Procedure:
  Split pages
  Arrange pages in time order
  Mirror pages to facilitate shrinking
    Ensures inter-node dependency
  Shrunk pages executed on altered time-schedules
e0
e1
e2
e3
e4
e5
e6
e7
e8
e9
e10
e11
e12
e13
e14
e15
P3
P0
1
2
3
P1
4
5
6
7
8
9
P2

## Slide 17: Step 2: Dynamic Transformation enabling multiple schedules
e0
e1
e4
e5
e8
e9
e12
e13
e10
e11
e14
e15
T0
T1
T2
P0
1
2
3
P1
4
5
6
7
8
9
P2
e10
e11
e14
e15
7
8
9
P2
P0,1
1
2
3
P1,1
4
5
6
T2
T3
T4
Example:
  application mapped to 3 pages
  Shrink to execute on 2 pages
Transformation Procedure:
  Split pages
  Arrange pages in time order
  Mirror pages to facilitate shrinking
    Ensures inter-node dependency
  Shrunk pages executed on altered time-schedules
Constraints
  inter-page dependencies should be maintained

## Slide 18: Experiment 1: Compiler Constraints are Liberal
Mapping quality measured in Iteration Intervals
  smaller II is better
Chart: Interation Interval (II)
| mpeg2_form_pred | yuv2rgb | swim_calc2 | wavelet | sor | Laplace | Swim Calc1 | Compress | gsr | lowpass | sobel | Average
2 PEs/Page | 1 | 1 | 0.63093 | 1 | 1 | 1 | 1.0833 | 1 | 1 | 1 | 1 | 0.95345
4 PEs/Page | 1 | 1.4447 | 0.86667 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0092
8 PEs/Page | 1 | 1.25 | 1 | 1 | 0.75 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Constraints can also improve individual benchmark performance by, ironically, limiting compiler search space
Constraints can degrade individual benchmark performance by limiting compiler search space
On average, performance is minimally impacted

## Slide 19: Experimental Setup
CGRA Configurations used:
  4x4, 6x6, 8x8
Page configurations:
  2, 4, 8 PEs per page
Number of threads in system:
  1, 2, 4, 8, 16
  Each has a kernel to be accelerated
Experiments
Single-threaded CGRA
  Each thread arrives at “kernel”
  thread is stalled until kernel executes
Multi-threaded CGRA
  CGRA used to accelerate kernels as and when they arrive
  No thread is stalled
CPU
Core
CPU
Core
CPU
Core
CPU
Core
CGRA
Thread 1
Thread 2
Thread 3
Thread 4
kernel to be accelerated
Only ONE thread serviced
MULTIPLE threads serviced

## Slide 20: Multithreading Improves System Performance
Chart: Performance across CGRA Size (4 PEs/Page)
| 1 | 2 | 4 | 8 | 16
4x4 CGRA | 1 | 1.0959 | 1.3004 | 1.3786 | 1.3418
6x6 CGRA | 0.99137 | 1.2825 | 1.7701 | 2.2233 | 2.9369
8x8 CGRA | 0.99969 | 1.3344 | 2.1305 | 3.2014 | 4.2916
Chart: Performance across # PEs/Page (6x6 CGRA)
| 1 | 2 | 4 | 8 | 16
2 PEs/Page | 0.96555 | 1.2155 | 1.715 | 2.4168 | 2.9316
4 PEs/Page | 0.99702 | 1.2376 | 1.7337 | 2.2678 | 2.8567
8 PEs/Page | 0.9799 | 1.1092 | 1.3369 | 1.572 | 1.704
Number of Threads Accessing CGRA:
As the number of threads increases, multithreading provides increasing performance
CGRA Size:
As we increase CGRA size, multithreading provides better utilization and therefore better performance
Number of PEs per Page:
For the set of benchmarks tested, the number of optimal PEs per page is either 2 or 4
Notes:   Performance improvement numbers ??

## Slide 21: Summary
Power-efficient performance is the need of the future
CGRAs can be used as accelerators
  Power-efficient performance can be achieved
  Has limitations on usability due to compiling difficulties
  With multi-threaded applications, need multi-threading capabilities in CGRA
Propose a two-step dynamic methodology
  Non-restrictive compile-time constraints to schedule application into pages
  Dynamic transformation procedure to shrink/expand the resources used by a schedule
Features:
  No additional hardware required
  Improved CGRA resource usage
  Improved system performance
Notes: Numbers ?

## Slide 22: Future Work
Using CGRAs as accelerator in systems with inter-thread communication.
Study the impact of compiler constraints on compute-intensive and memory-bound benchmark applications?
Possible use of thread-level scheduling to improve overall performance?

## Slide 23: Thank you !

## Slide 24: Measuring CGRA Performance
A completed mapping is called a schedule
  A schedule consists of a prolog, kernel, and epilog
Mapping Quality is measured by Initiation Interval (II)
  II is a measure how many cycles it takes the kernel portion to execute a single iteration of a loop
    ie, if II=2, every two cycles, an iteration of the original loop is completed
II is limited by CGRA resources (number of PEs, etc) and by recurrence cycles
  If there are only 4 PEs but a DDG contains 9 nodes, II can at best be 3
  If a loop cannot be unrolled, II can be hurt
Recurrence Cycle:
t1 = A[i] + C[i - 1]
C[i] = B[i] + t1
1i
3i
2
4
5i
Unrolling:
t1a = A[i] + C[i-1]
C[i] = B[i] + t1a
t1b = A[i+1] + C[i]
C[i+1] = B[i+1] + t1b
1i
3i
2
4
5i
1i+1
3i+1
2
4
5i+1
t1b can never execute any earlier,
no matter how many times we unroll

## Slide 25: DDG with Recurrance
1i-1
3i-1
2i-1
4i-1
5i-1
6i-1
1i
3i
2i
4i
5i
6i
1i-2
3i-2
2i-2
4i-2
5i-2
6i-2
1i
3i
2
4
5i
1i+1
3i+1
2
4
5i+1

## Slide 26: State-of-the-art Multi-threading on CGRAs
Polymorphic Pipeline Arrays [Park 2009]
  Enables dynamic scheduling
    Collection of schedules make a kernel
    Some schedules can be given more resources than other schedules
  Limitations
    Collection of schedules must be known at compile-time
    Schedules are assumed to be ‘pipelining’ stages in a single kernel
Filter 1
Filter 2
Filter 3
Data Set 1
Output
Core 1
Core 2
Core 3
Core 4
Core 5
Core 6
Core 7
Core 8
Mem
Bank 1
Mem
Bank 2
Mem
Bank 3
Mem
Bank 4
Filter 1
Filter 2
Filter 3
Filter 1
Filter 2
Filter 3
Data Set 2
Output
Filter 1
Filter 2
Filter 3
Filter 1
Filter 2
Filter 3
Data Set 3
Output
Filter 1
Filter 2
Filter 3
Notes: More clarity in the PPA technique explanation