## Slide 1: EXPERT: Effective and Flexible Error Protection by Redundant Multithreading
Hwisoo So*, Moslem Didehban#, Yohan Ko*, Aviral Shrivastava#, Kyoungwoo Lee* *Department of Computer Science, Yonsei University, Seoul, Korea #Compiler Microarchitecture Lab, Arizona State University, Tempe, AZ Presented by Hwisoo So

## Slide 2: EXPERT: Effective and Flexible Error Protection by Redundant Multithreading
Background and motivation
Problem: vulnerability in previous redundant multithreading (RMT)
EXPERT: an improved RMT
Experiments and conclusion

## Slide 3: Soft and hard error: main threats to reliability
Now, reliability is one of the most important design concerns
Main sources of hardware unreliability
  Soft error, aka transient fault
  Hard error, aka permanent fault
Photo-illustration: iStockphoto

## Slide 4: Redundant Multithreading: flexible and effective
Software-level redundancy: flexible error detection
  No hardware modification
  Can provide flexibility
Redundant multithreading: effective software-level detection
  Main approaches of software-level redundancy are
 | Instruction-level redundancy | Redundant multithreading
Soft error | Can detect | Can detect
Hard error | Can not detect | Can detect
Controlflow | Difficult to detect | Can detect

## Slide 5: Previous RMT researches
SRMT: software-based redundant multithreading [Wang, CGO ‘07]
COMET[Mitropoulou, Cases ‘16], DAFT[Zhang, IJPP ‘12]: Improves runtime
[Wadden, ISCA ‘14][Gupta, DAC ‘17]: Applies SRMT to GPU
RedThreads[Hukerikar, IJPP ‘16]: Programmer-tunable SRMT for HPC
Data Memory
Leading thread
Trailing thread
Identical
computation
Memory operation
Checking values for memory operation

## Slide 6: Experiment: Setup
Benchmark: 9 applications in MiBench
  Original / SRMT-protected
    Without hardware supports for inter-thread communication
Fault Injection on cycle-accurate gem5 simulator
  6 components for fault injection
  1 error injection per 1 execution
    500 soft errors and 100 hard errors per each component / benchmark
Fault coverage validation
  Main target: # of silent data corruption
  With correction factor[Schirmeier, DSN ‘15] (# of SDCs * runtime * # of cores)

## Slide 7: Experiment: error coverage of SRMT
Total: 27,000 soft error and 5,400 hard error injection
  For unprotected and SRMT-protected application
  On average, SRMT requires ~3.9x runtime
  2 cores are used for physically separated multithreading
Chart: # of SDC against soft and hard error injection
| Number of SDCs
SRMT-protected | 1310
Unprotected | 7061

## Slide 8: Why SRMT suffers vulnerability?
SRMT checking only checks old snapshot of registers
  Incorrect execution of memory operation can be undetected
    Vulnerable input replication & vulnerable output comparison
Leading thread
Trailing thread
Data Memory
#1: Load
#2: Store
#1: Checking
#1: Copying result
#2: Checking
#1: Send addr
#1: Send result
#2: Send addr, data
Communication Queue
Address of #1
Result of #1
Address of #3
Data of #3
Corrupted

## Slide 9: EXPERT: Reliable software-level RMT
Data Memory
Data for load
result of store
Main Thread
Checker Thread
Store data → [addr]
Load temp*  [addr*]
(temp*result of store)
Check temp*, data*
Load data*  [addr*]
Load data  [addr]
Identical
computation
Corrupted
Load temp*  [addr*]
(temp*result of store)
Check temp*, data*
Store data* → [addr*]
①
②
③
Store data* → [addr*]
② waits until checker reaches ①
③ waits until ② is done

## Slide 10: EXPERT: Store Packing Optimization
2-way sync for every store
  ~7.2x runtime on average
If there is no dependency between ①, ②, and ③
  Expert checking needs to keep
“Store Packing” is possible
  If there is no memory dependency for both STORE and LOAD
  ~43% performance improvement
①
❶
Main Thread
Checker Thread
Wait
Store
Notify
Wait
Store
Notify
Wait
Store
Notify
Notify
Wait
Check
Notify
Wait
Check
Notify
Wait
Check
1❶❷❸❹①②③④⑤⑥⑦
②
③
❷
❸
①
②
③
❶
❷
❸

## Slide 11: Experiment: Setup
Benchmark: 9 applications in miBench
  Original / SRMT-protected / EXPERT-protected
Fault Injection on cycle-accurate gem5 simulator
  6 components for fault injection
  1 error injection per 1 execution
    500 soft errors and 100 hard errors per each component / benchmark
    Total # of injections : 81,000 soft errors & 16,200 hard errors
Fault coverage validation
  Main target: # of silent data corruption
  With correction factor[Schirmeier, DSN ‘15] (# of SDCs * runtime * # of cores)

## Slide 12: Experiment: SDC coverage validation
Chart: 
| bitcount | baiscmath | fft | sha | susan_c | susan_e | susan_s | adpcm | crc | sum
EXPERT hard error | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| bitcount | baiscmath | fft | sha | susan_c | susan_e | susan_s | adpcm | crc | sum
EXPERT hard error | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| bitcount | baiscmath | fft | sha | susan_c | susan_e | susan_s | adpcm | crc | sum
Original soft error | 1447 | 786 | 542 | 1430 | 69 | 73 | 478 | 1053 | 1183 | 7061
SRMT soft error | 172.4977 | 14 | 69.5333 | 186.7398 | 60.8055 | 60.7058 | 46.7689 | 239.892 | 458.925 | 1309.8682
EXPERT soft error | 2.193 | 0 | 0 | 0 | 0 | 0 | 0 | 17.8011 | 0 | 19.9941
Chart: 
| bitcount | baiscmath | fft | sha | susan_c | susan_e | susan_s | adpcm | crc | sum
Original hard error | 75 | 59 | 38 | 55 | 21 | 17 | 24 | 111 | 23 | 423
SRMT hard error | 8.6249 | 4 | 28.7 | 10.3744 | 24.3222 | 45.5294 | 33.9203 | 9.9955 | 0 | 165.4667
EXPERT hard error | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Normalized Number of SDCs (log scale)
Chart: 
| a
Original soft error | 0
SRMT soft error | 0
EXPERT hard error | 0
Original hard error | 0
SRMT hard error | 0
EXPERT hard error | 0
7,061
(21.79%)
1,310
(4.04%)
20
(0.062%)
0
0
0
0
0
0
0
Notes: soft hard total
Original : 6638 / 423 / 7061
SRMT: 1145 / 165 / 1310
EXPERT: 20 / 0 / 20

## Slide 13: Conclusion
Improved soft and hard error detection
  With load-back checking & load replication on redundant multithreading
    Additional sync scheme is needed
  65x better SDC coverage compared to SRMT
Limitations
  Runtime becomes ~5.0x on average, even with sync optimization,
    SRMT: 3.9x on average
    Can be improved with hardware support for communication
  SDC cases on silent store
Notes: https://www.date-conference.com/av-guidelines/
A slide containing the conclusion of your talk

## Slide 14: References
[Wang, CGO ‘07] C. Wang et al., “Compiler-managed software-based redundant multi-threading for transient fault detection,” in CGO, 2007.
[Mitropoulou, Cases ‘16] K. Mitropoulou et al., “Comet: communication-optimised multithreaded error-detection technique,” in CASES. ACM, 2016.
[Zhang, IJPP ‘12] Y. Zhang et al., “DAFT: Decoupled Acyclic Fault Tolerance,” International Journal of Parallel Programming, 2012.
[Wadden, ISCA ‘14] J.Wadden et al., “Real-world design and evaluation of compilermanaged gpu redundant multithreading,” in ISCA. IEEE, 2014.
[Gupta, DAC ‘17] M. Gupta et al., “Compiler techniques to reduce the synchronization overhead of gpu redundant multithreading,” in DAC, 2017.
[Hukerikar, IJPP ‘16] S. Hukerikar et al., “Redthreads: An interface for applicationlevel fault detection/correction through adaptive redundant multithreading,” IJPP, 2016.
[Schirmeier, DSN ‘15]] H. Schirmeier et al., “Avoiding pitfalls in fault-injection based comparison of program susceptibility to soft errors,” in DSN, 2015.
Notes: https://www.date-conference.com/av-guidelines/
A slide containing the conclusion of your talk

## Slide 15: Extra slides
Notes: https://www.date-conference.com/av-guidelines/
A slide containing the conclusion of your talk

## Slide 16: Soft error and hard error
Soft error: temporal bit flip
Hard error: permanent bit fault
Adder
R0
R1 | 2
R2 | 4
=
+
R3
R4 | 4
R5 | 4
=
+
This adder always make last bit of result as 1
R0 | 6 → 7
R3 | 8 → 9
#1
#2
Adder
R0
R1 | 2
R2 | 4
=
+
R3
R4 | 4
R5 | 4
=
+
Soft error occurs while executing #1
R0 | 6 → 7
R3 | 8
#1
#2

## Slide 17: SRMT: Error cases
Leading thread
Load in SRMT-protection
Store in SRMT-protection
Load data  [addr]
Check addr, addr*
Copy data* ← data
Leading thread
Trailing thread
Load
Fine
Data Memory
Load data  [addr]
Data Memory
Check addr, addr*
Check data, data*
Trailing thread
Fine
Store data → [addr]
Store
Corrupted

## Slide 18: EXPERT: Removing Vulnerability from LOAD
Main Thread
Replicating load operation on checker thread
Data Memory
Main Thread
Checker
Thread
Soft error on load operation can only corrupt one thread
  System can detect mismatch, as another thread is clean
Checking for load operation is not necessary
  Only store operation can propagate error effect
  Mismatch will be found on later checking for store operation
load data[addr]
load data*[addr*]
NOTE: Checker thread access memory with its local register

## Slide 19: EXPERT: Load-back checking against error
If error corrupts data of store operation
If error corrupts address of store operation
Store data  [addr]
Load temp*  [addr*]
Cmp temp*, data*
Data Memory
Wrong result
Main Thread
Checker Thread
Store data  [addr]
Load temp*  [addr*]
Cmp temp*, data*
Data Memory
Data
Main Thread
Checker Thread
Not Updated

## Slide 20: Silent Store Problem
Store data  [addr]
Load temp*  [addr*]
Cmp temp*, data*
Data Memory
Data
Main Thread
Checker Thread
Same to data
Silent store: if previous value in memory is same to data of store, store does not change memory
If address of silent store is corrupted, EXPERT can not detect memory corruption
Notes: 이전 글자들을 제거한 대신, 싱크로 얘기를 할것임
스토어 / 로드에서 에러가 발생하는 예시도 보여주자

## Slide 21: EXPERT: Memory Coherence Problem
In LOAD and STORE with same address
In STORE and relative CHECKING
Load R0[R4]
R1 = R0 + 4
Store R1[R4]
Load R0*[R4*]
R1* = R0 * + 4
DO CHECKING
Main Thread
Checker Thread
Data Memory
1000
1004
①
②
③
1000
1004
Store R1[R4]
(R1 = 1004)
Load Temp*[R4*]
Cmp temp*, data* (data* = 1004)
Main Thread
Checker Thread
Data Memory
1000
1004
1004
①
1000
②
1000
Not Done
Not Done

## Slide 22: 2-ways of Compiler-level error detection
data = data + 4
Original Code
data = data + 4
data* = data* + 4
In-thread replication
Replicates instructions
data + 4
data* + 4
Wrong result
Correct result
Adder on core i
Mismatch can be detected
Wrong result
Wrong result
Mismatch can not be detected
data = data + 4
data* = data* + 4
Redundant multithreading
Thread 1
Thread 0
Replicates execution thread
data + 4
Wrong Result
data* + 4
Correct result
Adder on core i
Adder on core j
Mismatch can be detected