## Slide 1: dMazeRunner: Optimizing Convolutions on Dataflow Accelerators
Shail Dave1, Aviral Shrivastava1, Youngbin Kim2, Sasikanth Avancha3, Kyoungwoo Lee2
[1] Compiler Microarchitecture Lab, Arizona State University
[2] Department of Computer Science, Yonsei University
[3] Parallel Computing Lab, Intel Labs
45th International Conference on Acoustics, Speech, and Signal Processing (ICASSP 2020)

## Slide 2: Must-Accelerate Applications in ML Era
Object Classification/Detection
Media Processing/Generation
Large-Scale Scientific Computing
Designing Software 2.0
Google shrinks language translation code from 500k LoC to 500
and more …
AlphaGo. https://www.nature.com/articles/nature24270
Multi Layer Perceptrons
http://yann.lecun.com/exdb/lenet/
Sequence Models
http://jalammar.github.io/visualizing-neural-machine-translation-mechanics-of-seq2seq-models-with-attention/
https://deeplearning.mit.edu/
Convolution Neural Networks
http://vision03.csail.mit.edu/cnn_art/index.html
https://pjreddie.com/darknet/
Reinforcement Learning
Graph Neural Networks
Points of Interest
Delaunay Triangulation
YOW! Data 2018 Conference. https://www.youtube.com/watch?v=lDRb3CjESmM
Widely Used ML Models
Popular Applications
Tropical Cyclon Detection
https://insidehpc.com/2019/02/gordon-bell-prize-highlights-the-impact-of-ai/
Designing Computer Systems for Software 2.0. Kunle Olukotun, NeurIPS 2018 Invited talk.
https://giphy.com
Compute Intensive, Needs Energy-efficient Acceleration

## Slide 3: Dataflow Accelerators: Promising Solution
Massive arrays of processing elements (PEs).
  Simple: absence of complex out-of-order pipeline and decoding.
  Programmable: accommodate executing all operations within a loop.
Private and shared memory for PEs sustain data reuse.
PEs can be busy performing computations while data is being communicated from lower memories.
  Taken care by effective data management i.e., software prefetching, data distribution, data allocation.
Known variations include - Systolic Arrays, - Spatially Programmable Architecture,
- Coarse-Grain Reconfigurable Array (CGRA)
DRAM (Off-Chip)
Scratch-Pad Memory
[1] Norman Jouppi et al. In-datacenter performance analysis of a tensor processing unit. In ISCA 2017. [TPU v1]
[2] Yu-Hsin Chen et al. Eyeriss: An energy-efficient reconfigurable accelerator for deep cnns. In JSSC 2016. [Eyeriss System, MIT]
[3] Kamran Khan. 2018. Xilinx DNN Processor (xDNN), Accelerating AI in Datacenters. [Xilinx xDNN]
[4] Bruce Fleischer et al., A Scalable Multi-TeraOPS Core for AI Training and Inference. In VLSI 2018. [IBM AI Accelerator]
[5] Dataflow Processing Unit from Wave Computing. In HOTCHIPS 2017. [Wave DPU]
[6] M. Thottethodi and T. N. Vijaykumar. Why GPGPU is Less Efficient than TPU for DNNs. ACM SIGARCH Blog, Jan 2019. (online)

## Slide 4: Mapping Computation in Space and Time
PEs compute different outputs
Data in RF of PE(1,1)
I: 1x3 , W: 1x1x3, O: 1x1x1
Scratch-Pad Memory
(multi-bank, double buffered)
% filters
% filter row
% filter column
% o/p row
% o/p column
DMA

## Slide 5: Vast “Execution Method” Space
Many many ways to execute nested loops (of DNN) on a dataflow accelerator
  Both software and hardware design space
  Hardware: Size, layout, and connectivity of PEs, size of on-chip buffer and registers, etc.
  Software: loop mappings, e.g., Spatial: parallelism, data reuse, Temporal: ordering and tiling of the loops, data reuse, data buffering, etc.
4D Convolution:
Scratch-Pad Memory
DRAM
Hardware Accelerator
L1 Accesses
L2 Accesses
L3 Accesses
Concurrent Execution
on PEs
7x7x512
9x9
9x9x256
3x3x256
*
=
(padded)
512 filters
.
.
256
256
3x3
1 ifmap
1 ofmap
Stride=1
<N,M,C,Ox,Oy,Fx,Fy> = <1,512,256,7,7,3,3>
Conv5_1 [ResNet]

## Slide 6: Orchestration of Loops
Scratch-Pad Memory
DRAM
Accelerator
L1 Accesses
L2 Accesses
L3 Accesses
Convolution Operator:
Concurrent Execution
on PEs
for n_L3 = 1:N_DRAM
for m_L3 = 1:M_DRAM
for c_L3 = 1:C_DRAM
for ox_L3 = 1:Ox_DRAM
for oy_L3 = 1:Oy_DRAM
for fx_L3 = 1:Fx_DRAM
for fy_L3 = 1:Fy_DRAM
{
dma( );
for n_L2 = 1:N_SPM
for m_L2 = 1:M_SPM
for c_L2 = 1:C_SPM
for ox_L2 = 1:Ox_SPM
for oy_L2 = 1:Oy_SPM
for fx_L2 = 1:Fx_SPM
for fy_L2 = 1:Fy_SPM
{
communicate_data_NoC( );
for n_L1 = 1:N_RF
for m_L1 = 1:M_RF
for c_L1 = 1:C_RF
for ox_L1 = 1:Ox_RF
for oy_L1 = 1:Oy_RF
for fx_L1 = 1:Fx_RF
for fy_L1 = 1:Fy_RF
{
for n_S = 1:N_SPATIAL
for m_S = 1:M_SPATIAL
for c_S = 1:C_SPATIAL
for ox_S = 1:Ox_SPATIAL
for oy_S = 1:Oy_SPATIAL
for fx_L3 = 1:Fx_SPATIAL
for fy_L3 = 1:Fy_SPATIAL
O[][][][] +=
I[][][][] *
W[][][][];
}
}
}
The problem of exploring the “execution methods” for mapping 7-deep nested loop onto dataflow accelerator becomes the problem of exploring all the possibilities of tiling and ordering factors in the 28-deep nested loop
28-deep nested loop
7-deep nested loop

## Slide 7: dMazeRunner Demo
Release: https://github.com/MPSLab-ASU/dMazeRunner
1
Estimate performance and energy-efficiency of individual execution method for a specified accelerator hardware and layer dimensions
2
Optimize specific or all layers of common CNN networks
3
Explore efficient accelerator designs for DNNs
Framework Features

## Slide 8: Execution Modeling of Dataflow Accelerators
Analyze arbitrary perfectly nested loops.
miss penalty and stall cycles (during PE execution and in managing PE’s local or shared memory).
inter-PE communication.
temporal/spatial data reuse.
Integrated support common ML libraries MXNet/Keras/... (thanks TVM! – leveraging front-end)
Validation against DNN Optimizer of Yang et al.
Yang, Xuan, M. Gao, J. Pu, A. Nayak, Q. Liu, S. Bell, J. Setter, K. Cao, H. Ha, Christos Kozyrakis, and Mark Horowitz. "DNN Dataflow Choice Is Overrated." [arXiv ‘18]
Energy estimate differs by ~4.2% for variety of execution methods.
For efficient mappings, major energy spent in RF accesses.
Features with detailed modeling of
Shail Dave, Youngbin Kim, Sasikanth Avancha, Kyoungwoo Lee, Aviral Shrivastava, dMazeRunner: Executing Perfectly Nested Loops on Dataflow Accelerators [CODES+ISSS, TECS 2019].
Step-wise equations and analysis:

## Slide 9: Optimizing Multiple Dataflows
Executing ResNet layers on a 256-PE, 512B RF, 128kB SPM dataflow accelerator
Oy | Ox: Output Stationary
Fy | Fx : Weight Stationary
Oy | Fy : Row Stationary

## Slide 10: Adaptable Mappings Yield Better Results
Adapts to layer / hardware architecture characteristics
  Scales for layers and tensors of different shapes
Finds non-intuitive mappings that are optimized for various key factors e.g.,
High Resource (PE/memories) Utilization
Maximized Reuse of Multiple Tensors
Minimized DRAM accesses
Hiding Communication Latency Behind Computations on PEs
Example Mapping of ResNet Conv5_2 with Output Stationary Dataflow
For data allocated in RFs of PEs,
PE Compute vs. Data comm. Latency:
Total cycles:
Ideal execution cycles for output-stationary:
Reduction in DRAM accesses (ifmaps, weights):
Perf. improvement (normalized to MOC):
Energy-Delay-Product reduction (normalized):
MOC
144 vs. 648
~10,616,832
2,359,296
(1x, 1x)
1x 1x
dMazeRunner
576 vs. 576
~2,459,648
2,359,296
(4.57x, 2x) 4.44x 9.86x
MOC: Simultaneous spatial processing of Multiple Output Channels
[1] S. Gupta et al. Deep learning with limited numerical precision. In ICML, 2015.
[2] Y. Chen et al. Eyeriss: A spatial architecture for energy-efficient dataflow for CNNs. In ISCA 2016.

## Slide 11: Achieving Close-to-Optimal Solutions in Seconds
Search Space Exploration on an Intel i7-6700 Quad-core CPU
min: ~1 second, ResNet conv5_2 (753*9 methods) max: ~122 seconds, ResNet conv2_2 (122092*9 methods)
AlexNet and ResNet18 models in about 18 and 180 seconds, respectively
Quick exploration:
  In-built support for a few common opt strategies.
  Implementation – multi-threaded, caches commonly invoked routines of analytical model.
  Enables effective Design Space Exploration of architecture, e.g., explore impact of scaling PEs and memory sizes on performance and energy efficiency.
Search Space Reduction for DNN Optimizations
Even domain non-experts can explore the space
Does not preclude experts/programmers from directing the search.
python run_optimizer.py --frontend mxnet --model resnet18 --layer-index 0

## Slide 12: Conclusions
Dataflow accelerators: promising for accelerating ML applications.
Need to determine efficient “execution method” for spatiotemporal executions on dataflow accelerators.
dMazeRunner: Automated, succinct, and fast exploration of mapping search space and architecture design space.
Adaptive and non-intuitive mappings enable efficient dataflow acceleration.
[Release] https://github.com/MPSLab-ASU/dMazeRunner
[Project] https://labs.engineering.asu.edu/mps-lab/ml-accelerators